## Slide 1: NPCA and Virtual AP
Date: 2024-05-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Virtual AP
An AP device can include multiple virtual APs belonging to one multiple BSSID set.
  All the APs belonging to a multiple BSSID set share the same operating class, channel, receive/transmit antenna connector
  Only the AP with transmitted BSSID transmits the Beacon frames.
  All the virtual APs have the same primary channel.
11ax defines the co-hosted APs in an AP device by co-hosted BSSID set.
  All the APs belonging to a co-hosted BSSID set share the same operating class, channel, receive/transmit antenna connector
  Each co-host AP broadcasts its Beacon.
  All co-hosted APs have the same primary channel.

## Slide 3: Recap: NPCA
An AP enabling NPCA announces the NPCA primary channel where when the primary channel becomes busy because of the OBSS activity, the AP and its associated STA switch to the NPCA primary channel to do the frame exchanges until the end of the OBSS activity.
The AP may announce the threshold so that when the duration of the OBSS activity is smaller than the announced threshold, the AP and its associated STAs will not switch to the NPCA primary channel to do the frame exchanges.

## Slide 4: NPCA Primary Channel and Multiple BSSID
The APs that belong to a multiple BSSID set and enable NPCA need to have the same NPCA primary channel.
  This is because that all such APs share the same receive/transmit antenna connector.

## Slide 5: NPCA Operation and Multiple BSSID
The criteria to switch from the primary channel to NPCA primary channel need to be same for all APs that belong to a multiple BSSID set and support the switch, e.g.
  OBSS activity threshold for the switch.

## Slide 6: NPCA Primary Channel and Co-Hosted APs
The APs that belong to a co-hosted BSSID set and enable NPCA need to have the same NPCA primary channel.
  This is because that all such APs share the same receive/transmit antenna connector.

## Slide 7: NPCA Operation and Co-Hosted APs
The criteria to switch from the primary channel to NPCA primary channel need to be same for all APs that belong to a co-hosted BSSID set and support the switch, e.g.
  OBSS activity threshold for the switch.

## Slide 8: Summary
The NPCA primary channel announced by the APs belong to a multiple BSSID set and a co-hosted BSSID set needs to be same.
The criteria announced by the APs belong to a multiple BSSID set and a co-hosted BSSID set needs to be same.

## Slide 9: SP 1
Do you support that all the APs in a multiple BSSID set that enable NPCA announce the same NPCA primary channel?