## Slide 1: Additional Considerations on Non-Primary Channel Access
Date: 2024-04-27
Authors:

## Slide 2: Abstract
Several contributions has discussed non-primary channel access with generally good alignment[1-9].
After receiving an OBSS PPDU in the primary channel, a STA may switch to a secondary channel and obtain a TXOP.
In this contribution, we present additional considerations regarding NPCA.

## Slide 3: Non-Primary Channel Access
Non-primary channel access allows a STA to transmit on secondary channels if the primary channel is busy.
A busy primary channel could be from a non-zero NAV or from physical CS.
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
time
20MHz PPDU
(interference, OBSS)
80MHz PPDU
Busy
Busy
frequency
40MHz PPDU
(interference, OBSS)
(STA to AP or AP to STA)
60MHz PPDU
40MHz PPDU

## Slide 4: CCA in the secondary channel
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
OBBS NAV
Busy
Busy
frequency
Medium synchronization
After switching to the secondary channel, a STA employs a CCA procedure which may include a medium synchronization procedure followed by a backoff procedure.
  the medium synchronization procedure can be based on the MediumSyncDelay timer or NAVSyncDelay mechanisms in the existing standards.
  The backoff procedure is needed when two or more STAs are allowed to obtain a TXOP in the secondary channel.
Backoff
RTS
CTS
DATA
BA

## Slide 5: Packet reception during backoff (1/3)
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
OBSS NAV
Busy
Busy
frequency
Medium synchronization
Backoff
OBSS NAV
During medium synchronization or backoff, an OBSS PPDU may be received by a STA. The PPDU duration or NAV can prevent the NPCA transmission from occurring.
- the STA may return immediately to the primary channel whenever this occurs.
When the STA is back on the primary channel, a question is whether to allow the STA to ignore the NAV or PPDU duration in the secondary channel.
- Non-NPCA STAs will transmit on the secondary channel if energy detection is less than -72 dBm.
DATA

## Slide 6: Packet reception during backoff (2/2)
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
OBSS NAV
Busy
Busy
frequency
Medium synchronization
Backoff
OBSS NAV
DATA
Received
Power<-72 dBm
When the received power in the NPCA secondary channel is less than -72 dBm, we propose that NPCA STAs are allowed to ignore the NAV (or PPDU duration) in the NPCA secondary channel (similar to Non-NPCA STAs).
Whether NPCA STAs will use the secondary channel depends on implementation.

## Slide 7: When to switch to the NPCA secondary channel
In general, we want to switch at the earliest possible point in the OBSS PPDU. This can be set to the end of the OBSS PPDU plus a delay time to account for decoding the NAV information from the data field.
For HE and newer PPDUs, the switch time can be after the HE-SIG-A/U-SIG (after detecting the BSS color),
For VHT and HT PPDUs, the switch time can be after the PPDU, i.e. after validating the MAC header information to check whether the PPDU is from OBSS or not.
For non-HT PPDUs, the switch time depends on whether the non-HT PPDU carries an RTS or MU-RTS frame (see 10.3.2.4 ).
If the non-HT PPDU carries an RTS or MU-RTS frame, the switch time can be after the NAVtimeout.
If the non-HT PPDU does not carry an RTS or MU-RTS frame, the switch time can be after the non-HT PPDU
10.3.2.4 Setting and resetting the NAV
… A STA that used information from an RTS frame or MU-RTS Trigger frame as the most recent basis to update its NAV setting is permitted to reset its NAV if no (#3038)PHY-RXEARLYSIG.indication or PHYRXSTART.indication primitive is received from the PHY during a NAVTimeout period starting when the MAC receives a PHY-RXEND.indication primitive corresponding to the detection of the RTS frame or MURTS Trigger frame.
Received PPDU
Non-HT PPDU
HT/VHT PPDU
HE and newer PPDUs
After the HE-SIG-A/U-SIG of the PPDU
After the PPDU
(single MPDU)
Based on the NAVTimeout after the PPDU
RTS/MU-RTS?
Yes
No

## Slide 8: Conclusion
Non primary channel access operation may need to be terminated when the STA receives a frame in the secondary channel during channel contention.
After returning to the primary channel, we propose to allow STAs to ignore any NAV information it received from OBSS transmissions in the secondary channel based on baseline CCA rules.
In addition, we discussed when to switch from the primary channel to the secondary channel considering NAV reset when the OBSS PPDU contains an RTS or MU-RTS frame.

## Slide 9: References
  11-23/34, “Non-primary channel utilization,” Sindhu Verma
  11-23/631, “Secondary channel usage and secondary 20MHz channel backoff,” Liwen Chu
  11-23/797, “Non-primary channel access,” Yongho Seok
  11-23/961, “UHR secondary channel access,” Minyoung Park
  11-23/962, “UHR secondary channel access evaluation,” Dibakar Das
  11-23/1112, “Thoughts on secondary channel access,” Insun Jang
  11-23/1365, “Discussions on non-primary channel access,” Sanghyun Kim
  11-23/1911, “Secondary channel access and frame transmission,” Dongju Cha
  11-23/1951, “Concurrent CCA for non-primary channel access,” Leonardo Lanante
  11-23/2005, “Non-Primary Channel Access (NPCA),” Minyoung Park