## Slide 1: Wireless Power Transfer and Frequency Regulation in sub-1 GHz
Date: 2024-05-14
Authors:

## Slide 2: Abstract
Wireless power transfer is an important aspect for passive IoT devices. This presentation gives and introduction to the frequency regulation in the US and Europe and shows the operation of current RFID devices.

## Slide 3: Motivation
Changing the existing frequency regulation typically requires many years
Follow existing rules can speed up the adoption of 802.11bp
AMP devices may be treated as RFID devices from a frequency regulation perspective
Details on the frequency regulation are also presented in Chapter 5 of the “Draft Technical Report on support of AMP IoT devices in WLAN” (DCN 11-22/1562r8)

## Slide 4: Wireless Power Transfer for UHF-RFID
“The EPC® Radio-Frequency Identity Generation-2 UHF RFID Standard” [1] is a widely adopted for UHF-RFID applications
The standard operates in the frequency range between 860 MHz and 930 MHz
Passive tags are only operated by energy harvesting from the electromagnetic field using energy harvesting
Practically all tags support the complete frequency range  no regional profiling of the tags

## Slide 5: How do the Tags Harvest Energy?
The antenna as well as the LC circuit (C1, L1) are resonant in the frequency range between 860 MHz and 930 MHz
The diode and the capacitor C2 rectify the supported frequency range
Simple circuit that supports different frequencies for world-wide use

## Slide 6: How do the Tags Receive Downlink Data?
The additional red part is used for downlink data decoding
Diode D3 and capacitor C4 are a simple Amplitude Modulation / On-Off-Keying demodulator
The supported frequency range is again given by the LC circuit (C1, L1)
Simple, but not very selective!
The strongest downlink signal s assumed to be the relevant one!

## Slide 7: What are the Signal Requirements?
Downlink data has to use On-Off-Keying modulation
No real restrictions on the downlink waveform design during the On-Phases of the signal
“Wideband” signals are suitable
Narrowband signals are suitable as well
The EPC global UHF RFID standard [1] uses narrowband signals

## Slide 8: Sub-1GHz Frequency Regulation in the US
Relevant frequency regulation given in FCC 15.247 [2]
Two possibilities for high power signals (names are misleading):
  “Digitally Modulated Systems”  6dB bandwidth is at least 500kHz
  “Frequency Hopping Systems”  Typically 50 hopping channels with a channel spacing of at least 25 kHz and a dwell time of 0.4s
EPC global uses frequency hopping

## Slide 9: Implications of FCC 15.247
The downlink will effectively consume at least 500 kHz of spectrum (Digitally Modulated System) or 1.25 MHz (Frequency Hopping System)
Collisions of multiple downlink signals in sub-1GHz are practically not relevant as the On-Off-Keying Demodulator will only be able to decode the strongest signal
Goal should be minimized interference with existing users in sub-1GHz

## Slide 10: Sub-1GHz Frequency Regulation in Europe
High power transmission is only possible following the rules for UHF RFID systems defined in ETSI EN 302 208 [3]
Only 4 channels are supported (865.7 MHz, 866.3 MHz, 866.9 MHz, 867.5 MHz) within the complete EU
The channel bandwidth is limited to 200 kHz with strict channel masks
The on air-time shall not exceed 4s with an mandatory off-time of 100ms
 Only supports narrowband modultion

## Slide 11: Summary
UHF RFID supports different frequency bands by using wide-band receivers  no regional profiling
Downlink modulation is always based on On-Off-Keying
The On-Off-Keying receivers are only able to receive the strongest signal
Frequency regulation in the US may allow “wideband” and narrowband signals
Frequency regulation in Europe only allows for narrowband signals

## Slide 12: Literature
[1] “The EPC® Radio-Frequency Identity Generation-2 UHF RFID Standard” https://ref.gs1.org/standards/gen2/
[2] FCC 15.247 https://www.govinfo.gov/content/pkg/CFR-2013-title47-vol1/pdf/CFR-2013-title47-vol1-sec15-247.pdf
[3] ETSI EN 302 208 https://www.etsi.org/deliver/etsi_en/302200_302299/302208/03.03.01_60/en_302208v030301p.pdf