## Slide 1: Traffic Indication Bloom Filter (TIBF)
Date: 2024-05-15
Authors:

## Slide 2: Abstract
Problem: TIM enables a client to test if its AID is a member of the set S of AIDs for clients with traffic buffered at AP. Current EDP strategy: anonymize TIM using confidential AID. Proposals for confidential AID are:
  [1] obfuscate AID by adding random, per-epoch, BSS-wide offsets (concerns of insider attacks etc.), or
  [3] AP assigns new AID randomly every epoch and unicasts values to clients (concerns: traffic complexity)
Background: Bloom filters [4], provide efficient way to test if a value is a member of a set of values. Size proportional to size of the set. Not natively confidential. Returns either
  “possibly in set” (false positives allowed with low probability) or
  “definitely not in set” (false negatives not allowed).
Proposal: Supplement TIM with Traffic Indication Bloom Filter (TIBF) constructed from values derived from KDK (providing confidentiality/anonymity) and public nonce (avoiding replay).
  Positives : Anonymity w/out per-client unicasts. No false negatives. Efficiency.
  Neutral: Grows linearly with size of S. Small for small S . Big for big S .
  Negatives : False positives occur, but with low probability.

## Slide 3: TIM
TIM (traffic indication map) element
  TIM identifies the subset S of the STA associated to the AP for which traffic is pending and buffered in the AP.
    “Sleeping” STA: if STA in S then wake up, else go back to sleep
    Note: Also applies to MLO scenarios, replacing “STA” with “non-AP MLD”, and replacing “AP” with “AP MLD”
Currently TIM is computed from the unique AID assigned to each STA by the AP at association.
  Set S can be trivially determined from TIM. No anonymity
TGbi needs a TIM functionality which provides anonymity

## Slide 4: Current approaches to an anonymous TIM
Adding BSS-wide offsets. See [1] for details
Approach: Every epoch, a random BSS-wide AID offset is generated by AP & Client in BSS. This AID offset is added to the AID of each client
Advantages: No traffic. Simple
Disadvantages: Anonymity concerns (insider attacks, shared offset across BSS)
Randomly re-assigned AID. See [3] for details
Approach: Every epoch, AP randomly assigns new AIDs to the set of associated clients, and unicasts new AID values to clients
Advantages: Anonymous. Simple
Disadvantages: Traffic.
Neither is perfect. Suggests we should explore other options.

## Slide 5: Probabilistic equivalents to TIM
A probabilistic equivalent to TIM would provides a result to a STA indicating whether the STA has pending traffic, but allowing a small probability that the result is wrong
  A false negative occurs when a STA has traffic pending & result says the opposite. A sleepy STA gord back to sleep and never receive the traffic. False negative must be avoided.
  A false positive occurs when a STA has no traffic pending, & result says the opposite. A sleepy STA waked up & waits for traffic that never comes. This wastes battery but not bandwidth. Wasting battery occasionally is OK. False positive is acceptable with low probability.
I.E., in a probabilistic equivalent to TIM, the results received by the STA are either
  “Possibly [in set / traffic pending]” – sleepy STA wakes up, small prob of no pending traffic
  “Definitely [not in set / no traffic pending]” – sleepy STA sleeps, doesn’t miss pending traffic.

## Slide 6: Introduction to Bloom Filters
Quotes from [4], with some emphasis added and changes in square brackets.
A Bloom filter is a space-efficient probabilistic data structure, …, that is used to test whether an element is a member of a set. False positive matches are possible, but false negatives are not – in other words, a query returns either "possibly in set" or "definitely not in set".
Algorithm
  An empty Bloom filter is a bit array of m bits, all set to 0. There must also be k different hash functions defined, each of which maps or hashes some set element to one of the m array positions, generating a uniform random distribution. Typically, k is a small constant which depends on the desired false error rate [p], while m is proportional to k and the number [n] of elements to be added.
  To add an element, feed it to each of the k hash functions to get k array positions. Set the bits at all these positions to 1.
  To query for an element (test whether it is in the set), feed it to each of the k hash functions to get k array positions.
    If any of the bits at these positions is 0, the element is definitely not in the set;…
    If all are 1, then either the element is in the set, or the bits have by chance been set to 1 during the insertion of other elements, resulting in a false positive.

## Slide 7: Example: Generating BF with m=64, k=4, n=10
Element | Hash fn outputs | Bits set to 1 for input
1 | 35, 13, 18, 59 | 00001000 00000000 00000000 00001000 00000000 00000100 00100000 00000000
2 | … | 00000010 00000000 00001000 00000000 00100000 00000000 00000000 00000001
3 | … | 00000000 00011000 00000000 00000000 00100000 00000000 00000100 00000000
4 | … | 00000100 00000000 00010000 00001000 00000000 00100000 00000000 00000000
5 | … | 00000010 00000001 00100000 00000000 00100000 00000000 00001000 00000000
6 | … | 00000000 00000000 00000000 00000000 00001000 00000000 00000100 10000001
7 | … | 00001000 00000000 00000000 00010000 00000000 00010000 00000000 00010000
8 | … | 00010000 00000100 00000000 00000100 00000000 00000100 00000000 00000000
9 | … | 00000000 00000000 00010000 00001000 00000100 10000000 00000000 00001000
10 | 52, 32, 58, 42 | 00000100 00010000 00000100 00000001 00000000 00000000 00000000 00000000
Bloom filter output |  | 00011110 00011101 00111100 00011101 00101100 10110100 00101100 10011001 30 out of 64 bits set to 1.
Note: I cheated and selected these bits by hand in a way I hoped was random. They probably aren’t random.

## Slide 8: Example: Querying BF with m=64, k=4
Note: I cheated and selected these bits by hand in a way I hoped was random. They probably aren’t random.
Element | Hash Fn Outputs | Check Bits positions tested by Client A(j4) in set – True positive
4: in set | 21, 35, 44, 58 | 00000100 00000000 00010000 00001000 00000000 00100000 00000000 00000000
Bloom Filter |  | 00011110 00011101 00111100 00011101 00101100 10110100 00101100 10011001
Element | Hash Fn Outputs | Check Bits positions tested by Client not in set – False positive
11: not in Set | 4, 27, 42, 58 | 00000100 00000000 00000100 00000000 00001000 00000000 00000000 00010000
Bloom Filter |  | 00011110 00011101 00111100 00011101 00101100 10110100 00101100 10011001
Element | Hash Fn Outputs | Check Bits positions tested by Client not in set – True negative (no false negatives)
12: not in Set | 4, 22, 38, 44 | 00000000 00000000 00010000 01000000 00000000 01000000 00000000 00001000
Bloom Filter |  | 00011110 00011101 00111100 00011101 00101100 10110100 00101100 10011001

## Slide 9: Bloom Filter Parameter Selection
Bloom Filter (BF) Parameters
  n = number of elements in the set, p = desired false error rate
  m = number of bits in BF, k = number of “add/query” positions per element.
  Formula for optimal efficiency [5]
    n = ceil(m / (-k / log(1 - exp(log(p) / k)))) p = pow(1 - exp(-k / (m / n)), k) m = ceil((n * log(p)) / log(1 / pow(2, log(2)))); k = round((m / n) * log(2));
The parameter k and the ratio of m/n for n 4 can be approximated (rounded to closest multiple of 0.5) for a given p as shown below
False positive rate p | 0.1 | 0.05 | 0.025 | 0.01 | 0.005 | 0.0025 | 0.001
Bits set per element (k) | 3 | 4 | 5 | 7 | 8 | 9 | 10
Ratio of filter size/ set size (m/n) | 5 | 6.5 | 8 | 9.5 | 11 | 12.5 | 14.5

## Slide 10: Non-anonymous TIBF equivalent to TIM
TIM: enables a client to test if its (non-secret) AID is a member of a set S of AIDs for STA with traffic buffered at AP. Non-probabilistic. “Definitely no” o/“Definitely yes”
BF: enables testing if a value is a member of a set S. Probabilistic. “Definitely no” / “Possibly yes”
TIBF: Non-anonymous BF-based probabilistic equivalent to TIM:
  AP selects BF parameters m, k (BF size, number of “add/query” positions )
    Note: m, k depend on the size of S, not the total number of associated STA.
  For each STA with buffered traffic,
    AP “adds” STA’s (non-secret) AID to TIBF
  AP broadcasts TIBF, (o)k
  STA process TIBF to test if it has traffic buffered at AP
    STA “queries” its (non-secret) AID from TIBF.
  Result: “Definitely no” / “Possibly yes”
    “Definitely no”, STA acts as if it does not buffered traffic (e.g., sleeps). /STA is not in S w/ probability 1.
    “Possibly yes”, STA acts as if it has buffered traffic (e.g., wakes). STA is in S w/ probability (1- p ) .

## Slide 11: Anonymous TIBF equivalent to TIM
Replace AID with a secret, per-STA inSTA generated from STA’s KDK.
  AP selects BF parameters m, k (BF size, number of “add/query” positions )
  For each STA with buffered traffic,
    AP applies PRF using STA’s KDK to generate inSTA
    AP “adds” inSTA to TIBF
  AP broadcasts TIBF, (opt) k
  STA process TIBF to test if it has traffic buffered at AP
    STA generates inSTA as in step 2a.
    STA “queries” its inSTA from TIBF.
  Result: “Definitely no” or “Possibly yes”

## Slide 12: Replay protection
Note the following steps from Slide 11:
  2a. AP applies PRF using STA’s KDK to generate a inSTA
  4a. STA generates inSTA as in step 2a
Problem:
  In these steps, if there is no input to PRF other than KDK, then inSTA remains constant for the duration of the association, & the same bits positions of TIBF are used whenever the STA has buffered traffic.
  If these bits positions for a given STA are identified, then any other TIBF with those bits set to 1'b1 indicates (with high probability) the presence of that STA.
Solution:
  Include a per-epoch nonce (number used once) as an input to the PRF generating inSTA.
  This can be the same nonce input to the generation of MAC addresses and SN/PN Offsets.
    This nonce is not yet specified but could be TSF of scheduled epoch start or Epoch Number [2].
  Nonce is known to AP and STAs prior to receiving TIBF. Consequently, the AP and STAs can precompute inSTA prior to receiving TIBF

## Slide 13: Simple Hash Functions
Note the following steps from the Slide 11:
  2b. AP “adds” inSTA to TIBF
  4a. STA queries inSTA from TIBF
Problem:
  The definition of “adding” and “querying” involves a step of applying k hash functions to the element being checked (in this case, inSTA ) to obtain k random bit positions.
  Computing inSTA already involves invoking a PRF, so it would be convenient if the hash fn could be something very simple, rather than using a (complex) cryptographic hash fn.
  Note that a bit position in an m-bit TIBF is represented by log2(m) bits, where x indicates the smallest integer greater than or equal to x. Consequently, k random bit positions is represented by (k  log2(m)) bits
Solution:
  The PRF generates a value inSTA comprising (k  log2(m)) bits so inSTA can be partitioned into k blocks of log2(m) bits, where each block provides one of the k random bit positions.
    That is, the hash functions simply output a block of log2(m) bits from the input inSTA

## Slide 14: Full TIBF proposal
Per Epoch Steps
These steps would be implemented in HW or SW.
Per Beacon Step
This step would be implemented in HW (like TIM check). Checking a pre-determined set of bit positions is easy to implement.
  AP obtains values which are common for all STA
    AP selects BF parameters m, k (BF size, number of “add/query” positions )
    AP constructs a nonce.
  For each STA with buffered traffic,
    AP applies PRF using STA’s KDK and nonce to generate inSTA comprising (k  log2(m)) bits
    AP obtains k random bit positions from inSTA by partitioning inSTA into k blocks of log2(m) bits each
    AP “adds” inSTA to TIBF, by setting these k random bit positions to 1'b1
  AP broadcasts TIBF, (opt) k
  STA process TIBF to test if it has traffic buffered at AP
    STA constructs a nonce as in step 1b.
    STA generates inSTA as in step 2a.
    STA obtains k random bit position from inSTA as in step 2b.
    STA “queries” its inSTA from TIBF, by checking the values of TIBF at these k random bit positions
  Result: “Definitely no” or “Possibly yes”

## Slide 15: Transmission Efficiency
The table in Bloom Filter Parameter Selection provides appropriate values for TIBF parameters based on the false positive rate
  m: length of the TIBF in bits, as a constant times the number n of STA with traffic pending.
  k: number of random bit positions set to 1 for each STA with traffic pending.
Examples
  If aiming for a 1% false positive rate, then can use k = 7 and k = 9.5  n.
    E.g., 100 STA with traffic pending implies using a TIBF comprising m = 950 bits.
  If a higher 5% false positive rate is acceptable, then can use k = 4 and m = 6.5  n, where n is the number of STA with traffic pending.
    E.g., 100 STA with traffic pending implies using a TIBF comprising m = 650 bits, which is only 70% the size needed for 1% false positive rate
  Other false positive rates can be considered

## Slide 16: “Legacy” STA
A beacon can include both
TIBF for those STA supporting it, and
TIM for “Legacy” STA who do not support TIBF

## Slide 17: Conclusion
A Traffic Indication Bloom Filter TIBF can be used in the place of TIM to indicate the set of STA/non-AP MLD with traffic pending.
Anonymity and replay protection can be provided using KDK & nonces.
TIBF size example: if a false positive error rate of 1% is desired, then the TIBF size is 9.5 bits for each STA/non-AP MLD with traffic pending

## Slide 18: References
[1] 24/579r0 Periodic Obfuscation (automatic epoch)
[2] 24/604r8 Periodic Frame Anonymization
[3] 23/0873r02 Client Frame Tracking Countermeasures (CFTC)
[4] https://en.wikipedia.org/wiki/Bloom_filter
[5] Bloom Filter Calculator, https://hur.st/bloomfilter