## Slide 1: Coex SC Closing Report
Date: 2024-07-18
Authors:

## Slide 2: Abstract
Closing report for IEEE 802.11 Coex SC (Coexistence Standing Committee) for July 2024.

## Slide 3: Coex SC’s week at a glance
Met three times
Two Coex SC (only) slots
One Joint session with 15.4.ab

## Slide 4: ETSI BRAN Update to 802.11 (1/2)
EN 303 687 (Wireless Access System/Radio Local Area Network (WAS/RLAN) in the license-exempt 6 GHz band)
Version 1.1.1 published
EC criticizes normative reference to IEEE 802.11ax-2021 because EC does not recognize IEEE as SDO
TC BRAN asking EC to consider listing version 1.1.1 in OJEU – Even if this requires adding a note limiting how the standard may be used for providing presumption of conformity
Version 1.1.5 uses IEEE 802.11ax-2021 as informative reference
Inclusion of normative text describing requirements for operating Narrowband Frequency Hopping (NB FH) remains most important discussion item

## Slide 5: ETST BRAN Update to 802.11 (2/2)
EN 301 893 (Wireless Access System/Radio Local Area Network (WAS/RLAN) in the license-exempt 5 GHz band)
Normative reference to IEEE 802.11-2020 replaced by ISO/IEC/IEEE 8802-11:2022
Additional normative reference updated to latest version of standard
Next: National Standards Bodies (NSBs) requested to review final version; To be published as version 2.2.1 if successful
TC BRAN asking EC to extend the Date of Withdrawal of version 2.1.1 to 36 months once 2.2.1 is in OJEU

## Slide 6: ETSI BRAN Update on review of ITU-R WP5B.AR
ITU-R WP5B.AR contribution 556 by the World Meteorological Organization (WMO) and ITU-R R23-WP5B
  Discuss “Technical specifications of solid-state weather radar system – Draft liaison statement to WP 5A on efficiency of DFS regarding these radars in the 5 GHz frequency band”
  Announce that modern/future weather radars use/will use solid-state transmitters (SSTX)
  Will RLAN equipment be capable to detect the new radar pulses sequences that are transmitted a lower transmit powers?
Topic also discussed in 802.11 ITU AH

## Slide 7: Update from Bluetooth SIG Work
Recent actions
Participating in and contributing to the ETSI BRAN
Reviewing draft text for EN 303 687
Plans for ETSI BRAN #125
Bluetooth SIG (and others) plan to present a full Narrow Band Equipment (NBE) Clause 4 changes for the EN 303 687 draft
The plan is to then begin the development of Clause 5 changes for the NBE test plans

## Slide 8: Technical Submissions & Discussion Items (1/4)
NB Status Update (11-24/1143r0)
Discussion on interactions with 802.15.4ab / comment provided on the draft
Submissions presents Spectrum sensing based deferral (SSBD) as a suggested mandatory baseline mechanism
Narrowband Frequency-Hopping blocking Wideband (11-24/1138r0)
Analyse the probability of a wideband link being blocked from the channel access by multiple active narrowband frequency hopping (NBFH) links due to continuously received energy
Proposed mitigation dynamic Energy Detection Threshold (EDT)

## Slide 9: Technical Submissions & Discussion Items (2/4)
NB Hop Density (11-24/1150r0)
Discussion of relation between hop density and Wi-Fi channel access latency
Increased hop density causes more partially overlapping NB transmissions, which impacts WiFi transmissions
Discussed mitigation: (dynamically) control the NB duty cycle (DC)
High Duty Cycle NB Transmission vs Wi-Fi (11-24/1305r0)
Discussion how wultiple high duty cycle NB connection can result in very high channel access latency for Wi-Fi
Proposed mitigation: Prioritize certain channels (not or not frequently used by WiFi) for NB high duty cycle transmissions.

## Slide 10: Technical Submissions & Discussion Items (3/4)
Co-Existence of Wi-Fi with Narrowband Technology (11-24/1059r0)
Revisit of WNG presentation
Discussion of results with group members
Is 802.11 Compatible with SLB? (11-24/1148r0)
Raised question: NearLink, in its Wi-Fi-like technology, Smart Link Basic (SLB), may or may not be compatible with IEEE 802.11
Learn more about SLB if members step forward to bring in corresponding contribution
Discussion / feedback: Impact out of control of 802 (i.e. Coex); other urgent issues on the table should be prioritized.

## Slide 11: Technical Submissions & Discussion Items (4/4)
Joint Session Coex SC with 802.15.4ab
Discussion of: Energy Detect Proposal for NB Technologies (11-24/1182)
  Propose transmit power control (TPC)-based ED threshold
Review of comments received on the 802.15.4ab CAD

## Slide 12: Plans for September
Coex slots:
One joint 802.11 Coex SC – 802.15.4ab – Tuesday EVE
Two dot11 Coex (only) slot (one before and one after the joint session with .15.4ab)
  Tuesday AM 1
  Thursday AM 1
Joint dot11 dot15.4ab slot:
Continue discussion on channel access schemes
Coex (only):
Update on ETSI BRAN
Update on Bluetooth SIG
Technical submissions (tba)
Note: coexistence-related topics are welcome. Please contact the Chair

## Slide 13: Telcos
No telco scheduled.
May be announced with 10-day notice. Member feeling the need for telco and have submissions ready for discussion are asked to approach the Chair.

## Slide 14: References for this week
Agenda for this week: 11-24/0970
Snapshot Slide: 11-24/0971
Meeting / Chair’s Slide Deck: 11-24/0972
Closing report: 11-24/0973
Meeting minutes: 11-24/1313

## Slide 15: Coex Submissions
Bluetooth SG update | 11-24/1085
ETSI TC BRAN update | 11-24/1233
NB Status Update | 11-24/1143
Narrowband Frequency-Hopping blocking Wideband | 11-24/1138
NB Hop Density | 11-24/1150
Energy Detect Proposal for NB Technologies | 11-24/1182
Is 802.11 Compatible with SLB? | 11-24/1148
Co-Existence of Wi-Fi with Narrowband Technology | 11-24/1059
High Duty Cycle NB Transmission vs Wi-Fi | 11-24/1305