## Slide 1: EPCS Priority Access for Additional Use Cases
Date: 2024-06-06

## Slide 2: Abstract
This presentation discusses the need for EPCS Priority Access to support additional use cases

## Slide 3: Background
EPCS (Emergency Preparedness Communications Service) Priority Access features were specified in IEEE 802.11be for supporting National Security and Emergency Preparedness (NSEP) Communications
The use case required Non-AP MLD to be successfully authenticated and associated with an AP MLD before EPCS Priority Access can be enabled
AP MLD can grant the EPCS Priority Access once it verifies that non-AP MLD has the authority to use the features
Either non-AP MLD or AP MLD can request and teardown the EPCS Priority Access
This feature is optional in IEEE 802.11be

## Slide 4: Use Case and Requirement
Use Case I: During emergencies, network congestion may present users with emergency preparedness responsibilities from (re)associating. Enabling their access requires that STAs capable of obtaining EPCS Priority Access (i.e., those configured to be authorized for the service) should be able to transmit management frames for authentication and association with higher priority than normal STAs
  Failure to support the above will prevent EP personnel, whose mission is to help the citizens during emergencies and save lives, from performing their responsibilities
The current solution in IEEE 802.11be does not support the above use case
  The scope in IEEE 802.11be was limited and it was appropriate at that time
Given the market acceptance of the EPCS features, it is essential that we address this use case in IEEE 802.11bn

## Slide 5: Regulatory Update in USA
Federal Communication Commission (FCC) within United States released a new Report and Order (FCC-22-36) addressing the Wireless Priority Service (WPS) (a.k.a., NSEP Priority Service) in 2022
  Report and Order (R&O) specifies operation of priority service on public wireless communications networks
A Few highlights on Wireless Priority Service (WPS)
  Explicitly authorizes WPS preemption of public communications
    Preemption: process of terminating or degrading lower priority communications in favor of higher priority communications
  Expressly permits priority voice, video, and data sessions
  Expressly authorizes priority signaling (registration, invocation)
  Expands WPS eligibility to include additional users
  Clarifies that higher priority users take precedence over those with lower priority
    Five (5) priority levels were defined in earlier R & O
Note: Wireless Priority Service (WPS) is not mandated by the FCC

## Slide 6: Example Priority Services Offered in Various Countries
In Belgium, Blue Light Mobile service enables priority communications for users with national security and emergency preparedness responsibilities
  Priority involves both exemption network management controls for both lower-and higher-priority users and preemption of other traffic on behalf of higher-priority users
In Czech Republic, mobile crises communications service provides priority for three user classes and four priority levels
  Traffic assigned to priority levels based on user class and situation (e.g., crisis or non-crisis)
  Service includes variety of priority actions, e.g., calls at highest priority level can preempt lower-priority and non-priority calls other than emergency (i.e., 112) calls.
In Denmark, priority communications program provides preferential network access for first responders and individuals supporting critical infrastructure
  Supports two priority levels, one that includes preferential access by authorized users and another that, when declared, restricts network access by (i.e., preempts) non-priority users

## Slide 7: Use case II and Requirements
Use Case II: During crisis situation, WLAN may become congested with traffic from general public and users authorized for priority at several levels. To ensure authorized EPCS users can communicate to fulfill their emergency responsibilities, network may need to restrict access. Such restrictions could apply to public users with an exemption for EPCS users to ensure their ability to communicate.
  Form of Preemption: process of terminating (or degrading) lower priority communications in favor of higher priority communications
  Our aim is to provide mechanism that gives benefits of preemption, as defined, through controlled management of channel access
IEEE 802.11 networks should provide means to enable access control with an exemption on behalf of EPCS STAs
  Current EPCS priority in IEEE 802.11be only provides probabilistic advantage via EDCA
  Controlled access could provide critical advantage for NS/EP personnel under extreme conditions
Given the new regulatory and existing service requirements, it is important that we address the above in IEEE 802.11bn

## Slide 8: Use case II: Cellular Network Analogy
Cellular networks support concept of Access Class Barring
  Every station is assigned one of ten base access classes
  Select stations are also assigned one of a small set of elevated access classes
    e.g., access classes for network management, those making emergency (e.g., 911, 112) calls
  When network load increases, Base Station can (probabilistically) bar some classes from gaining access
    Base station broadcasts barring factors for ten base access classes
    User devices generate random number – only those with number less than barring factor are allowed attempt network access
    Select stations with an elevated access class are exempt from access class barring test
NS/EP users have dedicated access class that gives them exemption from access class barring
  This is analogy with desirable characteristics. Implementation within WLAN is TBD.

## Slide 9: Straw Poll -1
SP1: Do you agree to define mechanism(s) that enable APs to assign priority channel access to EPCS capable STAs during association?
Y –
N -
A -

## Slide 10: Straw Poll -2
SP2: Do you agree to define mechanism(s) that enable APs to preempt STAs to better support EPCS authorized STAs?
Note: Preempted STAs could include non-EPCS and lower priority EPCS STAs
Y –
N -
A -

## Slide 11: References
IEEE 802.11be Draft 5.1: https://www.ieee802.org/11/private/Draft_Standards/11be/Draft%20P802.11be_D5.1.pdf
FCC Review of Rules and Requirements For Priority Services, FCC-22-36, https://www.fcc.gov/document/fcc-modernizes-and-improves-its-priority-services-rules-0
https://mentor.ieee.org/802.11/dcn/22/11-22-1074-01-0wng-priority-access-fcc-r-o-and-additional-use-cases.pdf
Information on the Belgium Blue Light Mobile service was found in the following sources (Last viewed May 2024): https://www.astrid.be/en/services/blue-light-mobile, (in English), https://www.astrid.be/sites/public/files/2024-02/BLM_userguide_jan2024_NL.pdf (in Dutch), https://www.criticalcomms.com/content/news/belgium-astrid-launches-the-next-generation-of-its-blue-light-mobile-service (in English), https://www.criticalcomms.com/content/news/belgium-astrid-launches-the-next-generation-of-its-blue-light-mobile-service (in English)
Information on the mobile crisis communications services within the Czech Republic was found in the following sources (Last viewed: May 2024): http://www.hzscr.cz/soubor/04-krizova-komunikace-rezim-kompatibility-pdf.aspx (in Czech) and § 18 - Communication of the Integrated Rescue System (netstranky.cz) (in Czech).
Information on the mobile crisis communications services within Denmark was found in the following sources (Last viewed: May 2024): Beskrivelse af mobilprioriteringsordningen__CFCS_juli 2019 (in Danish) and vejledning-til-prioriteringsordningen-i-4g-netvark.pdf (cfcs.dk) (in Danish)
Description of access class barring: Performance analysis of access class barring for next generation IoT devices - ScienceDirect