## Slide 1: Some thoughts on security enhancement

## Slide 2: Introduction
A bunch of contributions discussed on security enhancement.
  Propose MAC Header protection to prevent SN reorder attack
  Propose control frame protection to prevent mimics attack
  Others.
In this contribution, we would like to discuss whether it’s necessary to define security enhancement feature in 11bn group

## Slide 3: Recap some security TG and the features
TGi (MAC Security Enhancements)[6 years]
  The PAR is approved in 2001, the draft is published in 2007
  Define RSNA protocol, including TKIP,CCMP, etc.
  Define RSNA security association management, including PTKSA,GTKSA,etc.
TGw(Protected Management Frames)[2005-2012]
    Define integrity protocol: BIP
    Define the protection of Robust Management frames protocol
    Update RSNA security association management, add IGTKSA,BIGTKSA,etc.
TGbi(Enhanced Data Privacy) [2021-2026]
  Update the protection of Robust Management frames protocol
    Including Beamforming/CSI/CQI Frame
  Encryption of the (Re)Association Request/Response Frame

## Slide 4: Conclusion for security enhancement feature
Security enhancement features are always defined in a dedicated TG, but it’s never in the mainstream.
  Mainstream: TGac,TGax,TGbe,etc.
It needs quite a long time to well define a security enhancement feature.
  At least 5--7 years from PAR approved to the draft published

## Slide 5: Potential/determined features identified in 802.11bn
Seamless roaming(*)
Power saving scheme
P2P operation enhancement
In-device coexistence
DSO(dynamically sub-channel operation)
NPCA(*non-primary channel access)
Relay function
MAP features
  C-TDMA,C-SR,C-(R)TWT,C-BF,etc.
Low latency feature
  QoS enhancement,Preemption
Security enhancement

## Slide 6: The problem of security enhancement topic involving in 11bn
Only 4 years left for TGbn to complete the task group Job according to TGbn timeline
  Usually, TGbn defines new features in the first two years, and makes the new features stable in the second two years.
Resource compete with other features
  Involving security enhancement feature causes other important features missing from 11bn draft definitely.
  In order to make the security enhancement feature stable, TGbn may have to defer it’s timeline for several years, and thus losing the best market opportunity.

## Slide 7: Propose to have a new TG for security enhancement feature design(1)
Following the traditional way,set up a dedicated TG to get rid of security enhancement topic with the following consideration.
  11ax device will stay in the market for quite a long time although 11be draft closely to be published
  MLO is still an optional feature for 11be device
  New feature design need to be applicable on both single-link and MLO device.
The usage of security enhancement feature on Wi-Fi 8 device
  If the security enhancement feature is well designed by a new TG, then there is nothing to block the end-user to apply this feature on Wi-Fi 8 device.
Optional or mandatory concern
  Other Wi-Fi standard group can decide whether its an optional or mandatory on Wi-Fi 8 device

## Slide 8: Propose to have a new TG for security enhancement feature design(2)
Benefit to TGbn
  TGbn could leverage the vacant resource to develop other important features in the very limited time slots.
Moreover, security enhancement feature is an independent topic, moving it to another TG won’t bring negative effect to other features defined in TGbn.
  If there is some compatible issue between the other 11bn features and security enhancement features, the talent member can well address it.

## Slide 9: Summary
Traditionally, security enhancement feature should be defined in a dedicated TG, but not in mainstream.
Propose to set up a new TG to dedicate on security enhancement feature design
TGbn should focus on other important features rather than security enhancement.

## Slide 10
THANK YOU 

## Slide 11: Reference
[1] 802.11 Timeline
[2] 23/1931r1 TGbn proposed Timeline
[3] 23/1914r1 TGbn Enhanced Security Considerations in UHR