## Slide 1: TGbi – AID anonymization
Date: 2024-06-08
Authors:
Name | Affiliations | Address | Phone | email
D. Ficara | Cisco |  |  | dficara@cisco.com
J. Contreras | Cisco |  |  | jacontre@cisco.com
U. Campiglio | Cisco |  |  | ucampigl@cisco.com
J. Henry | Cisco |  |  | jhenry@cisco.com
F. Lovison | Cisco |  |  | flovison@cisco.com

## Slide 2: Current discussion on AID
AID can be used to track STAs
11-24/886 – if each STA chooses on its own -> collisions
11-24/796 – proposal to use 12th bit to indicate transition or to expand space
11-24/915 – proposal to change offset for AID at each epoch
11-24/930 – proposal to use hashing (Bloom Filters) for TIM

## Slide 3: Key requirements
Backward compatible, AID domain is small, around ~2000 elements
AID to change at each epoch
In a given epoch, no AID collisions (no 2 STAs with same AID)
No tracking from eavesdroppers (External Privacy)
No tracking from other STAs in same ESS/BSS (Internal Privacy)
We want: otaAID sequence to satisfy the above list
Can we have it computed through an algorithm at each epoch?

## Slide 4: How about…
…generating AIDs via a function F? i.e..: otaAID= FK(inAID)
  Opt 1: each STA chooses its F: then, as mentioned in 11-24/886r0, we get collisions
  Opt 2: same F and same secret (K) for all STAs: then STA X may know about STA Y’s AID and predict next AID
…generating AIDs via asymmetric encryption ?
  The domain is ~2000 -> STA X can brute force all inputs and get AID for STA Y
…extend the input domain to F?
  Because output is ~2000, then F is a hash, which means we’ll have collisions
…use a perfect-hash function?
  Generally, perfect-hash functions have o(N) space requirements

## Slide 5: ...therefore
It looks like we either:
Accept collisions (relax on requirement 3)
  Need to rely on other mechanisms to solve them
Or Have an o(N) space mechanism
  Roughly it means sharing some portion of message for each STA at each epoch

## Slide 6: A – Collision discussion
In 11-24/930, a BF is used for TIM, and if a false positive (collision) arises, then the incorrect STA will wake up
-> rare (with configurable probability) event
Can we live with collisions, in general?
Downlink: can decryption/MIC solve collisions?
Uplink: TIBF solves triggered scenario, how to handle untriggered one?

## Slide 7: B - No collision proposal
We want a sort of perfect-hash, and this needs o(N). So let’s not fight maths: we need o(N) space for this problem
Proposal (high level):
N STAs, M epochs
AP computes next M AIDs for each STA, for next M epochs
AP shares next M AIDs to each STA in protected action frame after Key exchange
After M-(margin) epoch, AP sends next N AIDs
Goto 3

## Slide 8: B - No collision proposal
Implementation:
Allocation sent during EAP4Way
Action frame for subsequent allocations
Benefits:
If M epochs total time, is same as reauth-timer, no additional messages per station
Worst case, total messaging is divided by size of M on initial allocation, reducing per-STA AID messaging needed
Airtime is amortized (one message for N epochs):
~1000 epochs -> ~1400bytes. if epoch is 1s -> 1400 bytes every 16m40s

## Slide 9: Example
11
7
89
6
67
..
54
STA 1
Epoch 1
1
2
3
4
5
N
..
AID Slot
78
45
1
67
23
..
18
Epoch 2
5
99
28
17
21
..
44
Epoch 3
33
18
71
32
11
..
74
Epoch 4
STA 2
STA 3
STA 4
STA 5
STA N
[7,45,99,18]
[11,78,5,33]
[89,1,28,71]
[6,67,17,32]
[67,23,21,11]
[54,18,44,74]
M Epochs
EAPoL M4
MxN matrix: column = epoch, row = STA

## Slide 10: B - No collision proposal
In order to support transition period, either:
  use 1 bit to alternate epochs
  Or avoid using last AID from prev epoch
  In both cases, half AID domain can be used
Compatible with legacy STAs
  Present and future AIDs under AP's control
  No risk of collision with fixed-AID STAs

## Slide 11: What about 11ah - dynamic AID assignment
STA can request AID via
AP assigns AID (solicited/unsolicited)via
But:
1 msg per AID (heavy)
{AID Switch Count, Response Interval} redundant for epoch scheme
Hence not re-usable for our scenario without changes

## Slide 12: Summary
Current status of discussion on AID
Requirements
Collisions or no Collisions?
Proposal with AP coordination for no collisions

## Slide 13: Straw Poll #1
Do you support a mechanism where AIDs for next epochs are assigned by APs to STAs hence preventing any collision?