## Slide 1: Considerations on switching for NPCA
Date: 2024-07-07
Authors:
Name | Affiliation | Address | Phone | Email
Dongju Cha | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongju.cha@lge.com
Insun Jang |  |  |  | 
 |  |  |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | 
 |  |  |  | js.choi@lge.com
Hongwon Lee |  |  |  | hongwon.lee@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10225 Willow Creek Rd, San Diego, CA, USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
Non-Primary Channel Access (NPCA) allows the STAs to switch to the NPCH for performing backoff when PCH is busy due to the OBSS traffic
When the STAs switch to the NPCH, it is important to consider that STAs switch almost at the same time at earliest point to maximize the efficiency of NPCA
And also, whether the non-AP STA can switch to the NPCH that is outside of its operating channel width need to be discussed

## Slide 3: When to switch to the NPCH
Basically, to perform NPCA, STAs need to know the information about whether the traffic is from OBSS and for how long it can perform NPCA
  Switching to the NPCH at the earliest point it can get those information leads to maximizing the performance of NPCA
When the received PPDU is
  Non-HT PPDU containing (MU)-RTS,
    Considering the NAV reset issue, STAs need to switch after receiving the responding frame (e.g., CTS) or frame followed by the responding frame (e.g., Data frame)
    However according to the location of the STAs, some STAs can hear CTS frame while the other STAs cannot hear CTS frame but only hear Data frame
    This may lead STAs to switch to the NPCH at different time
    So, STAs that confirm the NAV during NAVTimeout switch after NAVTimeout to guarantee both of the NAV reset issue and switching at the same time

## Slide 4: When to switch to the NPCH (Cont’d)
When the received PPDU is
  Pre-11ax PPDU (e.g., HT, or VHT PPDU)
    Both of the information (whether the PPDU is from OBSS or not and TXOP) is available from MAC header after validating FCS
    Switching can be done after end of the first MPDU in A-MPDU
      Marginal time may be need to guarantee STAs switch at the same time
    For non-HT PPDU not containing (MU)-RTS, switching can be done after the PPDU
  HE, EHT or UHR PPDU,
    Since 11ax, BSS color and TXOP field has been contained in PHY header
    Switching can be done after validating the CRC field of HE-SIG-A for HE PPDU, U-SIG for EHT and UHR PPDU
AP announcing the hearable OBSS AP list (e.g., BSS color or BSSID) or triggered based UL in the NPCH can be a helpful to guarantee the different view problem for the case: AP is IDLE, STA is BUSY
  Non-AP STA switches only when the received OBSS traffic is included in announced OBSS AP list

## Slide 5: Where to switch
AP shall announce the NPCH within its BSS Operating Channel Width that will be used for backoff when the PCH is occupied
In case of the announced NPCH is
  Within operating channel width of non-AP STA, channel switching delay may be 0 or short (no hardware switching is required) while outside of operating channel width may need longer channel switching delay
Only allowing the non-AP STA to switch within its operating channel may limit the benefits of Non-Primary Channel Access, whether to allow non-AP STAs to switch to the NPCH that is outside of the its operating channel width need to be discussed

## Slide 6: Where to switch (Cont’d)
When non-AP STA is only allowed to switch within its operating channel width,
  STAs are less likely to have chance to perform NPCA
    20MHz non-AP UHR STA and 20MHz-only non-AP UHR STA cannot perform NPCA at all
    Cannot perform NPCA when BW of OBSS traffic is occupying operating channel width of non-AP STA having capability w/ NPCA ([Case 2] in fig.)
  Wide bandwidth may be underutilized
    80 MHz operating STA can utilize only partial bandwidth which means 20 or 40 MHz PPDU is available ([Case 1] in fig.) while 20, 40 or 80 MHz PPDU can be transmitted ([Case 3] in fig.)
Thus, to maximize the efficiency of NPCA, non-AP STAs need to be allowed to switch outside of its operating channel width while considering channel swithch delay
[Case 1]
[Case 2]
[Case 3]

## Slide 7: Channel Switch Delay
Non-AP STAs need to signal their channel switch delay because,
  Basically, channel switch delay for NPCA means the delay that is required when the STA switches between the PCH and NPCH
  TXOP holder can guarantee that TXOP responder has done switching to the NPCH
  Also, by finishing the TXOP on the NPCH before Basic NAV – max (switch delay of TXOP holder, switch delay of TXOP responder) medium sync. can be guaranteed when STAs switches back to the PCH
Considerations on signaling the channel switch delay
  In case of the channel switch delay from the PCH to SCH and vice versa is different, maximum value can be signaled or it can be signaled seperately
  Also, channel switch delay of non-AP STA side may be depend on whether the NPCH is within its operating channel width or not
  Considering the case of non-AP STA changing its operating mode (e.g., channel width), channel switch delay can be signaled seperately when it switches within and outside of operating channel width

## Slide 8: Conclusion
In this contribution, we discussed some considerations when STAs switching to the NPCH
  When can STAs switch at the earliest point while guaranteeing NAV does not reset
  Whether the non-AP STAs can switch outside of its operating channel width
  Some considerations on the channel switching delay

## Slide 9: SP1
Do you agree to include the following into the 11bn SFD?
  STA that is capable of NPCA indicates its channel switch delay that is required when the STA switches between the primary channel and the NPCA primary channel
  How to indicate is TBD

## Slide 10: SP2
Do you agree to include the following into the 11bn SFD?
  Non-AP STA that is capable of NPCA is allowed to switch to the announced NPCA primary channel that is outside of its operating channel width
  NPCA Primary channel is in AP’s BSS operating channel width

## Slide 11: SP3
Do you agree to include the following into the 11bn SFD?
  STA that is capable of NPCA switches to the NPCA primary channel after validation check of CRC of the HE-SIG-A field when the OBSS PPDU is HE PPDU format

## Slide 12: SP4
Do you agree to include the following into the 11bn SFD?
  STA that is capable of NPCA switches to the NPCA primary channel after validation check of CRC of the U-SIG field when the OBSS PPDU is EHT/UHR PPDU format

## Slide 13: SP5
Do you agree to include the following into the 11bn SFD?
  STA that is capable of NPCA switches to the NPCH after validation check of FCS of the first MPDU in the OBSS PPDU that is not HE/EHT/UHR PPDU or is non-HT PPDU that does not include an (MU-)RTS frame

## Slide 14: SP6
Do you agree to include the following into the 11bn SFD?
  STA that is capable of NPCA switches to the NPCH immediately after NAVTimeout period when all the following conditions are met:
    Receives OBSS PPDU that contains RTS or MU-RTS
    The STA does not reset the Basic NAV set from RTS or MU-RTS during the NAVTimout period