## Slide 1: Initial Control Frame Exchange for Low Latency
Date: 2024-07-12
Authors:

## Slide 2: Introduction
Various low latency-related mechanisms are under discussion for 11bn
  C-TDMA [1-5], C-RTWT SP [6-10], TXOP Preemption [11-15], HiP-EDCA [16, 17], etc.
They have similar purposes that allow LL STAs to transmit LL traffic first by applying modifications on top of the baseline protocols
In this contribution, we propose to enhance initial control frame exchanges to reorder the following frame exchange sequence to deliver LL traffic first

## Slide 3: ICF/ICR exchange rules
ICF/ICR exchange sequence defined in the baseline
  A STA that receives an RTS frame addressed to it shall respond with a CTS frame if medium is idle
  Similar rules are applied for the other control frames (e.g., MU-RTS, BSRP TF, etc.)
Low latency-related problematic scenario based on the baseline rule
  A STA intending to transmit LL traffic receives an RTS frame, then it shall respond with a CTS frame and join the frame exchange sequence as a TXOP responder (LL traffic delayed)
RTS
Non-LL STA
LL STA
3
0
CTS
LL traffic enqueued
PPDU (non-LL traffic)
BA
LL STA acts as a TXOP responder
(LL traffic transmission is delayed due to the initiated frame exchange sequence)
BA
PPDU (non-LL traffic)

## Slide 4: ICF/ICR exchange rules (cont’d)
We can consider letting a STA having LL traffic to not respond to the received ICF by modifying the ICF/ICR exchange rule
  LL STA, after not responding to ICF, continues channel access procedure for its LL traffic transmission
Modifying the ICF/ICR exchange rules seems beneficial for LL traffic transmission, but may cause the following problems:
  A STA transmitting an ICF for LL traffic transmission cannot obtain a TXOP when the recipient STA decides not to respond to the ICF
  If a STA doesn’t respond to the received ICF, the ICF transmitter doubles the CW based on the failed ICF transmission

## Slide 5: Proposal
Two STAs inform each other about its LL requirement by using ICF/ICR
  The exchanged information can affect the following frame exchange sequence
Case examples (w/ 1-bit LL/non-LL indication)
  Case 1: ICF (non-LL) & ICR (LL)
    After ICR, TXOP holder shares/allocates TXOP/RU to the TXOP responder
  Case 2: ICF (LL) & ICR (LL)
    After ICR, TXOP holder transmits its LL traffic first
    If there is remaining TXOP, the TXOP holder shares/allocates TXOP/RU to the TXOP responder
  Case 3: ICF (LL) & ICR (non-LL), ICF (non-LL) & ICR (non-LL)
    TXOP holder manages frame exchange sequence based on the baseline

## Slide 6: Illustrations
ICF
STA1
(non-LL)
STA2
(LL)
3
0
ICR
(LL)
TF
/RDG
LL Data
Non-LL Data
ICF
(LL)
STA1
(LL)
STA2
(LL)
3
0
ICR
(LL)
TF
/RDG
LL Data
LL Data
BA
BA
BA
BA
Non-LL Data
Case 1 frame exchange sequence
Inserted sequence
Inserted sequence
Case 2 frame exchange sequence
LL traffic enqueued
LL traffic enqueued
LL traffic enqueued
ICF (LL): Initial control frame w/ LL traffic indication
ICR (LL): Initial control response w/ LL traffic indication
TF: Basic/MU-RTS TXS Trigger frame
RDG: Reverse Direction Grant

## Slide 7: Discussions – ICF from Legacy STAs
When the TXOP holder is legacy STAs, the frame exchange sequence cannot be modified based on the 11bn TXOP responder’s low latency requirement
Therefore, we may need to consider postponing TXOP initiation of legacy STAs by allowing an AP (with TBD conditions) not to respond to an ICF from legacy STAs
The above TBD conditions should be carefully designed
  One condition could be R-TWT/C-RTWT SP
    An AP that received an ICF from a legacy STA during R-TWT/C-RTWT SP may not respond to the ICF
  Another condition could be LL traffic transmission
    An AP that has buffered LL traffic to a legacy STA may not respond to the ICF from that legacy STA
    (For further discussion) An AP that has buffered LL traffic may not respond to an ICF from legacy STAs

## Slide 8: Discussions – ICF under MLO
There are cases where a non-AP MLD that received the ICF shall respond with an ICR and also shall change its operating mode
  e.g., a non-AP MLD with two EMLSR links may receive an ICF on EMLSR link-1 while trying to transmit LL traffic through EMLSR link-2
    LL traffic transmission on the EMLSR link-2 will be delayed
    Note: An MLD w/ NSTR link pair has the similar issues
It means that a STA affiliated with an MLD also needs to consider low latency requirements of the other links when deciding whether to respond to the received ICF

## Slide 9: Summary
Enhancements on the ICF/ICR for LL traffic have been discussed
  Enhancements on the initial frame exchange are proposed to reorder the following frame exchange sequence to deliver LL traffic first
TXOP initiation of a legacy STA can be controlled by AP for certain conditions
Frame exchange sequence between two MLD STAs should be managed based on low latency operation on the MLD links

## Slide 10: Straw Poll 1
Do you agree to define a mechanism(s) to ensure that latency-sensitive traffic is transmitted with higher priority between TXOP holder and TXOP responder?
  Initial control frames (ICF/ICR) carry information to coordinate the order of frame exchanges within the corresponding TXOP.
  Details of the initial control frames are TBD.

## Slide 11: Straw Poll 2
Do you agree that an UHR AP may not respond to the received initial control frame from non-UHR STAs when TBD condition(s) is met?
  One condition is that the initial control frame is received during R-TWT SP of its BSS

## Slide 12: References
[1] 11-23/1895r2 C-TDMA frame sequence Abhishek Patil
[2] 11-24/0093r2 NAV setting for Coordinated TDMA Dibakar Das
[3] 11-24/0411r0 TXOP Return in C-TDMA Geonhwan Kim
[4] 11-24/0375r1 NAV protection for C-TDMA Si-Chan Noh
[5] 11-24/0423r0 NAV Rules in C-TDMA Sanket Kalamkar
[6] 11-23/2022r1 r-TWT for multi-AP follow up Laurent Cariou
[7] 11-23/1916r1 R-TWT Coordination in Multi-BSS Sunhee Baek
[8] 11-23/1952r3 Coordinated R-TWT for Multi-AP scenarios – Follow up Liuming Lu
[9] 11-24/0408r0 Enhancements on TWT SP Management Muhammad Kumail Haider
[10] 11-24/0827r0 OBSS Interference Impact on CR-TWT and Enhanced Channel Access Rules Qing Xia
[11] 11-23/1886r3 Preemption techniques to meet low-latency (LL) targets Giovanni Chisci
[12] 11-24/0103r0 TXOP level preemption for Low latency application in 802.11bn Juan Fang
[13] 11-24/0247r0 Legacy STA and OBSS Issues for Preemption Yunbo Li
[14] 11-24/0390r0 A Uniform Procedure for Preemption Yunbo Li
[15] 11-24/0470r0 rethinking-preemption Dmitry Akhmetov
[16] 11-23/2126r3 Low latency channel access follow up Dmitry Akhmetov
[17] 11-24/0840r0 hip-edca-proposal Dmitry Akhmetov