## Slide 1: Investigation of LDPC Improvements
Date: 15-July-24

## Slide 2: Introduction
LDPC Codes in 802.11
  LDPC FEC was introduced in 2007 for 802.11n and typical data rates in the tens of Mbit/s
  Codeword length up to 1944 bits at column weight around 3.5
Current Situation
  Increased data rate results in an OFDM symbol to contain many of FEC codewords
  In the last years, LDPC codes improved through the introduction in various technologies, e.g., 5G wireless, PON, DSL
  Ultra-high reliability drives use cases with low PER, where coding gain is increasingly important

## Slide 3: Details of current FEC and new Proposal
Current FEC
  3 code sizes: N=648, 1296, 1944
  4 code rates: 1/2, 2/3, 3/4, 5/6
  Quasi-cyclic codes with circulant sizes 27, 54 and 81
  Average column weight ~3.5
  Double-diagonal structure (simple encoder)
New Proposal [4]
  Additional size N=3888
  Same code rate and code structure

## Slide 4: Other recent LDPC Codes
PON [3]
  Single code rate ~0.85 (57/67.5), single code size: N=17280
  Circulant size 256, default puncturing 384bit, avg. column weight 4
Mgfast [2]
  Single code rate 0.75 (18/24)
  Variable code size 1536-12288 bit, single mother code
  Cirulant sizes 64-512 bit, default puncturing 1 circulant, avg. column weight 3
5G [1]
  Variable code size 0.5-0.81 from one code (hybrid ARQ) 22/44-22/27
  8 mother codes with 8 shift factors, largest code is 8448 bit payload
  2 columns default (data)-puncturing, avg. column weight 4.5

## Slide 5: This Submission
In [4], a high complexity decoder implementation (sum-product decoding with 20 max. iterations) is used.
Typical implementations likely use simpler decoders, e.g., min-sum decoding.
This submission presents a performance comparison with min-sum decoding with 10 max. iterations.
A comparison with LDPC codes used in other technologies is given.

## Slide 6: AWGN Performance Comparison Rate 1/2 code, 4-QAM
WIFI L K=972 N=1944
  Current code
WIFI XL K=1944 N=3888
  New code from [4]
Mgfast K=3584 N=7168
  Largest Mgfast code, 5632 bit shortened
5G K=8448 N=16896
  Largest 5G code, 768 bit punctured
PON K=3072 N=6144
  11520 bit shortened

## Slide 7: AWGN Performance Comparison Rate 2/3 code, 64-QAM
WIFI L K=1296 N=1944
  Current code
WIFI XL K=2592 N=3888
  New code from [4]
Mgfast K=7168 N=10752
  Largest Mgfast code, 2048 bit shortened
5G K=8448 N=12672
  Largest 5G code
PON K=6144 N=9216
  8448 bit shortened

## Slide 8: AWGN Performance Comparison Rate ¾ code, 256-QAM
WIFI L K=1458 N=1944
  Current code
WIFI XL K=2916 N=3888
  New code from [4]
Mgfast K=9216 N=12288
  Largest Mgfast code, 512 bit punctured (default)
5G K=8448 N=11264
  Largest 5G code, 1024 bit punctured to get rate 3/4
PON K=9216 N=12288
  PON code, 5376 bit shortened to get rate 3/4

## Slide 9: AWGN Performance Comparison Rate 5/6 code, 1024-QAM
WIFI L K=3240 N=1944
  Current code
WIFI XL K=1620 N=3888
  New code from [4]
Mgfast K=9216 N=11060
  Largest Mgfast code, 1740 bit punctured
5G K=8448 N=10138
  Largest 5G code, punctured to 10138 bit
PON K=13440 N=16128
  384 bit punctured and 1152 bit shortened

## Slide 10: Observations from AWGN Simulations
The 3888 bit WLAN codes show good performance at a short code length (and thus, low decoder complexity).
This gives a good performance/complexity trade-off.
At rate ½, the 5G code performs best (designed for this code rate)
At rates 2/3 and ¾, the Mgfast code performs best (designed for code rate ¾)
At rate 5/6, the PON code performs best (designed for a code rate of 0.85)
As the MGFAST code provides a good performance on most code rates and constellation sizes, it is used for reference for WLAN channel simulations

## Slide 11: D NLOS 2x2 1 Stream Channel Performance Rate 1/2 code, 4-QAM
Up to 0.75dB gain, depending on the channel, of 3888 bit code at PER 0.01

## Slide 12: D NLOS 2x2 2 Streams Channel Performance Rate 2/3 code, 64-QAM
Around 1dB gain of 3888 bit code at PER 0.01

## Slide 13: D NLOS 2x2 2 Streams Channel Performance Rate 3/4 code, 256-QAM
Around 1 dB gain with the longer Wi-Fi code

## Slide 14: D NLOS 2x2 2 Streams Channel Performance Rate 5/6 code, 1k-QAM
Around 1 dB gain with a larger Wi-Fi code

## Slide 15: Observations from D NLOS Simulations
SNR gains of larger LDPC like the new Wi-Fi codes on real channels are higher than in AWGN channels.
The 3888 bit Wi-Fi code gives a good performance/complexity trade-off.
The performance gains obeserved in [4] are visible with a low complexity LDPC decoder, too.
The SNR gain of the Mgfast code is higher, but it is 3x the length of the 3888 bit WLAN code.

## Slide 16: Rate-vs.-Range Simulation Nss=2 fixed
Conditions
  4 Channels, 0.2dB SNR steps
  >10k codewords per SNR
  10000 Byte packet
  no puncturing/shortening (large frame)
Observations
  Rate 3/4, 4QAM doesn’t work well (all codes)
D NLOS 2x2 2 streams

## Slide 17: Rate-vs.-Range Simulation Nss optimized
Conditions
  4 Channels, 0.2dB SNR steps
  >10k codewords per SNR
  10000 Byte packet
  no puncturing/shortening (large frame)
Observations
  Rate 3/4, 4QAM issue is not visible (1SS used)
D NLOS 2x2 1 or 2 streams (opt.)

## Slide 18: Details on Rate-Reach Observations
MCS2 vs. MCS3, 2 streams
  Required SNR for 4QAM, Rate ¾ is higher than 16QAM, Rate ½. This is the case for all codes and thus, not associated with the LDPC code matrix
SNR-vs.-goodput of larger codes
  Longer codewords have a much steeper transition from 0 to max. goodput  latency improvement
MCS2
MCS3
Higher latency due to packet errors

## Slide 19: Longer Codes for 2.4 GHz Band?
A 3888 bit LDPC decoder, as presented in [4] is equivalent to two parallel LDPC decoders for 1944 bit.
For higher bandwidth channels, e.g., 160MHz or 320MHz, multiple parallel decoders are typically used and thus, the overhead for introducing a 2x size codeword is small.
  This may not be the case for 2.4GHz where the max. bandwidth is 40MHz.
For the 2.4 GHz band it is recommended not to support 3888 bit LDPC codes to limit the added complexity.

## Slide 20: Conclusions
The proposed 3888 bit code shows a performance improvement on the AWGN channel and for WLAN channels, while it is still shorter than other state-of-the-art LDPC codes.
Longer LDPC codewords improve latency, as the packet error rate at the max. goodput operationg point is lower.
For code performance comparisons, limited decoder complexity (e.g., min-sum 10 iteration) should be considered. New codes shall provide gains with limited decoder complexity.
Implementation complexity can be limited by introducing larger codes in 5 and 6GHz bands, only.

## Slide 21: SP
Do you agree to not support longer LDPC codewords for 2.4 GHz band?
Yes
No
Abstain

## Slide 22: References
[1] 3GPP, “Technical Specification Group Radio Access Network; NR; Multiplexing and channel coding (release 15). 3GPP TS 38.212. September 2017
[2] ITU, Multi-gigabit fast access to subscriber terminals (MGfast) - Physical layer specification, ITU-T G.9711, April 2021
[3] ITU, Higher speed passive optical networks - Common transmission convergence layer specification, ITU-T G.9804.2, September 2021
[4] Rethna Pulikkoonattu et.al, “Longer Block-Length LDPC Codes”, IEEE 802.11-23-1985R4, 2024-05-12

## Slide 23: APPENDIX

## Slide 24: Simulation parameters
Parameter | Value
LDPC decoder algorithm | MinSum
Algorithm details | Row layered decoding
Max. iterations | 10
Bandwidth | 160 MHz
AP TX Power | 21 dBm
Channel model | D NLOS [8]
MCS | 
Frequency | 5.25GHz
Remarks:
[4] used sum-product decoding with max. 20 iterations and thus, a much higher complexity decoder as reference