## Slide 1: EML(SR/MR) Based Dynamic Power Save Design
Date: 2024-07-15
Authors:

## Slide 2: Background
Different power save mechanisms including scheduled PS, unscheduled PS, dynamic PS and link disablement are discussed in previous contributions and proposals [2-14].
This contribution focuses on EML(SR/MR) based dynamic power save, and specifically the framework for AP and STA to transition from a lower capability mode to a higher capability mode upon reception of an initial control frame [2-6].
  The lower capability mode refers to e.g., 20 MHz BW, one SS, limited data rates, PPDU format.
  The higher capability mode refers to e.g., operating BW, NSS and MCSs, with at least one value of these parameters that indicates higher capability than that used in the lower power capability mode.
  Padding is applied in the ICF frames to provide sufficient time to tolerate the transition delay.

## Slide 3: Recap
In EML(SR/MR) operation, a STA transmits or receives frames on the link on which the initial Control frame was received and shall not transmit or receive on the other EML(SR/MR) link(s) until the end of the frame exchange.
The EMLSR supports at least one spatial streams (SS) for on any EMLSR enabled link.
The EMLMR supports a specific NSS on any EMLMR link after responding to the initial frame.
  The NSS value is indicated in the EMLMR supported MCS and NSS Set of EML Control field of the EML Operating Mode Notification frame.

## Slide 4: Problem
  When one of the EML(SR/MR) links is used for transmitting or receiving frames with higher capability mode in dynamic PS, following issues may occur on the other EML(SR/MR) link(s):
    Lost of medium synchronization if all SS are used for TX/RX on the EML(SR/MR) link.
      The medium synchronization issue could be solved if any SS is left for listening.
      The configuration of SSs could be implementation dependent [1] or set by e.g., EMLMR supported MCS and NSS Set.
    Inefficient power consumption if AP or STA using any remaining SS for listening is not operating in lower capability mode.
  In current 11be spec, the EML(SR/MR) operation can only apply to non-AP MLD.
  The EML(SR/MR)-based power save mechanisms for AP MLD is missing.

## Slide 5: Power Save for other EML(SR/MR) Enabled Links
  When transmission and reception for a STA with higher capability mode are initiated after the exchange of ICF and ICR on one of the EML(SR/MR) links, e.g., Link 2 in case a) and b).
  There may be remaining SS(s) on other EML(SR/MR) link(s), e.g., Link 1 or Link 3.
  Other affiliated STA(s) on Link 1 or Link 3 could either maintain lower capability mode or transition from lower capability mode to doze mode (i.e., power off) until the affiliated device finishes the transmission or reception with higher capability mode on Link 2.
  Transition to doze mode helps save more power (e.g., case a), while keeping listening with lower capability mode on remaining SS(s) (e.g., case b) helps maintain medium synchronization.
Case a) EML(SR/MR) mode enabled link(s) transition from lower capability to doze state
Case b) EML(SR/MR) mode enabled link(s) maintain lower capability
Non-AP MLD
2.4 GHz
(Link 1)
STA1
5 GHz
(Link 2)
STA2
6 GHz
(Link 3)
STA3
Radios
AP MLD
2.4 GHz
(Link 1)
AP1
5 GHz
(Link 2)
AP2
6 GHz
(Link 3)
AP3
EML(SR/MR) mode enabled on L1,2,3
ICF
ICR
DL PPDU
ACK
STA2 on SS y
UL PPDU
ACK
Power Status:
STA1, 3
Higher Capability
Lower Capability
Doze
Doze
Doze state
SS x
SS x+1
SS y
SS y+n
…
SS z
SS z+1
DL PPDU
ACK
UL PPDU
ACK
STA2 on SS y+n
Radios
Radios
Non-AP MLD
2.4 GHz
(Link 1)
STA1
5 GHz
(Link 2)
STA2
6 GHz
(Link 3)
STA3
AP MLD
2.4 GHz
(Link 1)
AP1
5 GHz
(Link 2)
AP2
6 GHz
(Link 3)
AP3
EML(SR/MR) mode enabled on L1,2,3
ICF
ICR
DL PPDU
ACK
STA2 on SS y
UL PPDU
ACK
Power Status:
STA1, 3
Higher Capability
Lower Capability
SS x
SS x+1
SS y
SS y+n
…
SS z
SS z+1
DL PPDU
ACK
UL PPDU
ACK
STA2 on SS y+n
Radios
Radios
Radios

## Slide 6: EML(SR/MR) based Dynamic PS on STA side
STA(s) operating on enabled EML(SR/MR) link(s) should operate with the lower capability mode when the EML(SR/MR) mode starts on each of the enabled EML(SR/MR) link(s).
An AP MLD initiates frame exchanges with the non-AP MLD on one of the EML(SR/MR) links shall first exchange ICF and ICR frames with the non-AP MLD.
  Intermediate FCS and Padding fields should be included in the ICF frame before the FCS field.
  ICF may indicate the BW, NSS and max MCS for transmission and reception in the higher capability mode [3,5]
A STA in lower capability mode may initiate CCA over the wider operating BW without receiving any ICF frame from its associated AP MLD.
  The STA can transmit an un-solicited ICR frame or ICF to the affiliated AP on the wider operating BW after identifying the CCA is idle.
STA(s) operating on the EML(SR/MR) link(s) may transition from higher capability mode to lower capability mode under following conditions.
  STA finishes the frame exchange sequence with higher capability.
  After responding ICR frame to ICF, STA doesn’t receive any response within certain timeout.

## Slide 7: EML(SR/MR)-based PS on AP MLD side
AP MLD may keep at least one link to operate as EML(SR/MR) disabled link while other links are operating as EML(SR/MR) enabled links.
  The AP operating on the EML(SR/MR) disabled link(s) should be kept in active mode. These links should be able to support the following functionalities:
    Discovery, active probing and association for all STAs (including pre-EHT STA)
    Signaling other affiliated AP/STAs that maybe in doze mode on other links
AP MLD with lower capability mode may receive collide ICFs from different non-AP MLDs on one of the EML(SR/MR) enabled links.
  AP MLD may broadcast un-solicited ICR frames on the wider operating BW after detecting CCA idle.
  AP MLD may transmit and receive MU PPDU with multiple STAs when operating in higher capability mode
AP MLD with lower capability mode may receive ICFs from different non-AP MLDs on more than one of the EML(SR/MR) enabled links.
  The received ICF on one link may overlap in time with another ICF or the following frame exchange sequences on another link.
  AP MLD may only response ICR on one of the EML(SR/MR) enabled links.

## Slide 8: Summary
We propose that when an affiliated STA is transmitting or receiving frames with higher capability mode on one of the EML(SR/MR) link(s), the other affiliated STA(s) on other EML(SR/MR) link(s), with available NSS(s), could
  Either maintain lower capability mode
  Or transition from lower capability mode to doze mode
We discussed the differences in terms of EML(SR/MR) based Dynamic PS between AP MLD and non-AP MLD.
  AP MLD may keep at least one link to operate as active link.
  AP MLD may receive collide ICFs from different non-AP MLDs on one of the EML(SR/MR) links.
  AP MLD may receive ICFs from different non-AP MLDs on more than one of the EML(SR/MR) links.

## Slide 9: References
[1] 11-20-0562-07-00be-enhanced-multi-link-single-radio-operation
[2] 11-23-0010-00-0uhr-considerations-for-enabling-ap-power-save
[3] 11-23-1875-01-00bn-power-save-proposal-for-non-ap-mobile-ap
[4] 11-23-1936-00-00bn-ap-mld-power-save-follow-up
[5] 11-23-1965-02-00bn-dynamic-power-save-follow-up
[6] 11-23-2003-01-00bn-client-power-save
[7] 11-23-0015-00-0uhr-ap-mld-power-management
[8] 11-23-2040-01-00bn-enabling-ap-power-save-follow-up
[9] 11-23-0225-00-0uhr-considering-unscheduled-ap-power-save
[10] 11-23-1965-02-00bn-dynamic-power-save-follow-up
[11] 11-24-0352-00-00bn-enabling-unscheduling-ap-ps-follow-up
[12] 11-24-0450-00-00bn-a-proposal-for-uhr-soft-ap-power-save
[13] 11-24-0485-00-00bn-low-power-listening-mode-for-clients
[14] 11-23-1922-01-00bn-multi-link-sm-power-save-mode
[15] 11-20-0562-07-00be-enhanced-multi-link-single-radio-operation