## Slide 1: Further Considerations on In-Device Coexistence
Date: 2024-07-11
Authors:

## Slide 2: Introduction
The accommodation of other radio access technologies together has discussed under the term “In-Device Coexistence (IDC)” [1]-[4]
  At certain times or frequencies, it may not be possible for different radio access technologies to operate simultaneously
    2.4 GHz band: Bluetooth / BLE / P2P
    5 & 6 GHz bands: P2P, UWB, 3GPP radio (such as LAA / NR-U)
In a STA that simultaneously utilizes multiple radio access technologies, it is inevitable to experience performance degradation caused by coexisting IDC activities (e.g. a sudden drop of data rates, increased latency, buffer overflow, etc.)
  One effective approach would be to inform AP about IDC activities and define appropriate actions based on this information.

## Slide 3: Backgrounds
From our perspective, it is valuable to discuss periodic, deterministic, and long-term IDC as the majority of use cases in mobile devices follow this pattern
By supporting IDC, we enable the execution of one or more unavailable durations within a specified periodic or instantaneous timeframe
  Existing protocols [5] can be considered as potential options for IDC, requiring modification and extension to meet specific requirements of IDC
    The TWT element can include subfields specifying the duration of an IDC activity and the interval between two consecutive IDC activities.
    The Channel Usage element can contain relevant channel information related to the operating channel of IDC
    There are other elements like QTP, QPR that can potentially become part of the protocol supporting IDC functionalities

## Slide 4: Further Considerations on IDC
Each IDC activity may have a periodicity requirement to ensure its stable and reliable operations
  The requirement can be defined by specifying parameters such as the unique start time, duration, interval, and expected number of repetitions
  In the scenario where multiple IDC activities are taking place within a STA, the availability of Wi-Fi should be assessed while considering all these concurrent IDC activities
  An AP should avoid any downlink transmission or uplink scheduling for a STA when the STA is in its unavailable periods
Wi-Fi
IDC1
IDC2
Wi-Fi
IDC1
Wi-Fi
IDC1
Wi-Fi
IDC1
IDC2
Interval of IDC1
Period of IDC1
Interval of IDC2
Period of IDC2
…

## Slide 5: Further Considerations on IDC
To offer practical support for IDC of STAs, we are considering methods:
  To indicate the following actions related to IDC activities:
    Adding a new IDC activity or removing an existing one
    Suspending, resuming, or reconfiguring an already added (or registered) IDC activity
  To inform the specific radio mode of IDC activities (such as Tx-/Rx-only IDC) and Wi-Fi capabilities (like the number of spatial streams (NSS) and the operating bandwidth) while engaging in IDC activities.
IDC2 Rx
IDC1 Rx
IDC1 Rx
1x1 Rx Available
2x2 Rx Available
2x2 Rx Available
Wi-Fi
IDC1
Add IDC1
(Cycle: T1/P1)
Reconfigure IDC1
(Cycle: T1/P1  T11/P11)
Add IDC2
(Cycle: T2/P2)
Suspend / Remove IDC1
IDC2

## Slide 6: Further Considerations on IDC
To offer practical support for IDC of STAs, we are considering methods:
  To specify the number of repetition counts associated with IDC activity
    For example, some applications require running a predefined number of periods for IDC
  To Announce the type and profile of IDC activity
    Type: P2P, Bluetooth, BLE, …
    Profile: Peer information for P2P, Role-specific information for STA’s IDC (e.g. Owner / Client), …
  This Information can be used for prioritization, further enhancement, and coordination from the AP side
Wi-Fi
IDC1
Add IDC1
(3 repetitions)
Remove IDC1 (without extra signals)

## Slide 7: Summary
From mobile device’s standpoint, discussions regarding IDC support have focused on addressing several key considerations:
  Indicating the addition, removal, suspension, resumption, and reconfiguration of IDC activities
  Defining the transmit or receive mode of the IDC operations
  Notifying reduction in Wi-Fi capabilities while operating IDC
  Specifying the number of repetitions for IDC activity
  Announcing the type and profile of IDC activity
Potential solutions for practical standardization should be further discussed:
  Reusing existing elements
  Introducing a new element dedicated to IDC support

## Slide 8: References
[1] 11-23/2002r2 In-device Coexistence and P2P – follow-up (Laurent Cariou, Intel)
[2] 11-23/1964r1 In-Device Coexistence (Alfred Asterjadhi, Qaulcomm)
[3] 11-24/0420r2 Enabling Flexible Coexistence Operation (Guogang Huang, Huawei)
[4] 11-24/0436r0 SP Based In-Device Coexistence (Yuchen Guo, Huawei)
[5] IEEE P802.11-REVme/D6.0, June 2024

## Slide 9: Straw Poll 1
Do you agree to define a mechanism for a STA to announce addition, deletion, suspension, resumption, and reconfiguration of its periodic unavailability?
  Which frame to use is TBD
  Optional / Mandatory is TBD

## Slide 10: Straw Poll 2
Do you agree to define a radio mode of IDC activities and Wi-Fi capabilities while engaging in the IDC periods?
  Mode of IDC activities: Tx-only IDC, Rx-only IDC, Both Tx & Rx IDC
  Wi-Fi Capabilities: the number of spatial streams (NSS), the operating bandwidth, and further capabilities TBD