## Slide 1: Considerations on ELR transmission
Date: 2024-07-xx
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
July. 2024

## Slide 2: Introduction
The ELR (i.e. enhanced long range) was proposed at the previous F2F meeting to solve link budget imbalance caused by the difference TX power between AP and non-AP STA.[1-3]
In this contribution, we investigate consideration points on ELR transmission concerning the impact of the legacy preamble.

## Slide 3: ELR transmission (1/2)
Based on presented contributions[1~3], we can consider several options for ELR transmission.
  The following transmission methods may be considered to achieve the minimum data rate proposed as 1.5Mbps or a slightly higher rate as well as the link budget gain.
    For the simple design and low complexity, existing RU and MCS are considered.
      Option 1 - Three times repetition of 52 tone RU
      Option 2 – Repetition of 106 tone RU with MCS 15
52 tone RU1
52 tone RU2
52 tone RU3
52 tone RU4
106 tone RU1 with MCS 15
106 tone RU2 with MCS15
Repeated RU

## Slide 4: ELR transmission (2/2)
  Also, as shown in [1], to support the coexistence with legacy STA, the ELR PPDU should include the legacy preamble.
    Example of ELR PPDU format in [1]
There have been a lot of discussions about the impact of the legacy preamble such as range imbalance, packet detection, etc., and we checked first whether the legacy preamble was a performance bottleneck in case the range extension gain from ELR transmission might not be fully guaranteed.
  Herein, RL-SIG, U-SIG repetition, and two options described in the previous slide are used to evaluate the ELR transmission.
Legacy Preamble
ELR Preamble
ELR Data

## Slide 5: Performance evaluation (1/2)
Simulation parameters.
  5GHz Band
  20MHz bandwidth
  1000 data bits
  SISO
  MCS0 with BCC
  Channel B NLoS and D NLoS
  Real Channel estimation with CFO and TO
  ELR transmission with 3 times repetition of 52 tone RU/ repetition of 106 tone RU with MCS 15
  3dB power boosting in L-STF and L-LTF
  RL-SIG and U-SIG repetition defined in ER preamble were considered.

## Slide 6: Performance evaluation (2/2)
The performance of L-SIG and U-SIG at 1% PER is worse than the performance of the data field at 10% PER.
  Therefore, we need to consider a similarly guaranteed link margin gain in the SIG field as well as an enhancement in the data field.
Note : The performance of L-SIG means the performance of combined L-SIG and RL-SIG,
The performance of U-SIG means the performance of repeated U-SIG as described in ER preamble.

## Slide 7: Considerations for ELR (1/2)
To supplement the performance gap due to the SIG field, the following method can be considered.
  Method 1: ELR transmission based on TB PPDU.
    To address the range imbalance between the SIG field and ELR data field, ELR transmission may be applied only to trigger-based UL transmission in UHR, so the SIG field may not have a significant impact on the range aspect.
      The 3dB power boosting can be applied to L-STF and L-LTF of TB PPDU for ELR
      In ELR transmission performed based on TF, the SIG field information of the ELR PPDU is already known to the AP, so SIG field performance may not be an obstacle from the AP reception aspect.
      In addition, the ELR transmission can be protected through the trigger frame transmitted by AP in an AP coverage.

## Slide 8: Considerations for ELR (2/2)
  Method 2 : New PPDU with enhanced performance of the SIG fields.
    The ELR PPDU can be designed to provide the improved range of the SIG field, just like a data field.
      As a simple way for that, the symbol repetition in time domain can be considered.
        For example, the L-SIG field in the ELR PPDU can be repeated more than 2 times to improve the performance.
          By applying more repetitions, we can achieve the enhanced range of the L-SIG field as shown in the appendix while it is insignificant to increase overhead in the ELR transmission.
      Though the repetition of the L-SIG symbol does not affect on the packet classification of legacy STA, to obtain the combined gain from this extension, this PPDU format should be detected before receiving the L-SIG field when this PPDU is received.
        For that, as described in [3], the packet detection of this PPDU may be performed by using the L-STF that needs further discussion.

## Slide 9: Summary
In this contribution, we evaluated the performance gap between the L-SIG and the data field designed for ELR when the legacy preamble is included in ELR PPDU.
  The performance of L-SIG(with RL-SIG) and U-SIG(w/ repetition) at 1% PER is worse than the performance of a data field for ELR at 10%.
To reduce the impact of the legacy preamble, we propose to consider following ways for ELR transmission.
  Option 1 : ELR transmission based on the TF
  Option 2 : Design of new ELR PPDU format to overcome the range imbalance on legacy SIG fields.

## Slide 10: Straw poll 1
Do you agree that ELR PPDU starts with a legacy preamble in the PPDU for the ELR transmission?
  The legacy preamble contains the L-STF, L-LTF, L-SIG, RL-SIG, and U-SIG.
  Yes
  No
  Abstain

## Slide 11: Straw poll 2
Which option do you prefer for ELR transmission to solve the range imbalance between the SIG field(e.g., L-SIG/U-SIG) and ELR data field of the transmission methods described on slides 7-8?
  Option 1: ELR transmission based on TB PPDU
  Option 2: Design of new ELR PPDU format with improvement of legacy preamble
  Option 3: Need more study.

## Slide 12: Straw poll 3
Do you agree to include the following text to the 11bn SFD?
  In ELR transmission, a method of transmitting a RU smaller than a 242-tone RU, with a repetition(s) in frequency domain within 20MHz, is used.
  The details are TBD
  Y
  N
  Abstain

## Slide 13: Straw poll 4
Which option do you prefer to obtain the link budget gain in ELR transmission?
  Option 1: Three times repetition of 52 tone RU
  Option 2: Repetition of 106 tone RU with MCS 15
  Option 3: Need more study.

## Slide 14: Appendix
The performance of L-SIG with 2 repetition

## Slide 15: Appendix – Packet classification
  HT-MM : LENGTH%3 == 0 + HT-SIG1 QBPSK + HT-SIG2 QBPSK
  VHT : LENGTH%3 == 0 + VHT-SIG1 BPSK + VHT-SIG2 QBPSK
  HE SU/MU : LENGTH%3 ~= 0 +RL-SIG + HE-SIGA1 BPSK + HE-SIGA2 BPSK
  HE ER SU : LENGTH%3 ~= 0 +RL-SIG + HE-SIGA1 BPSK + HE-SIGA2 QBPSK
  EHT MU PPDU : LENGTH%3 = 0 + RL-SIG + U-SIG1 BPSK+ U-SIG2 BPSK + PHY identifier field = 0

## Slide 16: Reference
[1] 11-24-0873-00 Design Targets and Considerations for Enhanced Long Range
[2] 11-24-0875-01 UHR Enhanced Long Range Support
[3] 11-24-0921-00 An Enhanced Long Range PPDU