## Slide 1: Selective Non-Primary Channel Access
Date: 2024-09-05
Authors:

## Slide 2: Introduction
Non-Primary Channel Access (NPCA) has been discussed in TGbn [1-14]
Some following other details are still under discussed and TBD
  Whether Non-Primary Channel (NPCH) can cover the outside of the operating bandwidth
  TXOP duration constraint in NPCA
  NAV management per sub-channels to enable NPCA
  Conditional NPCA configured by AP or non-AP STA [11, 13]
  EDCA parameter to be used during NPCA [14]
  OBSS PPDU format as a NPCA triggering condition [12,13

## Slide 3: Introduction
This contribution focuses on the further details on ‘AP configurable triggering condition’ introduced in [24/1115r1] regarding the triggering conditions under which the NPCA is performed
  A minimum length of OBSS PPDU, a minimum length of OBSS TXOP that triggers AP and STA to switch channel to NPCH and perform NPCA
  RSSS of the OBSS PPDU
  Format of OBSS PPDU
  Unavailability windows, where PCA will not be used due to Co-Ex issues or C-R-TWT
This contribution further suggests to perform NPCA for a set of non-AP STAs even though more non-AP STAs listen OBSS PPDU with satisfied conditions
  In addition, unavailability window is further revisited

## Slide 4: Motivation
Do all NPCA-enabled non-AP STAs have to switch channel and perform NPCA whenever OBSS PPDU/TXOP is detected (under the assumption that the associated AP can detect the same OBSS TXOP in the primary channel)?
  NPCA is opportunistic channel access way that utilizes the only limited time resource bounded by OBSS PPDU length or TXOP in the primary channel
  Time synchronization issues should also be addressed
Do AP and non-AP STAs need to switch channel to NPCH for every OBSS PPDU detection?
  Due to OBSS(s) operating in the non-primary channel (NPCH), AP/STA may not obtain TXOP after switching to the NPCH
  It may be useful if non-AP STA and AP are aware that the secondary channel has been occupied and is not enough to exchange frames in advance
    OBSS (R-)TWT SPs scheduled in secondary channel

## Slide 5: An example topology
OBSS AP
OBSS STA
AP
Group A
Group B
STA can perform NPCA
STA detecting both OBSS AP and STA
STA detecting only OBSS AP
STA detecting only OBSS STA
Divide NPCA-available STAs by a certain OBSS into several set of STAs
  During time window #1, Group A performs NPCA under the condition #1
    An example of the condition
  During time window #2, Group B performs NPCA under the condition 2
    An example of the condition is whether to have low latency traffic
    Group B non-STAs may be R-TWT member STAs with SP overlapped with time window #2
  During time window #3, All NPCA-available STAs do not perform NPCA
    AP announces to non-AP STAs a periodic channel occupation or R-TWT SP within time window #3
STA not detecting OBSS AP and any OBSS STA
STA cannot perform NPCA

## Slide 6: Example) Group-based NPCA
AP
STA Group A
STA Group B
beacon interval
OBSS
OBSS
OBSS
OBSS
NPCA
NPCA
NPCA
NPCA
OBSS
OBSS
OBSS
OBSS
OBSS
OBSS
OBSS
OBSS
NPCA
NPCA
NPCA
NPCA
STA Group A is allowed to perform NPCA
STA Group B is allowed to perform NPCA

## Slide 7: Example) Group-based NPCA
AP
STA Group A
STA Group B
OBSS
OBSS
OBSS
OBSS
NPCA
NPCA
NPCA
NPCA
OBSS
OBSS
OBSS
OBSS
OBSS
OBSS
OBSS
OBSS
NPCA
NPCA
NPCA
NPCA
STA Group A is allowed to perform NPCA
with NPCA configuration parameter set #1
STA Group B is allowed to perform NPCA
with EDCA parameter set #2 and NPCH BW #2
beacon interval
Optionally, AP and a group of non-AP STAs do perform NPCA with a customized NPCA configuration parameter set applied to the group. The examples of NPCA configuration parameters are EDCA parameter set, NPCH bandwidth, and etc.

## Slide 8: Example) Time period not performing NPCA
AP
STA Group A
STA Group B
OBSS
OBSS
OBSS
OBSS
NPCA
NPCA
OBSS
OBSS
OBSS
OBSS
OBSS
OBSS
OBSS
OBSS
NPCA
NPCA
STA Group A is allowed to perform NPCA
STA Group B is allowed to perform NPCA
AP and non-AP STAs do not perform NPCA during a certain time period (called NPCA-disabled time duration)
NPCH busy or OBSS R-TWT SPs in NPCH
NPCH busy or OBSS R-TWT SPs in NPCH
NPCH busy or OBSS R-TWT SPs in NPCH
NPCA-enabled time duration #1
NPCA-enabled time duration #2

## Slide 9: Example) NPCA Control element
A detailed information about non-AP STA group or a set of STAs to perform NPCA and availability/unavailability Windows [3] (same terminology as NPCA-enabled/disabled time duration in this contribution)
Following parameters may be considered to be included in NPCA-enabled STA Info field to specify the non-AP STAs to perform NPCA
  List of {AIDs and/or TIDs}
  Access category
  Low Latency traffic presence
The field “Unavailability Windows” can be extended to contain more than one NPCA-enabled/disabled time duration
NPCA Status | TBTT Count | NPCA Info field 1 | NPCA Info field 2
NPCA Configuration parameter set | NPCA Trigger Conditions
Unavailability Windows | Max. PPDU version | MAC Address List | BSS Color List | Max. PPDU Bandwidth | RSSI Threshold
Element ID
Length
Control
NPCA Control Element Information
NPCA-enabled STA info

## Slide 10: Conclusion
We suggest to define a method to allow only a subset of non-AP STAs that satisfy the condition configured by the associated AP to perform NPCA
  due to the limited time duration of a single NPCA event
We suggest to define a method to specify which time duration NPCA is allowed and which time duration NPCA is not allowed
  In some cases, it may be beneficial not to perform NPCA
    to protect OBSS R-TWT SP

## Slide 11: Straw poll 1
Do you agree to allow an NPCA AP to indicate some trigger conditions for performing the NPCA channel switch in the BSS.
  Yes
  No
  Abstain
[NOTE] This SP is the same as the SP2 in 11-24/1115-01-00bn

## Slide 12: Straw poll 2
Do you support to define in 11bn a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions?
  - TBD conditions can be specified and announced to non-AP STA by AP
  - As one of the TBD conditions specified by the AP, it can be time duration when the NPCA is allowed or not allowed
  - As one of the TBD conditions specified by the AP, it can be information to specify one or more than one non-AP STAs which allows to perform NPCA
  Yes
  No
  Abstain
  [NOTE] The SP text except for notes has been already passed in March F2F meeting

## Slide 13: Reference
  [1] 11-23/34, “Non-primary channel utilization,” Sindhu Verma, et. al.
  [2] 11-23/631, “Secondary channel usage and secondary 20MHz channel backoff,” Liwen Chu, et. al.
  [3] 11-23/797, “Non-primary channel access,” Yongho Seok, et. al.
  [4] 11-23/961, “UHR secondary channel access,” Minyoung Park, et. al.
  [5] 11-23/962, “UHR secondary channel access evaluation,” Dibakar Das, et. al.
  [6] 11-23/1112, “Thoughts on secondary channel access,” Insun Jang, et. al.
  [7] 11-23/1365, “Discussions on non-primary channel access,” Sanghyun Kim, et. al.
  [8] 11-23/1911, “Secondary channel access and frame transmission,” Dongju Cha, et. al.
  [9] 11-23/1951, “Concurrent CCA for non-primary channel access,” Leonardo Lanante, et. al.
  [10] 11-24/70, “Some Details about Non-Primary Channel Access,” Yunbo Li, et. al.
  [11] 11-24/427, “Enabling Non-Primary Channel Access,” Dongju Cha, et. al.
  [12] 11-495, “Non-Primary Channel Access (NPCA) – Follow up, Minyoung Park, et. al.
  [13] 11-24/1115, “Channel Switching Rules for NPCA,” Vishnu V. Ratnam, et. al.
  [14] 11-24/1218, “NPCA – Next level discussions,” Gaurang Naik, et. al.