## Slide 1: Scanning and discovery for AMP IoT
Date: 2024-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com
Chuanfeng He |  |  |  | 
Doc.: IEEE 802.11-24/1202r0
July 2024

## Slide 2: Abstract
This submission is to discuss scanning and discovery for AMP IoT.
Doc.: IEEE 802.11-24/1202r0

## Slide 3
Scanning and discovery
Weijie Xu (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1202r0
July 2024
  In legacy WiFi system, both passive scanning and active discovery are supported.
    In passive scanning mode, non-AP STA needs to scan the beacon sent by a AP to discover the network.
      The beacon is transmitted periodically.
      Non-AP STA may need to search many/all the channels to find a beacon.
    In active discovery, non-AP STA doesn’t have to scan the beacon but instead to send a probe request when it wants to transmit data. And the AP send a probe response to the STA.
      The probe request can be transmitted in one of the uplink channels.
  For AMP IoT, how to support discovery procedure? Shall both passive scanning and active discovery be supported?

## Slide 4
Passive scanning: without vs. with periodic beacon
Weijie Xu (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1202r0
July 2024
  In legacy WiFi system, beacon is used to indicate the presence of the AP and broadcast the essential network parameters such as BSSID, timestamp, beacon interval, data rate etc.
    Non-AP STA can be aware of the existence of the network after reading a beacon and can acquire its configuration information.
    The beacon is transmitted in a periodic manner.
  For AMP IoT, the information carried in a beacon channel is still useful. But, will a AMP beacon is used? Or Another channel is used?

## Slide 5
Passive scanning: necessity and feasibility of periodic beacon
Weijie Xu (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1202r0
July 2024
  In some use cases, there are a lot of AMP STA needs to be handled(e.g. sensor data collection or inventory). The whole commutation procedure will last for quite a long time or a while. Periodical beacon is needed, because,
    It is still the easiest and efficient way to use periodic beacon to convey system information to lots of AMP devices and also indicate the presence of the network.
    Periodic beacon can provide stable timing reference, which has been utilized for many other function (e.g. power saving/management mechanisms, paging function). It is expected similar power saving/management mechanisms is also needed for AMP.
    Periodic beacon has pre-known time locations of beacon, it is beneficial for device’s power saving.
  For AMP STA with RF ED receiver[1], the receiving bandwidth can be tens of MHz. Once a beacon channel fall within its wide receiving bandwidth, it can be detected by AMP STA without much scanning effort.

## Slide 6
Passive scanning: feasibility of AMP operation without beacon
Weijie Xu (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1202r0
July 2024
  In some other use cases, there is only peer-to-peer communication, e.g. close range communication or finding home belongings at home.
    The AP only needs to communicate with one AMP STA at a time.
      The AMP STA can be scheduled immediately when it harvests sufficient power and wakes up.
      There is no scheduling delay as for multiple device scheduling.
    There is no need to send periodic beacon. A trigger frame can be send to start the communication procedure between the AP and the AMP STA. And, the system configuration information (if any) can be carried in the trigger signaling.

## Slide 7
Active discovery
Weijie Xu (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1202r0
July 2024
  On the other hands, it can be considered whether active discovery can be used.
    In active discovery procedure, the AMP STA sends a probe request when it wants to communicate with the AMP AP.
      The probe request can be send in a predefined channel when there are multiple candidate physical channels.
      As discussed in[2], for AMP STA that is not able to transmit a legacy preamble, its uplink transmission shall be triggered by the AP thus it can be protected by the AP.
  Therefore, it is difficult to support active discovery for AMP IoT.

## Slide 8
Summary and proposals
  In this submission, scanning and discovery for AMP is discussed. The following is proposed:
      Support AMP operation with and without beacon.
Weijie Xu (OPPO)
Slide 8
Doc.: IEEE 802.11-24/1202r0
July 2024

## Slide 9: Reference
IEEE 802.11-24/0853r0 Design target and device capabilities for AMP IoT
IEEE 802.11-23/0827r0, AMP IoT Medium Access
Doc.: IEEE 802.11-24/1202r0
July 2024