## Slide 1: Preemption Session Setup
Date: 2024-06-18
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Ross Jian Yu |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 

## Slide 2: Introduction
Preemption has been discussed extensively in UHR and TGbn, aiming to achieve the low latency (LL) target [1-6].
Assuming STA1 is the TXOP holder, STA2 is the TXOP responder. There can be three types of preemption, depending on who is the preemptor.
Type 1: the preemptor is STA1
  Easiest type. STA1 can control the length of the PPDU that it transmits so that it can quickly transmit LL traffic after any of the PPDU carrying non-LL traffic within its TXOP.
  No SPEC change is needed.
Type 2: the preemptor is STA2
  Medium complexity. STA2 can indicate its preemption request in the acknowledgement frame
  STA1 needs to divide the long PPDU into shorter PPDUs to allow STA2 to put its preemption request in the acknowledgement frame in a timely manner
Type 3: the preemptor is STA3
  More complex. Different IFS for data and PR signal, STA1 can not determine who is STA3 after receiving the PR signal. Some follow up procedure is needed to determine STA3.

## Slide 3: Introduction
We focus on Type 2 in this contribution.
In order to support the potential preemption request from STA2, STA1 and STA2 need to setup a preemption session to determine the parameters, including:
  Which TIDs will be carried in short PPDUs
  What type of preemption request can be carried in the acknowledgement frame
Besides, the following aspects will be discussed:
  Indication of LL traffic in the acknowledgement frame
  Follow up transmission procedure of LL traffic

## Slide 4: Preemption Session Setup
Assuming the LL requirement is from the non-AP STA, in order to setup a preemption session, the non-AP STA needs to transmit a preemption setup request frame to the AP, and the AP will transmit a preemption setup response frame to the non-AP STA. If the setup procedure is successful, the AP will transmit short PPDUs to the non-AP STA when transmitting data of certain TIDs.
How to determine the “certain TIDs”?
Option 1: the non-AP STA will indicate the TIDs that belong to LL traffic, both in UL and DL, the other TIDs (that are not indicated as LL traffic) will be classified as those “certain TIDs”
  For the DL non-LL TIDs, AP will divide the DL PPDU into shorter PPDUs
  For the UL non-LL TIDs, the non-AP STA will divide the UL PPDU into shorter PPDUs, and the AP will set small values to the UL Length field of the basic trigger frame that solicits the UL PPDU
  The max length of the “short PPDUs” is also indicated in the preemption setup request frame

## Slide 5: Preemption Session Setup
Option 2: the non-AP STA will directly indicate those “certain TIDs”, both in UL and DL.
  Note-LL TIDs are determined using other methods, e.g., SCS, RTWT
Comparison:
  In option 1, there are only two types of TIDs. Type 1: LL TIDs; Type 2: the TIDs that will use shorter PPDUs to transmit.
  In option 2, there can be a third type of TID: the TID that does not belong to LL traffic, and will not be divided into shorter PPDUs to transmit. High throughput traffic is suitable to use this type of TID
  To summarize, option 1 is simpler, option 2 can support the third type of TID

## Slide 6: Preemption Session Setup
Another issue to address during the preemption session setup is: What type of preemption request can be carried in the acknowledgement frame
  Type 1: only allow to carry preemption request in the acknowledgement frame when the receiver of the preemption transmission is the TXOP holder
  Type 2: allow to carry preemption request in the acknowledgement frame when the receiver of the preemption transmission is either the TXOP holder or a third STA.
For UL TXOP, if type 2 is chosen, then AP can carry PR signal in the acknowledgement frame to transmit LL data to another STA
For DL TXOP, if type 2 is chosen, then the non-AP STA can carry PR signal in the acknowledgement frame to transmit LL data for P2P.
In general, the TXOP holder should decide which type to use. Hence,
  The preemption type for UL TXOP will be indicated by the non-AP STA in the request frame
  The preemption type for DL TXOP will be indicated by the AP in the response frame

## Slide 7: Indication of LL traffic in the acknowledgement frame
Although one bit in the acknowledgement frame to indicate the existence of PR request can already work, we think more detailed PR info (e.g., the required duration of the preemption transmission) can work better
In TGbn, we have the chance to put more info in the acknowledgement frame.
Besides the preemption scheme, in TGbn, many other proposals raise the requirement to put more information in the acknowledgement frame:
  the IDC scheme proposes to carry IDC info in the acknowledgement frame, e.g., availability duration, unavailability duration
We need to have a good design on the acknowledgement frame to accommodate different requirements
Since the compressed Block Ack frame does not have much room to carry the new information, we propose to use the Multi-STA Block Ack frame to carry
A special Per AID TID Info field can be defined to carry the LL traffic duration info

## Slide 8: Follow up transmission procedure of LL traffic
After receiving the preemption information in the acknowledge frame, the TXOP holder can transmit an MU-RTS TXS Trigger frame to the responder
  The allocation duration in the MU-RTS TXS frame should try to satisfy the requirement indicated in the preceding acknowledge frame
The responder can use the well defined scheme in TGbe to transmit LL data, and to return the TXOP to the TXOP holder, if needed.
AP
Non-AP STA
Data
MBA
MU-RTS
LL Data
BA
Indicates required duration for LL traffic
Allocation duration
CTS

## Slide 9: Conclusion
We consider the preemption type where only TXOP responder can send preemption request
A preemption session setup procedure is needed to determine the parameters to be used during the preemption session, including:
  Which TIDs will be divided into shorter PPDUs
  Allowed preemption type
We propose to use the Multi-STA Block Ack frame to carry more detailed preemption information, including the required duration for LL traffic
The TXOP holder can transmit a MU-RTS TXS trigger frame to let the TXOP responder transmit LL traffic.

## Slide 10: References
[1] 11-24-0103-01-00bn-txop-level-preemption-for-low-latency-application-in-802-11bn
[2] 11-24-0168-00-00bn-txop-preemption-in-11bn
[3] 11-24-0131-00-00bn-signaling-of-preemption
[4] 11-23-1886-03-00bn-preemption-techniques-to-meet-low-latency-ll-targets
[5] 11-24-0389-00-00bn-preemption-for-low-latency
[6] 11-24-0390-00-00bn-a-uniform-procedure-for-preemption