## Slide 1: 802.11 Feature Re-use
Date: 2024-07-12
Authors:

## Slide 2: Abstract
In this contribution, we discuss the re-use of existing IEEE802.11 design features for use in 802.11bp.

## Slide 3: Background
Harmonization of Waveform has been proposed to streamline the design of 802.11bp [1]
An additional approach is to leverage existing 802.11 features
One such re-use has already been proposed: the use of 802.11ba (WUR) for the downlink [2]
Further existing features could be considered

## Slide 4: 1Mb/s DSSS for Backscatter Uplink
After .11ba downlink sequence, a 1Mb/s DSSS frame is also transmitted. This frame is then backscattered by the AMP STA to provide the uplink
Advantages:
infrastructure participating in AMP re-use existing TX and RX blocks
non-AMP infrastructure (existing STAs) can be used for uplink RX
of all existing waveforms, 1Mb/s DSSS offers best link-budget and is constant envelope
infrastructure forms frame – AMP STA only changes bits on backscatter (low complexity, low power)
1Mb/s DSSS could also be used for active transmit
Use of DSSS for backscatter does NOT require DSSS beacons / preambles

## Slide 5: 802.11bc
802.11bc Enhanced Broadcast Service (EBCS) can be used on both up- and down-link [3]
Advantages:
avoids the need/overhead of association
security specific to .11bp can be used for protection
ease and flexibility of deployment
no beacons to clutter network
PHY agnostic
use EBCS with 11ba PHY

## Slide 6: HE / EHT mechanism for protecting non-infrastructure traffic
Adapt (R)TWT for AMP communication [4]
  can help reduce power consumption of AMP STA for low/periodic traffic
Adapt channel usage request/response to allocate medium for AMP communication [3,4]

## Slide 7: Conclusions
Many opportunities to leverage existing 802.11 features in building an 11bp amendment.
Leveraging existing 801.11 features:
eases implementation
provides better interoperability between 802.11bp devices and other 802.11 devices
provides flexibility in deploying 11bp networks with traditional 802.11 networks.
leverage 802.11 features that have been adopted and proven-out

## Slide 8: References
Yinan Qi et. al., “Harmonization of Waveform”, IEEE 802.11-24/0849r1, May 2024
Bin Qian et. al., “Initial Thoughts on 2.4 GHz Downlink AMP PPDU Design”, IEEE 802.11-24/0867r0, May 2024
REVme D6.0
P802.11be D6.0