## Slide 1: Coordinated BF Goodput Discussion
Date: 2024-07-03
Authors:
Name | Affiliations | Address | Phone | email
Genadiy Tsodik | Huawei |  |  | Genadiy.tsodik@huawei.com
Rani Keren |  |  |  | 
Shimi Shilo |  |  |  | 
Doron Ezri |  |  |  | 
Ezer Meltzer |  |  |  | 
Arik Klein |  |  |  | 
Oded Redlich |  |  |  | 

## Slide 2
Coordinated BF was accepted in 802.11be as one of the M-AP Cooperation schemes (was postponed to R2) and is considered now for 802.11bn as well
Several contributions discussed the principles of the CoBF scheme and introduced some analysis of PHY requirements and beamforming principles [1]-[4]
In [5] we showed the nulling principles and explained the changes that should be applied to a classical SVD based precoder to ensure zero MUI in case of CoBF
In this contribution we want to compare the CoBF scheme to regular DL MU-MIMO as well as CoSR, and study the potential gain of CoBF
Recap

## Slide 3
We ran the simulation with the following parameters:
  2 APs, 4 Tx Antennas each
  4 STA, 2 Rx Antennas (each AP is associated with 2 STAs)
  Operation schemes: CoBF, DL MU-MIMO
  20MHz BW, Channel D, practical CHEST
  Modulation: MCS3 – MCS8
  Nss in CoBF: 1SS per STA, Nss in DL MU-MIMO: 2SS per STA
  Sounding: Joint NDP (see next slide)
  Payload Size: 50KB, 200KB
CoBF vs MU-MIMO Simulation
AP1
AP2
STA1
STA2
STA3
STA4

## Slide 4
To calculate the overhead and provide the goodput results, we assume that CoBF scheme uses Joint NDP Sounding – APs jointly transmit NDP to STAs associated with specific AP
Thus the timeline assumed for goodput calculations of CoBF is as depicted below
CoBF Timeline Diagram
AP1
AP2
STA1
STA2
STA3
STA4
NDPA
NDP
NDP
BFR
BFR
CoBF Data
CoBF Data
MAP TF
CoBF Data
CoBF Data
BFRP
MAP
TF
NDPA
NDPA
NDP
BFRP
MAP
TF
NDP
NDPA
BFR
BFR
MAP TF

## Slide 5
The goodput results of CoBF and DL MU-MIMO are showed in the figure below
The gain of ~5-6dB of CoBF may be observed along all the SNR values – due to larger (effective) number of Tx antennas used in the CoBF scheme
Goodput Results

## Slide 6
We assume a very simple CoSR protocol with minimal information exchange between Sharing and Shared AP – the only indication is the power requirements provided by the Sharing AP when CoSR is triggered
This assumption implies the following principles:
  Only Shared (OBSS) AP is mandated to control its power according to Sharing AP indication
  Interference is not synchronized (OBSS packet start is random in simulation - up to half of the PPDU duration)
  For simplicity, symmetry is assumed – same SIR at BSS and OBSS receiver
  We assume that each STA measures the signal RSSI from OBSS AP and reports it to its AP, so APs can carry out a better selection of STAs that participate in CoSR transmission
Comparison to CoSR

## Slide 7
We ran the simulation with the following parameters:
  2 APs, 2 Tx Antennas each
  2 STA, 2 Rx Antennas (each AP is associated with 1 STA)
  Operation schemes: CoBF, CoSR
  20MHz BW, Channel D, practical CHEST
  Modulation: MCS3 – MCS8
  CoBF: 1SS per STA, CoSR: 1 or 2 SS per STA
  CoBF Sounding: Joint NDP - same overhead as in previous comparison
  Payload Size: 200KB
CoBF vs CoSR Simulation
AP1
AP2
STA1
STA2

## Slide 8
The goodput results of CoBF and CoSR with 1SS per STA are showed in the figure below
When noise is dominant similar goodput is observed for CoBF and CoSR, whereas when interference is dominant CoBF achieves a higher goodput
Goodput Results – 1SS per STA

## Slide 9
The goodput results of CoBF and CoSR are showed in the figure below
  We compare to CoBF with 1SS per STA because CoBF is DoF limited (due to MUI nulling)
When SNR and SIR are high CoSR achieves higher goodput due to larger number of spatial streams, whereas at low SNR values CoBF shows better performance
Goodput Results – 2SS per STA in CoSR

## Slide 10
CoBF provides a clear & constant gain over MU-MIMO, mostly due to array gain
Both CoBF and CoSR are valid schemes with clear benefits, for which the results depend on transmission parameters and channel conditions:
  CoBF significantly outperforms CoSR when the same number of spatial streams is used in both schemes (for all SNR and SIR values)
  In specific scenarios (higher value of Nss, high SNR and SIR) CoSR yields higher goodput
We may consider both CoSR and CoBF as candidate MAP schemes; the relevant scheme may be selected for operation based on channel conditions
Conclusions

## Slide 11
Do you agree to add the following text to the TGbn SFD:
  TGbn shall define TXOP based Coordinated Spatial Reuse (CSR) and Coordinated Beamforming (CBF), which allow one AP to initiate concurrent transmissions of at least two PPDUs from at least two BSSes on the same channel within its TXOP.
    Y
    N
    A
Straw Poll #1

## Slide 12
References
[1] 11-24-0011-00-00bn-coordinated-spatial-nulling-c-sn-concept
[2] 11-24-0012-00-00bn-coordinated-spatial-nulling-c-sn-simulations
[3] 11-24-0009-01-00bn-coordinated-beamforming-coordinated-beamforming-for-802-11bn
[4] 11-23-0776-01-0uhr-performance-of-c-bf-and-c-sr
[5] 11-23-1998-00-00bn-zero-mui-coordinated-bf