## Slide 1
Feasibility study on long range backscatter operation
Date: 2024-07-15
Authors:
Name | Affiliations | Address | Phone | Email
Wei Lin | Huawei | Huawei, Shenzhen, China |  | lin.linwei@huawei.com
Lei Huang |  | Huawei, Singapore |  | 
Bin Qian |  | Huawei, Shenzhen, China |  | 
Panpan Li |  | Huawei, Singapore |  | 
Rojan Chitrakar |  | Huawei, Singapore |  | 
Shuqiao Chen |  | Huawei, Singapore |  | 
David Xun Yang |  | Huawei, Shenzhen, China |  | 

## Slide 2: Recap of Close Range & Long Range Backscatters
There are two different backscatter use cases have been discussed in AMP [1-4]
  Close range backscatter
    Mono-static: the Carrier Source and AP are integrated
    Wi-Fi transceiver has 2+ antennas to support full-duplex operation
    Coverage: 10 cm - 20 cm
  Long range backscatter
    Bi-static: the Carrier Source and AP are separated, which results in half duplex operation
    Coverage: several meters
Close range backscatter [4]
Long range backscatter
Leakage signal

## Slide 3: Close Range & Long Range Backscatters
According to the SP results during last IEEE meeting, it seems that the group in favor of the use case of close range backscatter operation [7]
  The feasibility of close range backscatter operation have been extensively investigated in [1-4]
Ref [1] [5] have addressed long range backscatters, but further investigations are required to clarify the feasibility for medium/long range backscatters at 2.4GHz frequency.
  In this contribution, we investigate the feasibility for backscatter operation of around 10~15m coverage
  Considered Use Case: Long range backscatter with separated Carrier Source and AP

## Slide 4: Link Budget for Long Range Backscatters
The link budget computations were extensively discussed in [3-6]
  To evaluate the feasibility of long range backscatter, we further investigate the link budgets of Bi-Static long range backscatter with separated Carrier Source and AP
  The AMP Tag in this case should have some power storage or WPT capabilities  better sensitivity
  Both Friis equation and 11n defined channel models (2.4GHz) are evaluated
Long range backscatter
Friis equation
11n channel model

## Slide 5: Downlink Link Budget for Long Range Backscatters
Downlink link budget computations of Bi-Static long range backscatters
  The Tx/Rx signal isolation is greatly alleviated with separated Carrier Source and AP
 | Bi-Static long range backscatter | 
Antenna gain of AMP Tag (dBi) | 2 | 
Minimum receiving power for AMP Tag (dBm) | -45 | 
Frequency | 2.4 GHz | 
EIRP of AP (dBm) | 27 | 20
Max. commun. distance from AP to AMP Tag (m) (Friis) | 49.85 | 22.27
Max. commun. distance from AP to AMP Tag (m) (11n Channel D) | 17.8 | 11.32
Pr = Pt + Gt + Gr + 20log10(λ) – 20log10(4πd) (with Friis Equation)

## Slide 6: Uplink Link Budget for Long Range Backscatters
Uplink link budget computations of Bi-Static long range backscatters at 2.4GHz Frequency
  The Tx/Rx signal isolation is greatly alleviated with separated Carrier Source and AP
Pr = Pt + Gt + Gr + 20log10(λ) – 20log10(4πd) (with Friis Equation)
 | Carrier Source to AMP Tag | 
EIRP of Carrier Source (dBm) | 27 | 20
Antenna gains of AMP Tag (dBi) | 2 | 
Minimum receiving power for AMP Tag (dBm) | -20 | 
Max. commun. distance from Carrier Source to AMP Tag (m) (Friis) | 2.80 | 1.25
Max. commun. distance from Carrier Source to AMP Tag (m) (11n Channel D) | 2 | 0.88
 | AMP Tag to AMP Reader | 
Receiver sensitivity of AP (dBm) | -95 | 
Maximum transmission power of AMP Tag (dBm) | -20 | 
Backscattering loss at AMP Tag (dB) | 5 | 
Max. commun. distance from AMP Tag to AP (m) (Friis) | 49.85 | 
Max. commun. distance from AMP Tag to AP (m) (11n Channel D) | 17.94 | 

## Slide 7: Uplink Link Budget for Long Range Backscatters
Uplink link budget computations of Bi-Static long range backscatters at 2.4GHz Frequency
  The Tx/Rx signal isolation is greatly alleviated with separated Carrier Source and AP
Pr = Pt + Gt + Gr + 20log10(λ) – 20log10(4πd) (with Friis Equation)
 | Carrier Source to AMP Tag | 
EIRP of Carrier Source (dBm) | 27 | 20
Antenna gains of AMP Tag (dBi) | 2 | 
Minimum receiving power for AMP Tag (dBm) | -25 | 
Max. commun. distance from Carrier Source to AMP Tag (m) (Friis) | 4.98 | 2.22
Max. commun. distance from Carrier Source to AMP Tag (m) (11n Channel D) | 3.50 | 1.56
 | AMP Tag to AMP Reader | 
Receiver sensitivity of AP (dBm) | -95 | 
Maximum transmission power of AMP Tag (dBm) | -25 | 
Backscattering loss at AMP Tag (dB) | 5 | 
Max. commun. distance from AMP Tag to AP (m) (Friis) | 28.03 | 
Max. commun. distance from AMP Tag to AP (m) (11n Channel D) | 12.91 | 

## Slide 8: Summary
In this contribution, we investigated the feasibility for long range backscatter operation of around 10~15m coverage
  Considered Use Case: Long range backscatter with separated Carrier Source and AP
According to the downlink / uplink link budget evaluations, it is feasible for long range backscatter operations of around 10~15m coverage

## Slide 9
Thank You

## Slide 10: Straw Poll
Do you support that 11bp defines at least one mode of MAC/PHY that supports long-range backscattering communication in 2.4 GHz as shown below

## Slide 11: References
[1] 11-24-0853-00-00bp-design-target-and-device-capabilities-for-amp-iot
[2] 11-24-0867-00-00bp-thoughts-and-questions-on-amp-phy
[3] 11-23-2038-01-0amp-close-range-amp-backscattering-in-2-4ghz
[4] 11-24-0798-01-00bp-close-range-amp-wifi-reader-feasibility-study-followup
[5] 11-24-0075-00-0amp-follow-up-on-amp-link-budgets
[6] 11-22-1562-08-0amp-draft-technical-report-on-support-of-amp-iot-devices-in-wlan
[7] 11-24-0953-00-00bp-2024-05-interim-meeting-minutes