## Slide 1: A Framework for Coordinated Access Points
Date: 2024-08-19
Authors:

## Slide 2: Introduction
Coordinated APs (C-AP) features are discussed for 11bn to improve latency and throughput and include coordinated spatial reuse (C-SR), coordinated beamforming (C-BF), coordinated rTWT (C-rTWT), coordinated TDMA (C-TDMA), etc.
This presentation discusses a general framework for Coordinated APs:
  C-AP general framework
    Capability advertisement
    Per-feature negotiations
    Container for C-AP information
  Examples: negotiations and frame exchanges for some C-AP features

## Slide 3: General framework
Consider the set of C-AP features in 11bn (e.g., C-SR, C-BF, CrTWT, C-TDMA)
Phase 1 (Advertisement): A lightweight advertisement of capabilities for the set of supported C-AP features in 11bn
  No session/agreement establishment at this level (only advertisement)
  An AP can transmit this frame at will, eventually updating capabilities/parameters for C-AP features
  Management frames are used
Phase 2 (Feature-specific negotiations): When a neighboring AP(s) with capability of a desired C-AP feature is discovered (e.g., after receiving the advertisement of Phase 1), negotiations can be carried out to establish a feature-specific agreement or update its parameters.
  Agreement is feature-specific (e.g., CrTWT/CTDMA/CBF/CSR agreement)
  Agreement (and associated messaging) is between a pair of APs
    Individually addressed Management frames are used
  Can include negotiation steps
    Negotiations can be optional/mandatory based on the specific C-AP feature
    If performed, at least agree on the intention to participate in the feature (request/accept/reject)
    If performed, may additionally agree on feature-specific parameters (via dedicated elements/subelements)
Phase 3 (Feature-specific frame exchange)
  May or may not include more inter-AP communications depending on the feature
    E.g., for C-TDMA/C-BF/C-SR inter-AP frames specific to the feature may be exchanged for the operation (e.g., during a TXOP)
    E.g., for CrTWT, no inter-APs frame exchange during the operation
AP BSS1
AP BSS2
Phase 1: capability exchange (management frames)
Phase 2: Feature-specific negotiation (inter-AP individually addressed management frames)
Phase 3: Feature-specific frame exchange

## Slide 4: Example: CrTWT Negotiation and Frame Exchange
Reuse the structure of 11be rTWT (based on B-TWT agreements)
Phase 2 (Negotiation): Individually addressed management frames to negotiate a CrTWT agreement
  Negotiation is optional and can start after an AP discovers another capable AP
  Negotiation includes at least a request message containing the schedule to be protected and a response accept/reject
  The reference to the CrTWT agreement is the tuple {CrTWT ID, Requesting AP’s MAC ID}
    Note: in 11be rTWT an agreement is referred to via the tuple {B-TWT ID, Scheduling AP’s MAC ID}
Phase 3 (Utilization): APs engaging in CrTWT perform the following:
  Owner AP: rTWT Information element with Broadcast TWT information with Broadcast TWT ID
    If the AP carries out negotiations with other APs, it should consistently use the B-TWT ID used for broadcasting the rTWT schedule in its own BSS as the value for the CrTWT ID used to obtain the agreement with the OBSS AP
  Non-owner AP: rTWT Information element with Broadcast TWT information with Broadcast TWT ID = 31 and Restricted TWT Schedule Information subfield set to 3
    Note: can be used to signal to the non-owner AP’s clients that it is an OBSS rTWT schedule
    Note: this is possible even if there is no formal CrTWT agreement between the APs

## Slide 5: Example: CrTWT Negotiation and Frame Exchange
C-AP Advertisement
C-AP Advertisement
CrTWT Request
CrTWT Response
rTWT Announcement over beacon (as in 11be rTWT)
(OBSS) rTWT Announcement over beacon (e.g., as in 11be rTWT, with B-TWT ID = 31)
CrTWT Request
CrTWT Response
Phase 1
Phase 2
Phase 3
Phase 2’
STA BSS1
AP BSS1
AP BSS2
STA BSS2
e.g., Accept agreement for the schedule in the Request frame
e.g., update SP parameters for CrTWT ID*
e.g., for a new agreement with CrTWT ID*
e.g., Reject the new parameters and tear down the agreement
B-TWT ID = CrTWT ID*

## Slide 6: Example: C-TDMA Negotiation and Frame Exchange
Phase 2 (Negotiation): Individually addressed management frames to negotiate a C-TDMA agreement
  Negotiation can start after an AP discovers another capable AP
  Negotiation (if performed) includes at least a request message and an accept/reject message to establish the intention of sharing the TXOP
    Other parameters characterizing the traffic for which the TXOPs can be shared can also be negotiated
Phase 3 (Utilization): APs can exchange frames at the TXOP granularity

## Slide 7: Example: C-TDMA Negotiation and Frame Exchange
C-AP Advertisement
C-AP Advertisement
C-TDMA Request
C-TDMA Response
TXOP level frame exchange
Phase 1
Phase 2
Phase 3
Phase 2’
AP BSS1
AP BSS2
e.g., Accept agreement for the TXOP sharing
e.g., update parameters
e.g., for a new agreement between the 2 APs
e.g., Reject the new parameters and tear down the agreement
C-TDMA Request
C-TDMA Response

## Slide 8: Containers for C-AP Information
New Public Action frames can be used
  Appealing because they can be sent in unassociated state (clause 11.3.3)
New Action frames could be used (e.g., “C-AP Action”)
  They would require exception to be transmitted in unassociated state
Beacon could be used
  Need to be mindful of Beacon bloating
For Negotiations (Phase 2) the Management frames should be individually addressed (pair-wise agreements)
MAC Header
Category
Action
Frame contents
Defines the category of the Action frame
Set according to Table 9-81
Category is set to 4 (Public)
Action Frame format in 11be
Defines specific action of the Action frame
Set according to rules in Section 9.6
If Category is set to 4, this is the “Public Action field”. New values for the Action would be defined from reserved values, e.g.:
  55: C-AP Advertisement
  56: C-AP Request
  57: C-AP Response
  58: C-AP Notification
  Etc.
Example: New Public Action frames

## Slide 9: Conclusion
A framework for C-AP features is discussed including:
  Advertising C-AP features capabilities
  Negotiating engagement and parameters
  Utilization of the C-AP feature
APs can advertise capabilities for C-AP features over management frames
APs can start negotiations for specific/individual C-AP features via individually addressed management frames
Notes: APs coordination can have essentially the following phases:
  Advertisement/Discovery (capabilities and enablement)

## Slide 10: SP1
Do you support that an AP supporting Coordinated AP (C-AP) features shall be able to discover a neighbor AP that indicates support of C-AP features and may initiate a negotiation(s) for coordination with the neighbor AP?

## Slide 11: SP2
Do you agree that APs that intend to participate in C-AP feature(s) can use management frames to advertise/discover the capability and/or parameters of individual C-AP features

## Slide 12: SP3
Do you agree that APs that discovered each other and want to establish an agreement for a specific C-AP feature, can use individually addressed management frames to establish the agreement and negotiate parameters
Note: The management frame can be a Public Action and/or new Action frames

## Slide 13: Thank You