## Slide 1: A Framework for Coordinated Access Points
Date: 2024-08-19
Authors:

## Slide 2: Introduction
Multi-AP Coordination (MAPC) features are discussed for 11bn to improve latency and throughput and include coordinated spatial reuse (C-SR), coordinated beamforming (C-BF), coordinated rTWT (C-rTWT), coordinated TDMA (C-TDMA), etc.
This presentation discusses a general framework for Coordinated APs:
  MAPC general framework
    Capability advertisement
    Per-feature negotiations
    Container for MAPC information
  Examples: negotiations and frame exchanges for some MAPC features
  Signaling
  Security

## Slide 3: General framework
Consider the set of MAPC features in 11bn (e.g., C-SR, C-BF, CrTWT, C-TDMA)
Phase 1 (Discovery): A lightweight advertisement of capabilities for the set of supported MAPC features in 11bn
  No session/agreement establishment at this level (only advertisement)
  An AP can transmit this frame at will, eventually updating capabilities/parameters for MAPC features
  Management frames are used
Phase 2 (Feature-specific negotiations): When a neighboring AP(s) with capability of a desired MAPC feature is discovered (e.g., after receiving the advertisement of Phase 1), negotiations can be carried out to establish a feature-specific agreement or update its parameters.
  Agreement is feature-specific (e.g., CrTWT/CTDMA/CBF/CSR agreement)
  Agreement (and associated messaging) is between a pair of APs
    Individually addressed Management frames are used
  Can include negotiation steps
    Negotiations can be optional/mandatory based on the specific MAPC feature
    If performed, at least agree on the intention to participate in the feature (request/accept/reject)
    If performed, may additionally agree on feature-specific parameters (via dedicated elements/subelements)
Phase 3 (Feature-specific frame exchange)
  May or may not include more inter-AP communications depending on the feature
    E.g., for C-TDMA/C-BF/C-SR inter-AP frames specific to the feature may be exchanged for the operation (e.g., during a TXOP)
    E.g., for CrTWT, no inter-APs frame exchange during the operation
AP BSS1
AP BSS2
Phase 1: capability exchange (management frames)
Phase 2: Feature-specific negotiation (inter-AP individually addressed management frames)
Phase 3: Feature-specific frame exchange

## Slide 4: Example: CrTWT Negotiation and Frame Exchange
Reuse the structure of 11be rTWT (based on B-TWT agreements)
Phase 2 (Negotiation): Individually addressed management frames to negotiate a CrTWT agreement
  Negotiation is optional and can start after an AP discovers another capable AP
  Negotiation includes at least a request message containing the schedule to be protected and a response accept/reject
  The reference to the CrTWT agreement is the tuple {CrTWT ID, Requesting AP’s MAC ID}
    Note: in 11be rTWT an agreement is referred to via the tuple {B-TWT ID, Scheduling AP’s MAC ID}
Phase 3 (Utilization): APs engaging in CrTWT perform the following:
  Owner AP: rTWT Information element with Broadcast TWT information with Broadcast TWT ID
    If the AP carries out negotiations with other APs, it should consistently use the B-TWT ID used for broadcasting the rTWT schedule in its own BSS as the value for the CrTWT ID used to obtain the agreement with the OBSS AP
  Non-owner AP: rTWT Information element with Broadcast TWT information with Broadcast TWT ID = 31 and Restricted TWT Schedule Information subfield set to 3
    Note: can be used to signal to the non-owner AP’s clients that it is an OBSS rTWT schedule
    Note: this is possible even if there is no formal CrTWT agreement between the APs

## Slide 5: Example: CrTWT Negotiation and Frame Exchange
MAPC Discovery
MAPC Discovery
CrTWT Request
CrTWT Response
rTWT Announcement over beacon (as in 11be rTWT)
(OBSS) rTWT Announcement over beacon (e.g., as in 11be rTWT, with B-TWT ID = 31)
CrTWT Request
CrTWT Response
Phase 1
Phase 2
Phase 3
Phase 2’
STA BSS1
AP BSS1
AP BSS2
STA BSS2
e.g., Accept agreement for the schedule in the Request frame
e.g., update SP parameters for CrTWT ID*
e.g., for a new agreement with CrTWT ID*
e.g., Reject the new parameters and tear down the agreement
B-TWT ID = CrTWT ID*

## Slide 6: Example: C-TDMA Negotiation and Frame Exchange
Phase 2 (Negotiation): Individually addressed management frames to negotiate a C-TDMA agreement
  Negotiation can start after an AP discovers another capable AP
  Negotiation (if performed) includes at least a request message and an accept/reject message to establish the intention of sharing the TXOP
    Other parameters characterizing the traffic for which the TXOPs can be shared can also be negotiated
Phase 3 (Utilization): APs can exchange frames at the TXOP granularity

## Slide 7: Example: C-TDMA Negotiation and Frame Exchange
MAPC Discovery
MAPC Discovery
C-TDMA Request
C-TDMA Response
TXOP level frame exchange
Phase 1
Phase 2
Phase 3
Phase 2’
AP BSS1
AP BSS2
e.g., Accept agreement for the TXOP sharing
e.g., update parameters
e.g., for a new agreement between the 2 APs
e.g., Reject the new parameters and tear down the agreement
C-TDMA Request
C-TDMA Response

## Slide 8: MAPC frames
New Public Action frames can be used
  Appealing because they can be sent in unassociated state (clause 11.3.3)
  A new set of actions would be defined (see figure)
  For Negotiations (Phase 2) the Management frames should be individually addressed (pair-wise agreements)
MAC Header
Category
Action
Frame contents
Defines the category of the Action frame
Set according to Table 9-81
Category is set to 4 (Public)
Action Frame format in 11be
Defines specific action of the Action frame
Set according to rules in Section 9.6
If Category is set to 4, this is the “Public Action field”. New values for the Action would be defined from reserved values, e.g.:
  55: MAPC Advertisement
  56: MAPC Negotiation Request
  57: MAPC Negotiation Response
  Etc.
MAPC Public Action frames

## Slide 9: MAPC Discovery
In the broadcast discovery frame, at least the following can be considered:
One bit for capability/enablement of each feature
  This provides information about what MAPC features an AP supports (features that might be leveraged with or without negotiations depending on the deployment)
  Could indicate the presence of other reported feature-specific parameters
One bit to allow/disallow negotiations
  Being saturated with negotiation agreements
  In case malicious devices are flooding with negotiation requests

## Slide 10: MAPC Negotiation exchange (I)
A MAPC Negotiation can be a 2 frames exchange between a requesting AP and a responding AP
The request frame should carry information for one or more negotiation categories (i.e., Co-RTWT, Co-TDMA, Co-BF, Co-SR)
The response frame should carry the corresponding information from the responder side, including at least responses (e.g., status codes) for each request
Note: AP ID assignment could be considered as one of the negotiations categories alongside Co-RTWT, Co-TDMA, Co-BF, Co-SR
AP1 to AP2
AP2 to AP1
Co-RTWT Info
Co-TDMA Info
Co-SR Info
Co-RTWT Info
Co-TDMA Info
Co-SR Info
…
Co-RTWT Info
Co-BF Info
Co-BF Info
Co-RTWT Info
MAPC Negotiation Resp. frame
MAPC Negotiation Req. frame
MAPC Negotiation Resp. frame
MAPC Negotiation Req. frame

## Slide 11: MAPC Negotiation exchange (II)
An AP1 may send a MAPC Negotiation request to another AP2 only if it received a MAPC Advertisement with the Negotiations allowed bit set to 1.
  Note: should add request for features for which AP2 signaled that is capable of/has enabled
An AP2 that receives a MAPC Negotiation request shall respond with a MAPC response.

## Slide 12: MAPC element
A new element for MAPC should be defined.
The element should be able to carry information about the different per-feature negotiations
There may be several options for how to include the per-negotiation category information, and those can be discussed going forward.
Negotiation categories are: Co-RTWT, Co-TDMA, Co-BF, Co-SR, TBD – AP ID assignment
AP1 to AP2
Co-RTWT Info
Co-TDMA Info
Co-SR Info
Co-RTWT Info
Co-TDMA Info
Co-SR Info
MAPC Negotiation Resp. frame
MAPC Negotiation Req. frame

## Slide 13: Security
MAPC negotiations with individually addressed Management frames should be encrypted.
MAPC should consider reusing baseline procedures such as PASN (with extensions if needed) for pairwise encryption key.
Group key derivation needs to be discussed.
Secure delivery of group keys using pairwise key can be considered.
The optionality of using MAPC security needs to be discussed.

## Slide 14: Conclusion
A framework for MAPC features is discussed including:
  Discovering MAPC features capabilities
  Negotiating engagement (for schemes) and parameters
  Utilization of the MAPC feature
Signaling is discussed based on:
  Public action Management frames (new actions for MAPC)
  New MAPC element
Security based on PASN

## Slide 15: SP1
Do you support that an AP supporting Coordinated AP (MAPC) features shall be able to discover a neighbor AP that indicates support of MAPC features and may initiate a negotiation(s) for coordination with the neighbor AP?

## Slide 16: SP2
Do you agree that APs that intend to participate in MAPC feature(s) can use management frames to advertise/discover the capability and/or parameters of individual MAPC features

## Slide 17: SP3
Do you agree that APs that discovered each other and want to establish an agreement for a specific MAPC feature, can use individually addressed management frames to establish the agreement and negotiate parameters
Note: The management frame can be a Public Action and/or new Action frames

## Slide 18: SPa1 (MAPC Public action frame actions)
Do you support to define new actions for Public Action frames for MAPC communications such as discovery and negotiations?
A new action is defined for MAPC Discovery
An action is defined for MAPC Negotiation Request
An action is defined for MAPC Negotiation Response
Others are TBD

## Slide 19: SPa2 (M-AP coordination discovery)
Do you support that when an AP use Management frames to discover the capabilities and/or parameters of individual M-AP coordination schemes, the AP shall use the defined MAPC Public Action frame with the following setting:
The action field is set to MAPC Discovery

## Slide 20: SPa3 (M-AP coordination negotiations - Request)
Do you support that, when an AP (AP1) uses an individually addressed Management frame to initiate a negotiation to establish agreements for M-AP coordination schemes (if enabled by another AP (AP2)), the AP (AP1) shall use the defined MAPC Public Action frame with the following setting:
  The action field is set to MAPC Negotiation Request
If new negotiations are disabled by another AP (AP2) the AP (AP1) shall not send a negotiation request the other AP (AP2)
  TBD details of ‘new negotiations disabled’

## Slide 21: SPa4 (M-AP coordination negotiations - Response)
Do you agree that when an AP (AP2) receives an individually addressed Management frame that initiates a negotiation to establish agreements for M-AP coordination schemes, the AP (AP2) shall respond by using the defined MAPC Public Action frame with the following setting, if the negotiation is not disabled:
  The action field is set to MAPC Negotiation Response

## Slide 22: SPc1 (Co-RTWT Parameters Set)
A Co-RTWT Requesting AP, shall include one or more Co-RTWT Parameter Set fields corresponding to each requested R-TWT schedule in the TBD individually addressed management frame used for the request to the Co-RTWT Responding AP. The Co-RTWT Parameter Set field includes the following:
Target Wake Time field
Broadcast TWT ID field
Broadcast TWT Persistence
TWT Wake Interval Mantissa
TWT Wake Interval Exponent
Nominal Minimum TWT Wake Duration
TBD other fields

## Slide 23: Thank You