## Slide 1: Pilot Tone Design in dRU Transmission
Date: 2024-07
Authors:
Name | Affiliations | Address | Phone | email
Lin Yang | Qualcomm |  |  | 
Qifan Chen |  |  |  | 
Bin Tian |  |  |  | 
Youhan |  |  |  | 

## Slide 2: Introduction
We have shared our thoughts on dRU pilots design methodology and principle in [1], in which hierarchical pilot structure for dRU was proposed to ensure pilot locations to be optimized globally and systematically
  dRU26’s pilot tones are the base set for lager dRU’s pilots
  Evenly distributed over entire distribution BW
  Within each dRU, large pilot separation ensures frequency diversity
  Across different RUs, guarantee of enough separation of pilots for any combination of dRU
In this contribution, we will discuss the detailed dRU pilots design based on these ideas

## Slide 3: How to Choose the Pilot Locations?
Across the distribution BW
  Uniform pilot tone index spacing with maximal possible separation
    Ensure enough separation of pilots for any combination of dRU
    Maximal uniform separation for pilots is 11 tones for all 20/40/80MHz distribution
      No pilots around DC tones or edge tones of each dRU
Within each dRU
  Pilots’ separation is critical for small dRU to ensure diversity
    Especially for dRU26 which only has 2 pilots across the distribution BW for phase tracking
  Pilot tone separation pattern is important for large dRUs
    Large dRU has less power boosting gain but can potentially harvest more gain from channel smoothing
    Fixed pilot pattern may simplify smoothing filter design

## Slide 4: Pilot Tone Design for 20/40/80MHz dRUs
The following detailed dRU pilot design assumed dRU tone plan in [2], which offers the following good properties aligning with pilot design
  Hierarchical structure
  Uniform or near-uniform tone distribution to ease channel smoothing and achieve better smoothing gains

## Slide 5: Pilots for 20MHz dRU
Hierarchical uniform pilot structure of distance of 11
[-111 -100 -89 -78 -67 -56 -45 -34 -23 15 26 37 48 59 70 81 92 103]
Fixed pilot tone separation patterns for all dRUs in 20MHz
Pilot indices for dRU transmission over 20MHz | 
dRU size | KdRxx_i
dRU26, i = 1:9 | {-111 15}, {-89 37}, {-100 26}, {-78 48}, {-67 59}, {-56 70}, {-34 92}, {-45 81}, {-23 103}
dRU52, i = 1:4 | {-111 -89 15 37}, {-100 -78 26 48}, {-56 -34 70 92}, {-45 -23 81 103}
dRU106, i = 1:2 | {-111 -78 15 48}, {-56 -23 70 103}

## Slide 6: Pilots for 40MHz dRU
Hierarchical uniform pilot structure of distance of 11
[-224 -213 -202 -191 -180 -169 -158 -147 -136 -125 -114 -103 -92 -81 -70 -59 -48 -37 28 39 50 61 72 83 94 105 116 127 138 149 160 171 182 193 204 215]
Fixed pilot tone separation patterns for all dRUs in 40MHz
Pilot indices for dRU transmission over 40MHz | 
dRU size | KdRxx_i
dRU26, i = 1:18 | {-224 28}, {-125 127}, {-202 50}, {-103 149}, {-81 171}, {-114 138}, {-213 39}, {-92 160}, {-191 61}, {-169 83}, {-70 182}, {-147 105}, {-48 204}, {-180 72}, {-59 193}, {-158 94}, {-37 215}, {-136 116}
dRU52, i = 1:8 | {-224 -125 28 127}, {-202 -103 50 149}, {-213 -114 39 138}, {-191 -92 61 160}, {-169 -70 83 182}, {-147 -48 105 204}, {-158 -59 94 193}, {-136 -37 116 215}
dRU106, i = 1:4 | {-224 -103 28 149}, {-213 -92 39 160}, {-169 -48 83 204}, {-158 -37 94 215}
dRU242, i = 1:2 | {-224 -213 -103 -92 28 39 149 160}, {-169 -158 -48 -37 83 94 204 215}

## Slide 7: Pilots for 80MHz dRU
Hierarchical uniform pilot structure of distance of 11
[-447 -436 -425 -414 -403 -392 -381 -370 -359 -348 -337 -326 -315 -304 -293 -282 -271 -260 -249 -238 -227 -216 -205 -194 -183 -172 -161 -150 -139 -128 -117 -106 -95 -84 -73 -62 53 64 75 86 97 108 119 130 141 152 163 174 185 196 207 218 229 240 251 262 273 284 295 306 317 328 339 350 361 372 383 394 405 416 427 438]
Fixed pilot tone separation patterns for dRU242 and dRU484 in 80MHz
  E.g., uniform pilot distribution for dRU242
Pilot indices for dRU transmission over 80MHz | 
dRU size | KdRxx_i
dRU52, i = 1:16 | {-447 -359 53 141}, {-403 -315 97 185}, {-227 -139 273 361}, {-183 -95 317 405}, {-425 -117 75 383}, {-381 -73 119 427}, {-337 -249 163 251}, {-293 -205 207 295}, {-194 -106 306 394}, {-150 -62 350 438}, {-370 -282 130 218}, {-326 -238 174 262}, {-260 -172 240 328}, {-216 -128 284 372}, {-392 -84 108 416}, {-436 -348 64 152}
dRU106, i = 1:8 | {-403 -315 97 185}, {-227 -139 273 361}, {-381 -117 119 383}, {-293 -205 207 295}, {-150 -62 350 438}, {-326 -238 174 262}, {-260 -172 240 328}, {-348 -84 152 416}
dRU242, i = 1:4 | {-403 -315 -227 -139 97 185 273 361}, {-381 -293 -205 -117 119 207 295 383}, {-326 -238 -150 -62 174 262 350 438}, {-348 -260 -172 -84 152 240 328 416}
dRU484, i = 1:2 | {-403 -381 -315 -293 -227 -205 -139 -117 97 119 185 207 273 295 361 383}, {-348 -326 -260 -238 -172 -150 -84 -62 152 174 240 262 328 350 416 438}

## Slide 8: Summary
Proposed clean and consistent pilot tone design for distribution BW 20/40/80MHz, in which pilot locations are optimized globally and systematically
  Hierarchical uniform pilot structure of distance of 11
    Consistent for all 20/40/80MHz distribution
    Guarantee of enough separation of pilots for any combination of dRUs
  Fixed large pilot separation for small dRUs ensure frequency diversity in phase tracking
  Fixed pilot tone separation patterns for all dRUs in 20/40 MHz and large dRUs in 80MHz to ease channel smoothing and achieve better smoothing gain

## Slide 9: SP 1
Do you support to add the following text to the TGbn SFD?
  Hierarchical uniform pilot structure of distance of 11 will be used for distribution BW of 20/40/80MHz

## Slide 10: SP 2
Do you support to add the following text to the TGbn SFD?
  The following pilot index table from hierarchical uniform pilot structure of distance of 11 will be used for distributed transmission over 20MHz
Pilot indices for dRU transmission over 20MHz | 
dRU size | KdRxx_i
dRU26, i = 1:9 | {-111 15}, {-89 37}, {-100 26}, {-78 48}, {-67 59}, {-56 70}, {-34 92}, {-45 81}, {-23 103}
dRU52, i = 1:4 | {-111 -89 15 37}, {-100 -78 26 48}, {-56 -34 70 92}, {-45 -23 81 103}
dRU106, i = 1:2 | {-111 -78 15 48}, {-56 -23 70 103}

## Slide 11: SP 3
Do you support to add the following text to the TGbn SFD?
  The following pilot index table from hierarchical uniform pilot structure of distance of 11 will be used for distributed transmission over 40MHz
Pilot indices for dRU transmission over 40MHz | 
dRU size | KdRxx_i
dRU26, i = 1:18 | {-224 28}, {-125 127}, {-202 50}, {-103 149}, {-81 171}, {-114 138}, {-213 39}, {-92 160}, {-191 61}, {-169 83}, {-70 182}, {-147 105}, {-48 204}, {-180 72}, {-59 193}, {-158 94}, {-37 215}, {-136 116}
dRU52, i = 1:8 | {-224 -125 28 127}, {-202 -103 50 149}, {-213 -114 39 138}, {-191 -92 61 160}, {-169 -70 83 182}, {-147 -48 105 204}, {-158 -59 94 193}, {-136 -37 116 215}
dRU106, i = 1:4 | {-224 -103 28 149}, {-213 -92 39 160}, {-169 -48 83 204}, {-158 -37 94 215}
dRU242, i = 1:2 | {-224 -213 -103 -92 28 39 149 160}, {-169 -158 -48 -37 83 94 204 215}

## Slide 12: SP 4
Do you support to add the following text to the TGbn SFD?
  The following pilot index table from hierarchical uniform pilot structure of distance of 11 will be used for distributed transmission over 80MHz
Pilot indices for dRU transmission over 80MHz | 
dRU size | KdRxx_i
dRU52, i = 1:16 | {-447 -359 53 141}, {-403 -315 97 185}, {-227 -139 273 361}, {-183 -95 317 405}, {-425 -117 75 383}, {-381 -73 119 427}, {-337 -249 163 251}, {-293 -205 207 295}, {-194 -106 306 394}, {-150 -62 350 438}, {-370 -282 130 218}, {-326 -238 174 262}, {-260 -172 240 328}, {-216 -128 284 372}, {-392 -84 108 416}, {-436 -348 64 152}
dRU106, i = 1:8 | {-403 -315 97 185}, {-227 -139 273 361}, {-381 -117 119 383}, {-293 -205 207 295}, {-150 -62 350 438}, {-326 -238 174 262}, {-260 -172 240 328}, {-348 -84 152 416}
dRU242, i = 1:4 | {-403 -315 -227 -139 97 185 273 361}, {-381 -293 -205 -117 119 207 295 383}, {-326 -238 -150 -62 174 262 350 438}, {-348 -260 -172 -84 152 240 328 416}
dRU484, i = 1:2 | {-403 -381 -315 -293 -227 -205 -139 -117 97 119 185 207 273 295 361 383}, {-348 -326 -260 -238 -172 -150 -84 -62 152 174 240 262 328 350 416 438}

## Slide 13: Reference
[1] 11-24-0501-02-00bn-pilot-design-considerations-for-dru
[2] 11-24-0468-01-00bn-dru-tone-plan-for-11bn
[3] 11-24-0767-00-00bn-20-mhz-tone-plan-and-pilot-design-for-dru-follow-up
[4] 11-24-0800-02-00bn-dsicussions-on-dru-pilot-design-principles