## Slide 1: Discussions on Extended Long Range PPDU
Date: 2024-01-01
Authors:

## Slide 2: Abstract
Enhanced Long Range PPDU was recently proposed in 802.11bn [1-3].
An ELR PPDU will be helpful in reducing the downlink/uplink range asymmetry problem in current Wi-Fi.
For backward compatibility, an ELR PPDU was proposed to be prepended by the legacy preamble.
In this contribution, we discuss our thoughts regarding the ELR PPDU.

## Slide 3: ELR PPDU Format and Design
In [2], an ELR PPDU format was proposed
The legacy preamble portion supports ELR PPDU backward compatibility. This portion may or may not be received by a very far away AP.
The ELR preamble supports long range STF/LTF/SIG-fields and does not need backward compatibility. This may be the first portion of the PPDU detected by a far away AP.
The ELR Data may feature expanded DCM modes, and/or time domain repetition.
Legacy Preamble
ELR Preamble
ELR Data

## Slide 4: Thoughts on the Legacy Preamble
There are several options for the legacy preamble
Option 1: L-STF, L-LTF, L-SIG
Option 2: L-STF, L-LTF, L-SIG, HT/VHT-SIG-A
Option 3: L-STF, L-LTF, L-SIG, RL-SIG, HE-SIG-A (ER and non-ER)
Option 4: L-STF, L-LTF, L-SIG, RL-SIG, U-SIG (ER and non-ER)
For options 1-3, a new mechanism is required for an ELR STAs to distinguish between an ELR PPDU and a Legacy PPDU. This has been built-in in Option 4. We prefer option 4 as a legacy preamble portion of the ELR PPDU.

## Slide 5: Thoughts on the ELR preamble
There are two options regarding the ELR preamble
Option 1: New designs for ELR-STF, ELR-LTF, ELR-SIG
Option 2: Reuse portions of the Legacy Preamble for ELR-STF and ELR-LTF, New design for ELR-SIG
For option 1, we have full freedom to design the ELR-STF and ELR-LTF. However, complexity may be an issue.
For option 2, we can reuse portions of the legacy preamble to serve as ELR-STF and ELR-LTF. This is our preferred option, but performance may be limited.

## Slide 6: Some thoughts on the ELR-STF
Assuming the AP does not detect the L-STF due to low signal power, a new ELR-STF will be used for
  Packet detection
  Symbol timing
  AGC
  CFO estimation
Proposal : Use L-LTF as ELR-STF: In our opinion, improved packet detection and symbol timing for low signal PPDUs can be done by correlating the L-LTF symbol to the PPDU.
  L-LTF is not optimal for AGC due to only 2 repetitions– However, if the signal power is very low, the AGC may not be critical (i.e. the receiver can set the gain to maximum level).
  L-LTF is not optimal for coarse CFO estimation due to narrow CFO estimation range - To solve this, CFO pre-compensation by STAs using downlink PPDUs may help reduce the need for coarse CFO estimation.

## Slide 7: Some thoughts on the ELR-LTF
Channel estimation when the signal level is extremely low can be improved by having multiple copies of the channel estimate.
Proposal: ELR STA may send predetermined L-SIG and U-SIG symbols for channel estimation purpose. Using the extended range U-SIG, we can have 4x better diversity (i.e. 6 dB) compared to a channel estimate just using the L-LTF.
  Predetermined L-SIG/RL-SIG and U-SIG will result in several constraints that needs further discussions (e.g. PPDU duration, TXOP duration)
L-STF
L-LTF
L-SIG
RL-SIG
U-SIG1
U-SIG1
ELR-SIG
DATA
U-SIG2
U-SIG2
2x
1x
1x
1x
1x
1x
1x
Predetermined L-SIG/RL-SIG
Predetermined ER U-SIG
Diversity of channel estimate using the symbol

## Slide 8: Summary
We proposed an ELR PPDU that aims to reuse the EHT preamble for achieving longer range operation. To achieve longer range operation, some suggestions included
- PPDU detection using L-LTF correlation
- Pre-compensation of CFO at the transmitter
- Predetermined L-SIG/RL-SIG/U-SIG for improved channel estimation performance.
Legacy Preamble
ELR Preamble
ELR Data
L-STF
L-LTF
L-SIG
RL-SIG
U-SIG1
U-SIG2
ELR-SIG
ELR-STF
ELR-LTF

## Slide 9: References
[1] https://mentor.ieee.org/802.11/dcn/24/11-24-0921-00-00bn-an-enhanced-long-range-ppdu.pptx
[2] https://mentor.ieee.org/802.11/dcn/24/11-24-0873-00-00bn-design-targets-and-considerations-for-enhanced-long-range.pptx
[3] https://mentor.ieee.org/802.11/dcn/24/11-24-0875-01-00bn-uhr-enhanced-long-range-support.pptx