## Slide 1: ETSI TC BRAN, July 2024 update
Date: 2024-07-13
Authors:

## Slide 2: ETSI TC BRAN meeting #124
TC BRAN met in June
EN 301 893 (Wireless Access System/Radio Local Area Network, WAS/RLAN, in license-exempt 5 GHz band) finalized
  Submitted for third HASTAC (Harmonised Standard Technical Advisory Consultant) review
  Submitted for final nation vote
Work on EN 303 687 (WAS/RLAN in license-exempt 6 GHz band) continued
Final version of EN 303 753 (Wideband Data Transmission Systems, WDTS, for Mobile and Fixed Radio Equipment operating in the 57 GHz to 71 GHz band) published in May

## Slide 3: EN 301 893 (1)
Normative reference to IEEE 802.11-2020 replaced by ISO/IEC/IEEE 8802-11:2022
  For documents to be listed in the Official Journal of the European Union (OJEU), European Commission (EC) mandates normative references to be limited to standards from ISO, IEC, ITU, CEN, CENELEC, or ETSI
Second normative reference to an ETSI Technical Specification (TS) updated
  EC expects normative references to always refer to the latest version of the reference
TC BRAN asking EC to extend the Date of Withdrawal of version 2.1.1 to 36 months once 2.2.1 is in OJEU
  Ongoing communication with EC

## Slide 4: EN 301 893 (2)
Third and final HASTAC review received
  See BRAN(24)125006 for details
  HASTAC criticizes that second normative reference has been updated since the latest version of EN 301 893 was created
    Catch-22?
TC BRAN to develop HASTAC response at next meeting
  Since EN 301 893 has been submitted for final national vote, HASTAC comments cannot be addressed, anymore
  However, responses needed when final version is submitted to EC for OJEU consideration
Final national vote requested
  National Standards Bodies (NSBs) requested to review final version
    Takes 60 d
    Not yet initiated
  See BRAN(24)124029r2
  To be published as version 2.2.1 if successful

## Slide 5: EN 303 687 (1)
TC BRAN asking EC to consider listing version 1.1.1 in OJEU
  Even if this requires adding a note limiting how the standard may be used for providing presumption of conformity
  See BRAN(24)124019r2
  E-mail exchange between ETSI and EC occurred
    Hopefully can be shared with TC BRAN in the future
Inclusion of normative text describing requirements for operating Narrowband Frequency Hopping (NB FH) remains most important discussion item
  See proposed draft text contained in BRAN(24)124017

## Slide 6: EN 303 687 (2)
Version 1.1.5 of EN 303 687 uses IEEE 802.11ax-2021 as informative reference
  No ISO version of available
  Because of EC concerns, IEEE 802.11ax-2021 no longer used as normative reference

## Slide 7: Modern weather radars
ETSI TC BRAN reviewed ITU-R WP5B.AR contribution 556 by the World Meteorological Organization (WMO) and ITU-R R23-WP5B Temporary Document 33
  Discuss “Technical specifications of solid-state weather radar system – Draft liaison statement to WP 5A on efficiency of DFS regarding these radars in the 5 GHz frequency band”
  Announce that modern/future weather radars use/will use solid-state transmitters (SSTX)
Will RLAN equipment be capable to detect the new radar pulses sequences that are transmitted a lower transmit powers?
ETSI TC BRAN chair invited a member of German Weather Service to report to TC BRAN
  Also, in contact with an employee of a radar manufacturer
  Hopefully, TC BRAN will receive further input
Need to understand requirements and new technical parameters
TC BRAN aims at talking with radar industry instead of industries talking about each other

## Slide 8: Next meetings
Rapporteurs meeting #124a
  Online, 2024-08-23T12:00Z until 2023-08-23T15:00Z
Plenary meetings, all hybrid (online and at ETSI in Sophia Antipolis, France)
  #125, 2024-09-02T12:00Z until 2024-09-05T10:30Z
    Foreshorten by ca. 1 d  provides more time to travel to IEEE 802.11 meeting in Hawaii
  #126, 2024-10-21T12:00Z until 2024-10-25T12:00Z
  #127, 2024-12-16T13:00Z until 2024-12-20T13:00Z