## Slide 1: Low power listening mode for clients follow up
Date: 2024-07-01
Authors:

## Slide 2: Recap (1/2)
To accommodate the large number of small packets in practical scenario, the simple “ACK” function was proposed for low capability mode [1]
  More than 60% DL packets and almost 90% UL packets are less 100 bytes in enterprise scenarios. Similar tendency can also be seen in other scenarios [2]
Moreover, 20 MHz Data transmission was also proposed for low capability mode
  20 MHz Data transmission is in non-HT PPDU format with 1 spatial stream and low MCS
  Mandate inclusion of initial control frame (ICF) at the beginning of the TXOP for transmission with more than 20 MHz bandwidth
  It increases the duration of low capability mode such that to have more power save gain.
MU-RTS
CTS
PPDU
BA
Low capability mode
1 ss, 20 MHz, low MCS
High capability mode
Up to 8 ss, 320 MHz, 4K QAM
Low capability mode
1 ss, 20 MHz, low MCS
20 MHz non-HT PPDU
Ack

## Slide 3: Recap (2/2)
Only a single User Info field was proposed to carry include extra FCS
  An earlier indication in Common User info field for location identification of extra FCS of 4 bytes
  The Use Info field that includes extra FCS starts with an extra FCS. The remaining bits in this User Info field are reserved.
In this contrition, we provide more details based on the received comments in the call.
Frame Control
Duration
RA
TA
Common Info
Special User Info
User Info 1
User Info 2
Extra FCS
Padding User Info…
FCS
Example for initial control frame

## Slide 4: Low capability mode
Low capability mode should be further improved by adding “ACK”
  20 MHz non-HT PPDU transmitted in low capability mode not only includes Data frames, but also includes Management frames and Control frames
Additional overhead could be saved by using a piggyback signaling carried in the 20 MHz non-HT PPDU instead of extra ICF/ICR frame exchange.
The Block Ack function is not provided in low capability mode
20 MHz non-HT PPDU
PPDU
BA
Low capability mode
1 ss, 20 MHz, low MCS
High capability mode
Up to 8 ss, 320 MHz, 4K QAM
Low capability mode
1 ss, 20 MHz, low MCS
20 MHz non-HT PPDU
Ack
Ack
Piggyback a signaling for mode transition

## Slide 5: User Info field for extra FCS
A concern was raised before that user info field starts with an extra FCS will be misread as an AID of a non-AP STA
Same issue was discussed in NDPA design in 802.11ax
  HE STA Info field was extended from 2 bytes to 4 bytes, starting with an AID
  The first 12 bits of the second 2 bytes in HE STA Info field may be interpreted as an AID by the non-AP STA
  The adopted way is to add “Disambiguation” bit to address the above “misinterpretation” issue

## Slide 6: User Info field for extra FCS
Following NDPA design, propose to add “Disambiguation” bit to the User Info field as shown below
  Disambiguation bit is set to 1 in this case
Extra FCS part 1
Disambiguation
Extra FCS part 2
B0
B10
B11
B13
B33
Reserved
B34
B39
User Info field
Note: there is an earlier indication in Common User info field to tell the receiver that the above user info field carries extra FCS

## Slide 7: Summary
In this contribution, we propose more detail about reference [1].
  Low capability mode should be further improved by adding “ACK” function
  Following NDPA design, “Disambiguation” bit is proposed to be added to the User Info field

## Slide 8: References
[1] 11-24-0485-01-00bn-low-power-listening-mode-for-clients
[2] 11-14-0874-00-00ax-unified-traffic-model-on-enterprise-scenario

## Slide 9: SP
Do you agree to use only one User Info field in the initial control frame (e.g., MU-RTS) to carry extra FCS.