## Slide 1: The Padding After Intermediate FCS
Date: 2024-07-05
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
When an AP indicates a non-AP STA to adjust the bandwidth through an initial control frame (ICF), a bandwidth switch padding delay is needed for the non-AP STA;
A normal way is adding the padding in the Initial control frame(ICF), but the issue is padding locates before FCS, but the STA can only start to do the bandwidth switch after FCS check;
Below Motion that passed during the 11bn May meeting solves this issue
  Move to add the following text to the TGbn SFD:
  Define a way in 11bn to include in an initial control frame an intermediate FCS for UHR STA(s) that precedes padding and the FCS field

## Slide 3: Motivation
It is a pure waste if the Padding field directly follows the Intermediate FCS field in the ICF;
If the User info fields for some non-AP STAs can locate after the intermediate FCS field, the total length of the ICF can be reduced;
Two cases will be discussed in the following slides
  Use case 1: Some non-AP STAs doesn’t need to adjust the bandwidth;
  Use case 2: Different non-AP STAs have different bandwidth switch padding delays.

## Slide 4: Use Case 1
Assumptions
  STA 1 ~ STA n have bandwidth switch padding delay requirements;
  STA n+1 ~ STA k don’t have switch delay requirement
The length of ICF will be k-n user info fields shorter when the User Info field of STA n+1~ STA k locate after the intermediate FCS User Info field;

## Slide 5: Use Case 2
Assumptions
  STA 1 ~ STA n1 have larger bandwidth switch padding delay requirements;
  STA n1+1 ~ STA n2 have smaller bandwidth switch padding delay requirements;
The User Info field for STA n1+1 ~STA n2 can locate after the first Intermediate FCS User Info field to save the padding overhead;
A second Intermediate FCS User Info field is needed for STA n1+1 ~STA n2.

## Slide 6: Use Case 2
For AP side, the main change is from two FCSs (1 Intermediate FCS and 1 legacy FCS) to more than two FCSs (>=1 Intermediate FCSs and 1 legacy FCS);
A non-AP STA side will always only need to check 1 FCS, it is the Intermediate FCS or legacy FCS that immediately follows the User Info field for this non-AP STA;
The signaling overhead of the ICF can be significantly reduced in use case 2;
When the AP schedule an ICF, use case 1 and use case 2 can happen simultaneously, and the signaling overhead of the ICF can be further reduced when both cases are considered.

## Slide 7: Key Parameters In Calculations
Below are the assumptions in the calculations:
  Normal PHY rate for non-HT duplicated PPDU is 6 Mbps;
  The length of one User info (for MU-RTS) is 40 bits, and the transmitted time duration is 40bits/6Mbps = 6.667us;
  The Intermediate FCS is carried in 1 User Info field;
    Depends on further discussion, it may be carried in 2 User Info fields, but it doesn’t change the conclusion
  The length of legacy FCS is 32 bits, and the transmitted time duration is 32bits/6Mbps = 5.333us;
  For simplicity, the length of the Padding field will be the integer time of User Info field in the calculations.
  For a non-AP STA with bandwidth switch padding delay t, it requires ceil ((t-5.333us)/6.667us) User Info fields as padding.
Padding delay (us) | 0 | 16 | 32 | 64 | 128 | 256 | 512 | 1024
# of User Info as padding | 0 | 2 | 4 | 9 | 19 | 38 | 76 | 153

## Slide 8: Example 1 for User Case 2
Bandwidth switch padding delay
  STA 1 ~ STA 2: 128us
  STA 3 ~ STA 4: 64us
  STA 5 ~ STA 6: 32us
  STA 7 ~ STA 8: 16us
1 IM FCS: the 1st ~8th User Info (UI) for STA1~STA8, the 9th UI for intermediate FCS (IM FCS), the 10th ~28th UI for padding;
Multiple IM FCS: The allocation showed in below table.
The proposed solution could save signaling overhead (28-22)/28 ≈ 21.4%.
1st UI | 2nd UI | 3rd UI | 4th UI | 5th UI | 6th UI | 7th UI | 8th UI | 9th UI | 10th UI | 11th UI
STA1 | STA2 | IM FCS | STA3 | STA4 | IM FCS | STA5 | STA6 | IM FCS | STA7 | STA8
12th UI | 13th UI | 14th UI | 15th UI | 16th UI | 17th UI | 18th UI | 19th UI | 20th UI | 21st UI | 22nd UI
IM FCS | Padding | Padding | Padding | Padding | Padding | Padding | Padding | Padding | Padding | Padding

## Slide 9: Example 2 for User Case 2
More signaling overhead can be saved if there are more pending STAs could be scheduled;
Bandwidth switch padding delay
  STA 1 ~ STA 2: 128us
  STA 3 ~ STA 10: 64us
  STA 11 ~ STA 14: 32us
  STA 15 ~ STA 16: 16us
1 IM FCS: the 1st ~16th User Info (UI) for STA1~STA16, the 17th UI for intermediate FCS (IM FCS), the 18th ~36th UI for padding;
Multiple IM FCS: The allocation showed in below table.
The proposed solution could save signaling overhead (36-22)/36 ≈ 38.9%.
1st UI | 2nd UI | 3rd UI | 4th UI | 5th UI | 6th UI | 7th UI | 8th UI | 9th UI | 10th UI | 11th UI
STA1 | STA2 | IM FCS | STA3 | STA4 | STA5 | STA6 | STA7 | STA8 | STA9 | STA10
12th UI | 13th UI | 14th UI | 15th UI | 16th UI | 17th UI | 18th UI | 19th UI | 20th UI | 21st UI | 22nd UI
IM FCS | STA11 | STA12 | STA13 | STA14 | IM FCS | STA15 | STA16 | IM FCS | Padding | Padding

## Slide 10: Summary
The Padding field after the intermediate FCS is a pure overhead, and could be long due to the bandwidth switch padding delay requirement from non-AP STA side;
Allowing some User Info fields locate after intermediate FCS can significantly reduce the padding overhead;
When multiple intermediate FCSs are allowed, the padding overhead can further reduced.

## Slide 11: SP1
Do you agree that one or more User Info fields can locate after a Intermediate FCS field in a initial control frame?

## Slide 12: SP2
Do you agree that more than one Intermediate FCS fields could be carried in a initial control frame?