## Slide 1: Preemption Procedure and Indication- Follow Up
Date: 2024-07-10
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
There are a lot of discussion on the procedure of preemptions, they could be divided into two categories in high level
  Preemption allows for both the receiver STA and third party STAs; or,
  Preemption allows only for the receiver STA
Some members concern about the preemption will affect the on-going transmission without the permission of the receiver STA;
Some members want the receiver STA has higher priority to do preemption;
In this proposal, a procedure is proposed which try to have a good balance among:
  Requirements from different members
  Flexibility
  Signaling overhead

## Slide 3: Design Principles
When a STA has low latency traffic, it follows below priority to send the low latency data:
  TXOP holder > receiver STA > the third party STAs
Flexible;
Low signaling overhead

## Slide 4: Proposed Preemption Procedures
A parameter Preemption Indication (PI) is carried in the frame from the TXOP holder
  PI = 0: preemption is not allowed
  PI = 1: only allows the receiver STA send low latency data to the TXOP holder
  PI = 2: allows the receiver STA send low latency data to the TXOP holder or a third party STA
  PI = 3: allows the receiver STA send low latency data to the TXOP holder or a third party STA, or allows a third party STA preempt
A parameter Low Latency (LL) is carried in the frame from the receiver STA
  LL = 0: no low latency data
  LL = 1: has low latency data to the TXOP holder
  LL = 2: has low latency data to the TXOP holder or a third party STA

## Slide 5: Preemption Procedures
When AP allows preemption at receiver STA side (PI = 1), and the receiver STA indicate pending low latency data to AP (LL=1), the receiver STA can directly transit the low latency data (PPDU2) to AP;
When the receiver STA has more pending low latency data to AP, it will indicate LL=1 in the transmitting packet (see PPDU2), otherwise indicate LL=0 (see PPDU3);
When AP receive a PPDU from the receiver STA with LL=0, the AP can indicate PI = 0 in the response frame (see BA3), and take back the TXOP;
Same procedure can be used when a non-AP STA is the TXOP holder.
PPDU1
(PI = 1)
BA1
(LL= 1)
PPDU2
(LL= 1)
BA2
(PI= 1)
PPDU3
(LL= 0)
BA3
(PI= 0)
PPDU4
AP
STA1

## Slide 6: Preemption Procedures
PPDU1
(PI = 2)
BA1
(LL= 2)
PPDU2
(LL= 2)
BA2
PPDU3
(LL= 0)
BA3
(PI= 0)
PPDU4
AP
STA1
STA2
When a non-AP STA allows AP to send low latency data to a third party STA (PI = 2), and the AP indicate pending low latency data to a third party STA (LL=2), the AP can directly transit the low latency data (PPDU2) to a third party STA;
When the AP doesn’t have more pending low latency data to the third party STA, it will send a PPDU to the TXOP holder and indicate LL=0 (see PPDU3) to return the TXOP to the TXOP holder.

## Slide 7: Preemption Procedures
PPDU1
(PI = 3)
BA1
(LL= 0)
PR
PPDU2
AP
STA1
STA2
PIFS
SIFS
When an AP indicates PI = 3 in a PPDU, and the receiver STA indicates no pending low latency data to AP (LL=0), the third party STAs can send PR frames to request for preemption;
The AP will stop transmitting following PPDU2 if a PR frame is received SIFS after BA1, otherwise the AP will transmit PPDU2 PIFS after BA1.

## Slide 8: Preemption Procedures
PPDU1
(PI = 3)
PR
PPDU2
AP
STA1
STA2
PIFS
SIFS
BA1
(LL= 1)
PPDU2
(LL = 0)
BA2
(PI= 3)
When an AP indicates PI = 3 in a PPDU, and the receiver STA indicates pending low latency data to AP (LL=1), the receiver STA will send low latency data (PPDU2) to AP;
When no further low latency data to AP, the receiver STA can indicate LL=0 to AP. Then AP can indicate PI = 3 in the response frame (see BA2) to allow preemption from third party STAs;
A third party STA is allowed to send PR to request preemption under this case.

## Slide 9: Proposed Preemption Procedures
The parameter LL can further indicates the receiver STA’s preference of preemption for the third party STAs;
A parameter Low Latency (LL) indication can updated as below:
  LL = 0: no low latency data, and preemption is allowed
  LL = 1: has low latency data to the TXOP holder
  LL = 2: has low latency data to the TXOP holder or a third party STA
  LL = 3: preemption is not allowed

## Slide 10: Preemption Procedures
The receiver STA can disallow preemption from a third party STA by indicate LL=3 in the response frame;
When AP indicate PI=3 in a PPDU, even the receiver STA doesn’t have pending low latency data, the receiver STA can indicate LL=3;
The third party STAs are not allowed to send PR frame to request for preemption.
PPDU1
(PI = 3)
BA1
(LL= 3)
PR
PPDU2
AP
STA1
STA2
SIFS
SIFS

## Slide 11: Summary
A preemption procedure is proposed for below purpose
  Give higher priority to the receiver STA compare with the third party STAs
  High flexibility
  Low signaling overhead

## Slide 12: SP1
Do you agree to adopt the preemption procedure illustrated from slide 4 to slide 8?