## Slide 1: Discussion on terminology: Sharing and shared AP
Date: 2024-08-06
Authors:

## Slide 2
Abstract
In this contribution we share some thoughts on the terminology used for multi-AP operations in 802.11bn.

## Slide 3: Introduction
Multi-AP has been proposed as a 802.11bn feature, including operations such as
  Coordinated TDMA/rTWT/TWT
  Coordinated OFDMA
  Coordinated spatial reuse
  Coordinated Beamforming
  Joint transmission
Out of these multi-AP coordination schemes, two have passed motion in 802.11bn:
  Multi-AP Spatial reuse at TXOP level
  Multi-AP coordinated beamforming
  Other multi-AP coordination modes are TBD
The terms “sharing AP” and “shared AP” have been used in the context of multi-AP coordination since 802.11be
In this contribution we share our thoughts on why these terms are not correct and on alternative terms

## Slide 4: Multi-AP terminology (1)
The original motion passed in 802.11be is as follows [1]:
    An EHT AP which obtains a TXOP and initiates the multi-AP coordination is the sharing AP.
    An EHT AP which is coordinated for the multi-AP transmission by the sharing AP is the shared AP.
    NOTE – The name of the sharing AP and the shared AP can be modified.
    [Motion 73]
The terms “sharing AP” and “shared AP” in this case are based on the sharing AP obtaining a TXOP first
In order to evaluate the terminologies for multi-AP operations, let us look at two different cases:
  Case 1: multi-AP operations in which an AP first obtains an TXOP and shares with other APs
  Case 2: multi-AP operations that do not depend on one single AP obtains a TXOP first

## Slide 5: Multi-AP terminology (2)
For case 1: multi-AP operations in which an AP obtains a TXOP first and shares with other AP
The terms “sharing AP” and “shared AP” in this case are based on the sharing AP obtaining a TXOP first
  The term sharing AP in this case makes sense, since the sharing AP is sharing its TXOP.
  The term shared AP is still problematic:
    The shared AP is not being shared
However, these terms are still confusing and is not correct, even when one AP shares its TXOP or obtained resources (such as time or frequency)
  AP1 (sharing AP) is sharing its obtained TXOP, but its TXOP is being shared
  AP2 (shared AP) is sharing AP1’s TXOP (a shared TXOP), but AP2 is not being shared

## Slide 6: Multi-AP terminology (3)
It would be better to choose alternative terms, for example,
  Sharing AP -> Initiating AP (IAP)
  Shared AP -> Participating AP (PAP)

## Slide 7: Multi-AP terminology (4)
For case 2: multi-AP operations that do not depend one single AP obtaining a TXOP first
  E.g., coordinated beamforming
In this case, the terms “sharing AP” and “shared AP” do not make sense; for these multi-AP operations, the terms “sharing AP” and “shared AP” should not be used
There are two questions:
  Q1: Would all multi-AP operations be based on TXOP sharing?
    For motions passed in August 2024, it seems that at least one multi-AP operation may not be based on TXOP sharing.
    In addition, we have another contribution in the queue that argues benefits for multi-AP operations that are not solely based on TXOP sharing
  Q2: should all multi-AP operations use the same terminology for participating APs?
    A more uniformed approach seems to be beneficial
It would be better to choose alternative terms than the current “sharing” and “shared AP”

## Slide 8: Conclusions
  We discussed the terminologies for multi-AP operations “sharing AP” and “shared AP”
  We evaluated these terms for two cases of multi-AP operations:
    For case 1: multi-AP operations that are based on one AP obtaining a TXOP and shares with other APs:
      These terms are confusing and not correct (“shared AP”) and should be changed
    For case 2: multi-AP operations that do not depend on one single AP obtaining a TXOP and sharing with other APs:
      These terms are not correct and should not be used
  Terminology should be uniform for all multi-AP operations defined in 802.11bn, alternative terms may be:
    Initiating AP (IAP)
    Participating AP (PAP)

## Slide 9
References
[1] 11-20/1935r66, Compendium of straw polls and potential changes to the Specification Framework Document Part 2, Edward Au
[3] 11-23/0170, Smooth Roaming, Liwen Chu
[4] 11-23/231, Thoughts on Seamless Roaming Under Non-collocated AP MLD Architecture, Guoguang Huang
[5] 11-23/295r1, Discussion on Multi-AP Coordination, Xiaofei Wang

## Slide 10: SP #1
Do you agree that the same terminology should be used for participating APs for all multi-AP operations?
  Yes
  No
  Abs:

## Slide 11: SP #2
Do you agree to use the following terms for APs that coordinates a multi-AP operation and that are being coordinated in a multi-AP operation:
    Initiating AP (IAP)
    Participating AP (PAP)
  Yes
  No
  Abstain