## Slide 1: Coordinated TDMA analysis for time-sensitive traffic under congested scenarios
Date: 05-13-2024

## Slide 2: Goals
Performance evaluation of C-TDMA under congested scenarios, including OBSS/ESS and repeater deployments, focusing on time-sensitive services
Establishment of realistic simulation frameworks including modeling of high-level transport protocols

## Slide 3: Introduction
802.11bn targets the improvement of packet delivery by reducing the transmission latency and enhancing network reliability [1]
Applications and use cases with QoS-related requirements (e.g., bounded latency and reliability) have been growing in recent times [2]
  The critical QoS services can be mainly characterized by periodic traffic patterns, and strict timing requirements for data exchange [2, 3]
  Relying on enhancing throughput is not tenable in the long term as a sole requirement for correct QoS service operation, especially under heavily congested scenarios

## Slide 4: Motivation
The wireless scenarios are getting more congested due to the increase of connected 802.11 devices, competing for the wireless medium in the same primary channel.
It has been shown that as congestion increases, and under contention-based congestion management, aggregated throughput gets saturated, and the latency is highly affected [4, 5, 6].
On the other hand, many services run over transport protocols such as TCP, whose functionality depends on the RTT (Round Trip Time) latency performance, degrading the throughput while the latency increases.
Coordinated TDMA mechanism under Multi-AP framework [7, 8] may improve the predictability of those time-sensitive services, helping to redistribute the time resources.

## Slide 5: C-TDMA: Recap
BSS1 TXOP
Time
BSS2 TXOP
Time
AP BSS1
AP BSS2
TXS RTS TF
CTS
Shared TXOP
BSS2 TXOP
BSS1 TXOP
TXS RTS TF
CTS
Shared TXOP
Coordinated TDMA allows cooperation of two APs, by sharing the gained TXOP between them
Both BSSs take advantage of the gained time, reducing the waiting time to access the channel, and hence the latency of the different traffic flows, especially for those that have higher priority access category
Other AP BSSs
TXOP
TXOP
Time

## Slide 6: C-TDMA: Latency Reduction
C-TDMA does not change the time used per BSS, it redistributes the assigned time to the coordinated APs, getting an improvement in latency, by reducing the access time for the shared AP
BSS1 TXOP
Time
Time
AP BSS1
AP BSS2
TXOP
BSS2 TXOP
BSS1 TXOP
TXOP
BSS1 Access Interval
Time
Uncoordinated
Other AP and non-AP STAs
Heavily Congested
BSS1 TXOP
Time
BSS2 TXOP
Time
AP BSS1
AP BSS2
TXS RTS TF
CTS
Shared TXOP
BSS2 TXOP
BSS1 TXOP
TXS RTS TF
CTS
Shared TXOP
Other AP and non-AP STAs
TXOP
Time
TXOP
BSS1 TXOP
BSS2 TXOP
TXS RTS TF
CTS
Shared TXOP
BSS1 Access Interval
BSS1 Access Interval
C-TDMA
Heavily Congested

## Slide 7: Simulation Setup
We identify two scenarios where the C-TDMA mechanism can be deployed
  OBSS scenario: coordination between at least one pair of independent neighboring BSSs sharing the same channel
  Repeater (ESS) scenario: coordination between two in-home AP devices from the same network (ESS), and sharing the same channel.

## Slide 8: OBSS Simulation Setup
Four independent BSSs, each one per apartment, each BSS is composed of one AP and 5 non-AP STAs
All STAs are in ED range
  Next step will include [PD, ED] range
Three possible coordination scenarios
  Uncoordinated (Baseline)
  BSS1/BSS2 coordinated
  BSS1/BSS2 and BSS3/BSS4 coordinated
PHY/MAC configuration for Data frames
  SU 80 MHz/1SS/MCS:11 for creating overloading/saturation situation
  SU 160 MHz/2SS/MCS:11 for creating underloading situation
Note: underload and overload situation is a combination of PHY settings, scheduling, data traffic, network topology and AC settings.

## Slide 9: Repeater Simulation Setup
ESS is composed of a Gateway (GW) and Repeater (R) devices, connected through a wireless backhaul
The Repeater is composed of a non-AP STA and AP devices, internally bridged using the same radio
Each AP has 5 associated STAs
The STAs All are in ED range
  Even if in ED range, Repeater associated STAs may have poor link with the Gateway
  Next step will include [PD, ED] range
Two possible coordination scenarios: uncoordinated and GW/R coordinated (both do C-TDMA)
PHY/MAC configuration for Data frames
  SU 80 MHz/1SS/MCS:11 for creating overloading situation

## Slide 10: Traffic Generation (OBSS Case)
Each BSS has the following data services:
  STA1 Service: Video conference (DL/UL 3 Mbps, 250B length) [UDP, VI_AC]
  STA2 Service: Video streaming 4K UHD H264 (DL 32 Mbps, 1500B length) [closed-loop TCP, VI_AC]
  STA3 Service: Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  STA4 Service: Cloud file sync (DL/UL 10 Mbps, 1500B length) [closed-loop TCP, BE_AC]
  STA5 Service: Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]
TCP generates TCP-ACK traffic (small length frames)
All the STAs generate UL traffic (using TB and EDCA mechanisms)

## Slide 11: Traffic Generation (Repeater Case)
Gateway associated STAs:
  STA1 Service: Video conference (DL/UL 3 Mbps, 250B length) [UDP, VI_AC]
  STA2 Service: Video streaming 4K UHD H264 (DL 32 Mbps) [closed-loop TCP, VI_AC]
  STA3 Service: Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  STA4 Service: Service 4: Cloud file sync (DL/UL 10 Mbps) [closed-loop TCP, BE_AC]
  STA5 Service: Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]
Repeater associated STAs:
  STA6 Service: Video conference (DL/UL 3 Mbps, 250B length) [UDP, VI_AC]
  STA7 Service: Video streaming 4K UHD H264 (DL 32 Mbps) [closed-loop TCP, VI_AC]
  STA8 Service: Video streaming 4K UHD H264 (DL 32 Mbps) [closed-loop TCP, VI_AC]
  STA9 Service: Gaming (DL/UL 140kbps, Periodicity 7 ms, 110B length) [UDP, VO_AC]
  STA10 Service: Camera (UL 2 Mbps, 1450B length) [UDP, VI_AC]
Backhaul link: STA6-10 services
All the STAs generate UL traffic (using TB and EDCA mechanisms)

## Slide 12: C-TDMA Strategies
We distinguish two different approaches to decide the shared TXOP length
Strategy 1: Share the remaining TXOP length, after the sharing AP local buffers are empty (for the gained and higher ACs)
Strategy 2: Pre-negotiated soft time threshold between the two coordinated APs
  The sharing AP may start sharing the TXOP before the time threshold if it has no more data, for the gained and higher ACs, in its BSS (Case A)
  The sharing AP may delay sharing the TXOP if there is an ongoing data exchange that exceeds the time threshold (Case B)
  It defines a flexible maximum time length that the sharing AP can use for transferring data, established by an external arbiter, while the rest will be used by the shared AP
Both strategies end the TXOP after the shared AP finishes
  It can be a premature termination sending CF-End frame
Next step simulations will include dynamic TXOP sharing ratio calculation
BSS1 TXOP
(Sharing)
BSS2 TXOP (Shared)
Time
AP BSS1
AP BSS2
TXOP
C-TDMA
BSS1
No Data
Time
Threshold
BSS2 TXOP
(Sharing)
BSS1 TXOP (Shared)
TXOP
Time
Threshold
Last exchange finished
S2: Case A
S2: Case B
BSS2
No Data
BSS1
No Data

## Slide 13: OBSS – Overall Network Results
Network overloaded/saturated situation
Network underloaded situation
For both network situations, while C-TDMA is set up the Strategy 2 using a time threshold of 50% (over the total gained TXOP length), it can be observed a trend for overall network latency (P95) reduction, including the total number of collisions in the air, increasing the air usage efficiency.

## Slide 14: OBSS - Gaming Results
Network overloaded/saturated situation
Network underloaded situation
For both network situations, it can be observed that when BSS1/BSS2 use C-TDMA, the latency is reduced by 20-30%, while the uncoordinated BSSs (BSS3/BSS4) are not affected by unfairness. The same latency gain is obtained when both BSS pairs coordinate their transmissions.

## Slide 15: OBSS – Video Conference Results
Network overloaded/saturated situation
Network underloaded situation
In a very similar trend, the video conference latency results show an improvement in the RTT latency by 40-60% respect the uncoordinated setup

## Slide 16: OBSS – Video Streaming Results
Network overloaded/saturated situation
Network underloaded situation
The use of C-TDMA improves the throughput performance for Video Streaming, as TCP is sensitive to latency performance, obtaining a gain in the range 10-20%

## Slide 17: Repeater/Mesh Simulation Results
Five different coordination setups
  No coordination between GW and Repeater (baseline)
  C-TDMA Strategy 1
  C-TDMA Strategy 2
    Having a sharing threshold of 50/50: 50% of TXOP length for the GW, and 50% length for the Repeater
    Having a sharing threshold of 60/40: 60% of TXOP length for the GW, and 40% length for the Repeater
    Having a sharing threshold of 70/30: 70% of TXOP length for the GW, and 30% length for the Repeater
No improvement for Strategy 1, few opportunities for sharing the TXOP, and having additional overhead, the network latency gets worse respect the uncoordinated setup.
Best improvements for sharing thresholds of 50/50 and 60/40, improving the data flow along the Repeater.
Reducing the shared TXOP length on the Repeater side increases the latency, having less time to schedule its associated STAs. Even if the traffic load is higher in the GW side, the number of associated STAs in both sides is the same.

## Slide 18: Repeater/Mesh – Gaming/Video Conference Results
The gaming latency improves in the Repeater side for both C-TDMA strategies. As the traffic load for gaming is low, the gained VO_AC TXOP has enough length for sharing in both BSSs.
For C-TDMA S2, video conference latency is improved by 65%, as the coordination enhances the data flow between the GW and Repeater
The GW side performance shows no variation, the main contribution of C-TDMA is the improvement on the Repeater side

## Slide 19: Repeater/Mesh – Video Streaming Results
The use of C-TDMA S2 improves the latency in video streaming service, and consequently the throughput is improved, as TCP is sensitive to the RTT latency.
Again, the GW side performance shows no variation, the main contribution of C-TDMA is the improvement on the Repeater side

## Slide 20: Summary
C-TDMA improves the performance in those latency-sensitive flows/services already configured with their corresponding high-priority ACs, otherwise the improvement is limited.
C-TDMA redistributes the time resources, giving more chances to specific already protected services, but does not create additional resources
C-TDMA provides better chances to give the channel to another BSS, especially in those highly congested scenarios with many contending STAs
Coordinated APs need to generate the same number of TXOPs, with the same priority, to have balanced cooperation, otherwise only one network will take advantage of C-TDMA
  Next steps will include scenarios of unbalanced networks
Most advantages of C-TDMA can be seen in repeater scenarios, improving the performance in terms of throughput and RTT latency of the Repeater network for the protected services

## Slide 21: Conclusion
We have presented simulation results for Coordinated TDMA mechanism, focusing on the performance improvement of the latency sensitive services.
We have covered the highly congested scenario under an OBSS environment, and the repeater scenario.
In both cases, we have showed how C-TDMA can increase the number transmission opportunities for those services configured with high priority AC, which under congestion conditions may have limited advantage.
In the repeater case, the coordination between the two APs improves the data flow through the wireless backhaul.

## Slide 22: References
[1] IEEE 802.11-23/0028r6, UHR PAR discussion
[2] Inaki Val and et al. (MaxLinear), “High Criticality Use Cases and Requirements”, 23/1522r0
[3] Oliver Holland and et al. “Low Latency Communication White Paper”, P802.24-23-0010r4
[4] Salvatore Talarico and et al. (Sony), “Enhanced HCCA for Controlled UHR Scenarios”, 24/0119r0
[5] Yanchun Li and et al. (Huawei), “Discussion on UHR enhanced channel access”, 23/1973r1
[6] Inaki Val and et al. (MaxLinear), “Managed Networks under highly congested scenarios - Follow up”, 24/0405r1
[7] Abhishek Patil and et al. (Qualcomm), “Coordinated TDMA (C-TDMA) Follow-up”, 23/1895r2
[8] Geonhwan Kim and et al. (LG Electronics), “Coordinated TDMA Procedure”, 23/1912r1