## Slide 1: Legacy preamble for ELR PPDU
Date: 2024-08-14
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | 

## Slide 2: Background
Legacy Preamble
ELR Preamble
ELR Data
The following PPDU format has been proposed in [1].
In this contribution, the legacy preamble in ELR PPDU is discussed.
  More accurately, the legacy preamble can be named as non-ELR preamble, can include other symbols besides symbols in L-STF field, L-LTF field and L-SIG field.

## Slide 3: ELR Legacy preamble functions
Legacy Preamble
ELR Preamble
ELR Data
The legacy preamble may need to provide the following functions:
  Spoofing function: provide coexistence for legacy devices and 3rd party devices.
  ELR identification: provide auto-detection function for receivers (e.g., an AP) which may need to receive both ELR PPDU and non-ELR PPDU.
    This can be a bonus and may simplify the Rx procedure.
Regarding the spoofing function, back in 11ba and 11be, it is preferred that the first and second symbols after L-SIG field are BPSK modulated.
  The new PPDU will be spoofed as a non-HT PPDU. Legacy devices will keep decoding until the end of the PPDU. This provides better protection.
  Otherwise, if the first symbol is detected as QBPSK, the PPDU will be spoofed as an HT PPDU. The L-SIG length may not be respected.
  If the first symbol is detected as BPSK, and the second symbol after L-SIG is detected QBPSK, the PPDU will be spoofed as a VHT PPDU. “VHT-SIG-A” will be wrongly decoded. If the Rx thinks it cannot decode a BPSK modulated SIG field correctly. This may lead to some unknown implementation issues.

## Slide 4: ELR Legacy preamble formats
Regarding the auto-detection function, here we assume the Rx (e.g., AP) will do parallel detections of L-STF field and ELR-STF field.
  ELR-STF field will be longer than L-STF field, and provides packet detection/auto-detection function for further range [2].
L-STF field from an ELR PPDU or non-ELR PPDU may also be detected by the Rx. If the legacy preamble can provide auto-detection function and helps the Rx identify ELR PPDU from non-ELR PPDUs. This can simplify the Rx procedure.
  Or the Rx may continue to do parallel detection of ELR-STF.
The following two options are proposed:
L-STF
L-LTF
L-SIG
ELR BPSK Mark 1
ELR BPSK Mark 2
ELR STF
…
L-STF
L-LTF
L-SIG
RL-SIG
U-SIG-1
U-SIG-2
ELR-STF
…
Opt 1:
Opt 2:

## Slide 5: ELR Legacy preamble comparison
For Opt 1, ELR BPSK Mark 1 and ELR BPSK Mark 2 can provide spoofing functions for legacy devices. And can additionally provide identification of ELR PPDU.
  ELR BPSK Mark symbols need to be different from RL-SIG and WUR BPSK Mark symbols.
For Opt 2, there is one additional symbol overhead. However, it provides forward compatibility. The auto-detection is simpler. The U-SIG can directly indicate the PPDU Type And Compression Mode as ELR PPDU.
If ELR PPDU is detected, the Rx can continue process ELR-STF.
  If some errors happen during the L-preamble processing, the Rx can continue to try to detect ELR-STF.
Opt 2 is preferred.
L-STF
L-LTF
L-SIG
ELR BPSK Mark 1
ELR BPSK Mark 2
ELR STF
…
L-STF
L-LTF
L-SIG
RL-SIG
U-SIG-1
U-SIG-2
ELR-STF
…
Opt 1:
Opt 2:

## Slide 6: L-SIG field and U-SIG field for an ELR PPDU
Following Opt2, in the L-SIG field, the RATE is set to 6 Mbps and the L-SIG length is set to a multiple of 3, same as an EHT PPDU.
In the U-SIG field of a UHR ELR PPDU, the PHY Version Identifier is set to 1 as any UHR PPDU.
The PPDU Type And Compression Mode can be used to indicate ELR PPDU.
  For UL, set to 2 or 3 to indicate ELR PPDU.
  For DL, if ELR PPDU can be applied, set to 3 to indicate ELR PPDU.
Version independent info in U-SIG field (e.g., Bandwidth, BSS color and TXOP) provides better coexistence and forward compatibility.

## Slide 7: Summary
In this contribution, two possible options of legacy preamble for ELR PPDU are discussed. Opt 2 is preferred among the two options.
Future work include ELR preamble and ELR data discussions.

## Slide 8: Straw Poll 1
Do you agree to include the following into the 11bn SFD?
  The legacy preamble for a UHR ELR PPDU includes: L-STF, L-LTF, L-SIG, RL-SIG and U-SIG field.
    The L-SIG field setting is the same as 11be.
  Y
  N
  A

## Slide 9: Straw Poll 2
Do you agree to include the following into the 11bn SFD?
  In the U-SIG field of a UHR ELR PPDU, the PHY Version Identifier is set to 1. And the PPDU Type And Compression Mode is used to indicate ELR PPDU.
    Whether applicable to UL only or both is TBD
  Y
  N
  A

## Slide 10
11-24-0873-02-00bn-design-targets-and-considerations-for-enhanced-long-range, Jianhan Liu (Mediatek)
11-24-1255-00-00bn-enhanced-long-range-frame-format, Junghoon Suh (Huawei)
11-24-1232-00-00bn-thoughts-on-extended-long-range-transmission, Leonardo Lanante (Ofinno)
11-24-1184-00-00bn-considerations-on-elr-transmission, Dongguk Lim (LGE)
11-24-0875-01-00bn-uhr-enhanced-long-range-support, Rui Cao (NXP)
11-20-0921-04-00be-discussion-about-str-capabilities-indication, Wook Bong Lee (Apple)
References