## Slide 1: UHR Multi-channel Access
Date: 2023-09-4
Authors:
Name | Affiliations | Address | Phone | Email
Yanchun Li | Huawei | Huawei Industrial Base, Bantian Longgang District, Shenzhen, China 518129 |  | liyanchun@huawei.com
Guogang Huang |  |  |  | 
Yunbo Li |  |  |  | 
Yuchen Guo |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Dekun Liu |  |  |  | 
Yanbin Sun |  |  |  | 
Xuming Wu |  |  |  | 
Yan Zeng |  |  |  | 
Notes: November 2012

## Slide 2: Introduction
UHR PAR has defined the requirement on reduced latency. Multi-channel access is a promissing scheme for this purpose. TGbe has adopted multi-link operation (MLO), while TGbn SFD has accepted non-primary channel access (NPCA).
Both of these schemes require deterministic channel occupation information, for link switching/ primary channel switching decision. However, realistic traffic has uncertainty and make multi-channel access challenging.
This contribution discusses the multi-channel access efficiency with uncertain traffic.
September 2024

## Slide 3: Background: Resource Reservation can reduce latency
September 2024
Fig.1 Delay due to OBSS channel occupation
Low-latency (LL) Traffic arrival
t
OBSS Tx
LL Traffic
Channel Busy
Primary Channel
Low-latency (LL) Traffic arrival
t
OBSS Tx
LL Traffic
Fig.2 e.g. Coordinated R-TWT
Primary Channel
Resource Reservation by TWT SP at expected traffic arrival time

## Slide 4: Background (2): Multi-channel Access schemes reduce latency
Once an OBSS announces that it will occupy part of channel, AP/STA can switch to non-primary channel or another channel/link. Keep in mind that the original primary channel or primary link is still AP/STA’s first (best) choice.
  NCPA:
  MLO (single radio): (assuming STA shares hardware for channel 1 and 2) (DSO is similar)
P80
P160
S80 (NP)
S80
P80
Ch2
Ch1
P160
P160
P80
OBSS occupation
AP’s primary mode
AP’s secondary mode
AP’s primary mode
AP’s secondary mode
t
t
Logical 20MHz control channel in real-time use
September 2024

## Slide 5: Channel reservation and traffic uncertainty
According to AP1’s high-priority application traffic pattern, AP1 can announce its reserve SPs on specific channel in advance.
S80
P80
P80
AP1
Announce
SP1
P80
SP1
P80
SP1
P80
SP1
If traffic is absent in some SP, this SP is left blank by AP1.
Traffic arrival
Traffic arrival
Traffic arrival
September 2024

## Slide 6: Issue in Basic Multi-channel Access schemes
OBSS’s R-TWT SP announcement does not always leads to non-primary channel use or channel switching.
S80
P80
P80 (wasted)
S80 (NP)
AP1
Announce
AP2
Announce
AP1 had announced SP1 on Ch1. But Ch1 is not efficiently used:
Case 1: due to lack of traffic, AP1 makes no use of this SP. (AP may transmit CF-End to release this SP.)
Case 2: AP1 only needs to transmit to a near STA with low transmit power, the spatial reuse is allowed in SP1.
To support low latency access at expected traffic arrival time, AP1 announces a SP1 (e.g. R-TWT or Coordinated R-TWT SP), or P2P R-TWT
To allow STAs to switch accordingly, AP1 announces a SP (e.g. R-TWT or Coordinated R-TWT) which involves secondary channel/link switching.
SP1
September 2024

## Slide 7: An Efficient Multi-channel Access operation
AP2 can sense channel in the begin period of OBSS’s announced R-TWT SP. If AP2 has not detected channel occupation in this period, AP2 can keep using this best channel, instead of switching to less favorable secondary link/non-primary channel.
S80
P80
P160
AP1
Announce
AP2
Announce
AP2 can announce that switch to Ch2 is tentative:
Condition 1: Ch1 is idle during CS period, AP2 keeps using Ch1.
Condition 2: Ch1 is busy, AP2 switches to Ch2.
AP2’s CS Period can be a preset duration. Or AP2 announce a value n1, can calculate the duration by SIFS+n1*backoff slot.
SP1
CS
AP2 channel sensing
AP2’s CS Period
September 2024

## Slide 8: STA’s behavior to catch up AP’s tentative switches
AP2 shall initiate transmission on Ch1 before (non-AP) STA’s CS period ends.
So that STA can detect AP2’s present on Ch1 before STA’s CS period ends.
If STA has detected AP2’s present on Ch1, STA can communicate with AP2 on Ch1.
If not, STA can switch to Ch2.
S80
P80
P160
AP1
Announce
AP2
Announce
SP1
CS
AP2 channel sensing
AP2’s CS Period (SIFS+N*slot)
STA’s CS Period1
AP2’s ICF frame on Ch1, or PPDU with AP2’s BSS color in Preamble.
September 2024

## Slide 9: STA’s behavior to catch up AP’s tentative switches
AP2 shall send channel occupation signal on Ch2 within STA’s CS Period2.
If STA has detected AP2’s present signal on Ch2, within CS period 2. STA keeps on Ch2.
Otherwise, STA can switch back to Ch1.
S80
P80
Ch2
AP1
Announce
AP2
Announce
SP1
CS
AP2 channel sensing
AP2’s CS Period
STA’s CS Period1
AP2’s ICF frame on Ch2, or PPDU with AP2’s BSS color in Preamble.
STA’s CS Period2
September 2024

## Slide 10: Framework for tentative TWT SP channel access
OBSS’s tentative TWT SP Announcement, e.g.
AP1
Announce
AP2
Announce
SP slot1
P80
SP slot2
P80
Target Wake Time
Nominal Minimum TWT Wake Duration
TWT Wake Interval Mantissa
(new added)
Spatial Reuse allowed
Tentative or not
September 2024

## Slide 11: Framework for tentative TWT SP channel access
Local AP’s tentative TWT SP Announcement, e.g.
Target Wake Time
Nominal Minimum TWT Wake Duration
TWT Wake Interval Mantissa
(new added)
Tentative or not
STA’s CS Period1
STA’s CS Period2
S80
P80
Ch2
AP1
Announce
AP2
Announce
SP1
CS
AP2 channel sensing
AP2’s CS Period
STA’s CS Period
STA’s CS Period2
September 2024

## Slide 12: Comparison of switching conditions in multi-channel schemes
September 2024
Triggering Signal for NPCA channel switch | Reference | Pros | Cons
OBSS Control Frame | Current SFD |  | Synchronization issue: e.g. AP on Primary, STA on Secondary, or vise versa.
ICF frame (for MLO/EMLSR/PS) | 11be/ 11bn contributions [6] | Robust | 
Reception of ‘switching’ indication frame from local AP on Primary channel | [5] | Low latency High efficiency Robust (STAs can receive control frame from their own AP with high probability) | 
Timeout of ‘stay-on-primary’ indication frame from local AP on Primary channel within a specified period | this contribution | Robust (STAs can receive control frame from their own AP with high probability) | 

## Slide 13: Conclusions
11bn aims at low latency access for some high-priority traffic. To guarantee contention/deferral free channel access, some OBSS AP may reserve TWT SPs beyond the actual needs. The uncertain arrival of traffic may lead to inefficient use of channel resource in these SPs.
Local AP’s active switching to a secondary link (or a non-primary channel) can avoid collision with OBSS AP’s reserve TWT SPs. But if there are lots of wasted over reserved TWT SPs and , local AP’s better choice is to watch OBSS AP’s actual occupation in OBSS AP’s claimed TWT SPs. So, local AP can avoid unnecessary secondary link (or a non-primary channel) switches.
In summary, 11bn shall define a scheme to allow use of leftover TWT SPs for channel efficiency.
September 2024

## Slide 14: Straw Poll 1
Do you agree to define such NPCA behavior in SFD:
- The BSS can switch to a non-primary channel at a period overlapped with OBSS’s SP on the primary channel?
  - Y
  - N
  - Abs
September 2024

## Slide 15: Straw Poll 2
Do you agree to define tentative SP in SFD to support low latency service in dense deployment scenario:
Tentative SP in multi-channel access scenarios, is a candidate SP which is cancellable on a specific channel, if AP has not presented within scheduled duration in this SP.
  - Y
  - N
  - Abs
September 2024

## Slide 16: Straw Poll 3
Do you agree to define such NPCA behavior in SFD:
- AP can announce switching to non-primary channel at the period overlapped with OBSS’s SP on primary channel?
  - Y
  - N
  - Abs
September 2024

## Slide 17: Straw Poll 4
Do you agree to define such NPCA behavior in SFD:
AP can announce tentative switching to non-primary channel
AP can insist on primary channel by transmitting TBD PPDU on primary channel, if primary channel is available.
  - Y
  - N
  - Abs
September 2024

## Slide 18: Reference
[1] 11-23-1952-00-00bn-coordinated-r-twt-for-multi-ap-scenarios-follow-up, Liuming Lu
[2] 11-23-2022-01-00bn-r-twt-for-multi-ap-follow-up, Laurent Cariou
[3] 11-23-1932-03-00bn-further-considerations-on-coordinated-twt, Rubayet Shafin
[4] 11-24-0742-00-00bn-obss-twt-management-for-map, Pascal Viger
[5] 11-24-0318-00-00bn-robust-secondary-channel-access, Yanchun Li
[6] 11-24-1587-02-00bn-discussion-on-dso-operation, Kaiying Lu
September 2024