## Slide 1: DPWiFi revA
Date: 2024-9-12
Authors:

## Slide 2: Abstract
TGbn PHY candidate DPWiFi originally proposed Nov ‘23, an improved radiowave polarization processing model incorporated June ‘24 unearthed a serious, latent flaw in the original Dynamic Polarization Propagation Channel formulation. Since remedied, the updated “DPWiFi revA” TRX model as well as its corresponding MATLAB functional validation and performance characterization data, analyses and conclusions are presented herein.

## Slide 3
WiFi Static Polarization Operation
A WiFi Tx antenna “polarizes” by launching RF waveforms S in a precise spatial orientation per an “Orthogonal Polarization Baseline (OPB)”
Linearly Polarized PTX radiates along a fixed 0o or 90o H/V angle
PTX(S) = H or V
Typical terrestrial propagation “depolarizes” S by rotating PTX by a “depolarization angle” ψ
  LP waveforms propagate fixed-rotated by ψo from true OPB H-V
  PTX (S, ψ) = ψ or ψ + 90o
A WiFi Rx antenna “polarization-filters” detected waveforms into “Matched-Polarization (MP)” or “Mismatched-Polarization (MMP)” components
PRX (S, ψ) = H or V
MP (PTX (S,ψ)) = cosψ S(t)
MMP (PTX (S, ψ)) = sinψ S(t)

## Slide 4
DPWiFi Dynamic Polarization Operation
A DPWiFi Tx Antenna modulates polarization by switching between two orthogonal antenna elements per a binary sequence DPC
DPTX(S) = Tx DPC
Propagation depolarization rotates DPTX orthogonality baseline by ψ
DPTX (S, ψ) = Tx DPC(ψ)
A DPWiFi Rx Antenna polarization-filters DPTX into “Matched-DPC (MDPC)” or “Mismatched-DPC (MMDPC)” elements
DPRX(S) = Rx DPC
MDPC (S, ψ) = cosψ S(t)
MMDPC (S, ψ) = f(S(t), cosψ, sinψ)
MDPC S*(t)
MMDPC S*(t)

## Slide 5
DPWiFi revA TRX Model
  Given n WiFi-7 RF stream n-vectors [S], [S*] and [S’], and
  The ψ-depolarized Propagation Channel nxn matrix [HDP], and
  Walsh n-vectors [TxDPC] and [RxDPC] such that
[TxDPC] = [DPC1 DPC2 … DPCn] = [RxDPC], where
DPCi · DPCj = cosψ if i = j
DPCi · DPCj = (cosψ + sinψ)/2 if i ≠ j
    If [HDP] is Non-Singular there exists an [HDP-1]such that [S’] = [S] x [HDP] x [HDP-1]= [S]

## Slide 6
DPWiFi revA [HDP] Propagation Channel
  Walsh-modulated DPWiFi Polarization establishes that
  S*(t) = cosψ S(t) if Tx DPC = Rx DPC, or S*(t) = (cosψ + sinψ)/2 S(t) if Tx DPC ≠ Rx DPC
  Extending to the case of n Si and corresponding DPCi we obtain [S*] = [S] x [HDP], where
  Noting that for 0o < ψ < 45o
  0.50 ≤ (cosψ + sinψ)/2 ≤ 0.71 and 0.70 ≤ cosψ ≤ 1.00, we can therefore conclude
    The DPWiFi revA Propagation Channel [HDP] is Indeed Non-Singular

## Slide 7
DPWiFi revA [HDP-1] Rx MIMO Demultiplexer
Given:
Then:
Equivalently:
Given:
Then:
Equivalently:
    The DPWiFi revA MIMO Demultiplexer [HDP-1] is a Trivial Construct

## Slide 8
DPWiFi (rev-) vs DPWiFi (revA)
    DPWiFi rev- is just a Degenerate Manifestation of DPWiFi revA
    Note: DPWiFi rev- and DPWiFi revA are equivalent for ψ < 7.5o

## Slide 9
DPWiFi revA MATLAB Representation

## Slide 10
DPWiFi revA [HDP] MATLAB Operation
S1
S2
S32
S*1
S*2
S*32
[S]
[S*]

## Slide 11
Representative DPWiFi revA MATLAB Simulation Results

## Slide 12
DPWiFi revA MATLAB Validation
(See Appendix A for full DPWiFiTRXv2 Control Panel/Visualization Window Screen Shots)
DPWiFiTRXv2 BER vs Channel Depolarization, Rx Adaptation |  |  |  |  | 
Case | Signal | MIMO Order | Channel ψ (o) | Rx Adaptation | BER
1 | MCS13 320 MHz | 32 | 0.0 | N | 0.00e0
2 | MCS13 320 MHz | 32 | 1.0 | N | 0.00e0
3 | MCS13 320 MHz | 32 | 1.1 | N | 3.84e-3
4 | MCS13 320 MHz | 32 | 1.1 | Y | 0.00e0
5 | MCS13 320 MHz | 32 | 5.0 | N | 1.96e-1
6 | MCS13 320 MHz | 32 | 5.0 | Y | 0.00e0
7 | MCS13 320 MHz | 32 | 10.0 | N | 2.75e-1
8 | MCS13 320 MHz | 32 | 10.0 | Y | 0.00e0
9 | MCS13 320 MHz | 32 | 25.0 | N | 3.84e-1
10 | MCS13 320 MHz | 32 | 25.0 | Y | 0.00e0
11 | MCS13 320 MHz | 32 | 40.0 | N | 4.50e-1
12 | MCS13 320 MHz | 32 | 40.0 | Y | 0.00e0

## Slide 13
DPWiFi revA MATLAB Validation Analysis
DPWiFi RevA Salient Observations
DPWiFi revA Evaluation
  DPWiFi revA is extraordinarily sensitive to propagation channel depolarization Absent receiver adaptation, even a slight morning mist would crash a DPWiFi link
  Rx Adaptation, however, comprehensively mitigates any amount of such depolarization
DPWiFi revA Concluding Remarks DPWiFi revA (henceforth simply “DPWiFi”) stands to become the highest performance (i.e., Rate-Range) and most robust (i.e., impairment-resilient) Wireless PHY ever devised
DPWiFi revA BER Performance in Impaired FWA Propagation Channels DPWiFi-32 MCS13 320 MHz vs Channel Depolarization, Rx Adaptation |  |  |  |  |  |  | 
Channel Impairment Depolarization Angle | None 0.0o | Mist 1.0o | Slight Fog 1.1o | Heavy Rain 5.0o | Foliage 10.0o | Med Reflection 25.0o | Lg Reflection 40.0o
Ch Depolarization Index | 0.5016 | 0.5087 | 0.5095 | 0.5417 | 0.5792 | 0.6645 | 0.7044
BER, No Adaptation | 0.000 | 0.000 | 0.003 | 0.196 | 0.275 | 0.384 | 0.450
BER, Adaptation | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000

## Slide 14
So, What’s Next Up? Hardware Validation!
Quick-turn Build a 92.2 Gbps PMX-32 DPWiFi Prototype
From 8x 11.5 Gbps SMX-4 WiFi-7 SoCs (QPC9274/ BCM67263/ MT7990)

## Slide 15
Summary and Conclusions
DPWiFi has proposed breakthrough MIMO Multiplexing multi-signal processing delivering 92 Gbps P2P data transport in a 320 MHz channel at 6 GHz, regardless of propagation impairments.
A 92 Gbps DPWiFi physical MATLAB model has fully simulation-validated the functionality and performance claimed above.
A contemplated WiFi-7 based 92 Gbps DPWiFi prototype will similarly hardware-validate DPWiFi by this year’s end.
DPWiFi remains without peer as a candidate TGbn PHY

## Slide 16: Appendix DPWiFi RevA MATLAB Simulation Results

## Slide 17
Case 1: DPWiFi-32 MCS13 320MHz / ψ = 0.0o / No Adaptation

## Slide 18
Case 2: DPWiFi-32 MCS13 320MHz / ψ = 1.0o / No Adaptation

## Slide 19
Case 3: DPWiFi-32 MCS13 320MHz / ψ = 1.1o / No Adaptation

## Slide 20
Case 4: DPWiFi-32 MCS13 320MHz / ψ = 1.1o / Adaptation

## Slide 21
Case 5: DPWiFi-32 MCS13 320MHz / ψ = 5.0o / No Adaptation

## Slide 22
Case 6: DPWiFi-32 MCS13 320MHz / ψ = 5.0o / Adaptation

## Slide 23
Case 7: DPWiFi-32 MCS13 320MHz / ψ = 10.0o / No Adaptation

## Slide 24
Case 8: DPWiFi-32 MCS13 320MHz / ψ = 10.0o / Adaptation

## Slide 25
Case 9: DPWiFi-32 MCS13 320MHz / ψ = 25.0o / No Adaptation

## Slide 26
Case 10: DPWiFi-32 MCS13 320MHz / ψ = 25.0o / Adaptation

## Slide 27
Case 11: DPWiFi-32 MCS13 320MHz / ψ = 40.0o / No Adaptation

## Slide 28
Case 12: DPWiFi-32 MCS13 320MHz / ψ = 40.0o / Adaptation

## Slide 29: References
1. 23/1606r1-UHRSG Dynamic Polarization Multiplexing and Beamforming WLANs Carlos A Rios (Terabit Wireless Internet), 13-Sep-2023
23/1756r3-TGbn MIMO Dynamic Polarization and Beamforming: Proposed IEEE802.11bn PHY Carlos A Rios (Terabit Wireless Internet), 16-Nov-2023
24/0041r12-TGbn DPWiFi MATLAB Validation Carlos A Rios (Terabit Wireless Internet), 02-Feb-2024
24/0440r6-TGbn DPWiFi for IEEE802.11bn WMANs Carlos A Rios (Terabit Wireless Internet), 22-Apr-2024