## Slide 1: DPWiFi revA
Date: 2024-09-23
Authors:

## Slide 2: Abstract
TGbn PHY candidate DPWiFi originally proposed in Nov ‘23, an improved radiowave polarization processing model incorporated June ‘24 unearthed a serious, latent flaw in the original Dynamic Polarization Propagation Channel formulation. Remedied, the updated “DPWiFi revA” TRX model plus corresponding MATLAB functional validation and performance characterization data, analyses and conclusions are presented herein.

## Slide 3
WiFi Static Polarization Operation
A WiFi Tx antenna “polarizes” by launching RF waveforms S in a precise spatial orientation per an “Orthogonal Polarization Baseline (OPB)”
Linearly Polarized PTX radiates along a fixed angle between 0o (H) or 90o (V)
PTX(S) = H or V, per the OPB
Typical terrestrial propagation “depolarizes” S by rotating PTX by a “depolarization angle” ψ
  LP waveforms propagate fixed-rotated by ψo from true OPB H-V
  PTX (S, ψ) = ψ or ψ + 90o
A WiFi Rx antenna “polarization-filters” detected waveforms into “Matched-Polarization (MP)” or “Mismatched-Polarization (MMP)” components
PRX (S, ψ) = H or V
MP (PTX (S,ψ)) = cosψ S(t)
MMP (PTX (S, ψ)) = sinψ S(t)

## Slide 4
DPWiFi Dynamic Polarization Operation
A DPWiFi Tx Antenna modulates waveform polarization by switching orthogonal antenna elements H and V per a binary sequence DPC
DPTX(S) = Tx DPC
Propagation depolarization rotates DPTX orthogonality baseline by ψ
DPTX (S, ψ) = Tx DPC(ψ)
A DPWiFi Rx Antenna polarization-filters DPTX into “Matched-DPC (MDPC)” or “Mismatched-DPC (MMDPC)” elements
DPRX(S) = Rx DPC
MDPC (S, ψ) = cosψ S(t)
MMDPC (S, ψ) = f(S(t), cosψ, sinψ)
MDPC S*(t)
MMDPC S*(t)

## Slide 5
DPWiFi revA TRX Model
  Given n WiFi-7 RF stream n-vectors [S], [S*] and [S’], and
  The ψ-depolarized Propagation Channel nxn matrix [HDP], and
  Walsh n-vectors [TxDPC] and [RxDPC] such that
[TxDPC] = [DPC1 DPC2 … DPCn] = [RxDPC], where
DPCi · DPCj = cosψ if i = j
DPCi · DPCj = (cosψ + sinψ)/2 if i ≠ j
    If [HDP] is Non-Singular there exists an [HDP-1]such that [S’] = [S] x [HDP] x [HDP-1]= [S]

## Slide 6
DPWiFi revA [HDP] Propagation Channel
  Walsh-modulated DPWiFi Polarization establishes that
  S*(t) = cosψ S(t) if Tx DPC = Rx DPC, or S*(t) = (cosψ + sinψ)/2 S(t) if Tx DPC ≠ Rx DPC
  Extending to the case of n Si and corresponding DPCi we obtain [S*] = [S] x [HDP], where
  Noting that for 0o < ψ < 45o
  0.50 ≤ (cosψ + sinψ)/2 ≤ 0.71 and 0.70 ≤ cosψ ≤ 1.00, we can therefore conclude
    The DPWiFi revA Propagation Channel [HDP] is Indeed Non-Singular

## Slide 7
DPWiFi revA [HDP-1] Rx MIMO Demultiplexer
Given:
Then:
Equivalently:
Given:
Then:
Equivalently:
    The DPWiFi revA MIMO Demultiplexer [HDP-1] is a Trivial Construct

## Slide 8
DPWiFi (rev-) vs DPWiFi (revA)
    DPWiFi rev- is just a Degenerate Manifestation of DPWiFi revA
    Note: DPWiFi rev- and DPWiFi revA are equivalent for ψ < 7.5o

## Slide 9
DPWiFi revA [HDP] MATLAB Operation
S1
S2
S32
S*1
S*2
S*32
[S]
[S*]

## Slide 10
DPWiFi revA MATLAB Representation: DPWiFiTRXv2
[S] [P] x [ψ] [P] x [HDP-1] = [S’]

## Slide 11
DPWiFiTRXv2 Processing
[S] [P] x [ψ] [P] x [HDP-1] = [S’]
[S] [HDP] x [HDP-1] = [S’] = [S]

## Slide 12
Representative DPWiFi revA MATLAB Simulation Results

## Slide 13
DPWiFi revA MATLAB Validation
(See Appendix A for full DPWiFiTRXv2 Control Panel/Visualization Window Screen Shots)
DPWiFiTRXv2 BER vs Channel Depolarization, Rx Adaptation |  |  |  |  | 
Case | Signal | MIMO Order | Channel ψ (o) | Rx Adaptation | BER
1 | MCS13 320 MHz | 32 | 0.0 | N | 0.00e0
2 | MCS13 320 MHz | 32 | 1.0 | N | 0.00e0
3 | MCS13 320 MHz | 32 | 1.1 | N | 3.84e-3
4 | MCS13 320 MHz | 32 | 1.1 | Y | 0.00e0
5 | MCS13 320 MHz | 32 | 5.0 | N | 1.96e-1
6 | MCS13 320 MHz | 32 | 5.0 | Y | 0.00e0
7 | MCS13 320 MHz | 32 | 10.0 | N | 2.75e-1
8 | MCS13 320 MHz | 32 | 10.0 | Y | 0.00e0
9 | MCS13 320 MHz | 32 | 25.0 | N | 3.84e-1
10 | MCS13 320 MHz | 32 | 25.0 | Y | 0.00e0
11 | MCS13 320 MHz | 32 | 40.0 | N | 4.50e-1
12 | MCS13 320 MHz | 32 | 40.0 | Y | 0.00e0

## Slide 14
DPWiFi revA MATLAB Validation Analysis
Salient Observations
Key Assessments
  DPWiFi is extraordinarily sensitive to propagation channel depolarization Absent receiver adaptation, even a slight morning mist would irremediably crash a DPWiFi link
  Rx Adaptation, however, comprehensively mitigates any amount of such depolarization
Fundamental Conclusions DPWiFi revA (henceforth simply “DPWiFi”) stands to become the fastest (Rate), farthest (Range) and toughest (Impairment-impervious) Wireless PHY ever devised
DPWiFi revA BER Performance in Impaired FWA Propagation Channels DPWiFi-32 MCS13 320 MHz vs Channel Depolarization, Rx Adaptation |  |  |  |  |  |  | 
Channel Impairment Depolarization Angle | None 0.2o | Mist 1.0o | Slight Fog 1.1o | Heavy Rain 5.0o | Foliage 10.0o | Grz Reflection 25.0o | Orth Reflection 40.0o
Ch Depolarization Index | 0.5016 | 0.5087 | 0.5095 | 0.5417 | 0.5792 | 0.6645 | 0.7044
BER, No Adaptation | 0.000 | 0.000 | 0.003 | 0.196 | 0.275 | 0.384 | 0.450
BER, Adaptation | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000

## Slide 15
So, What Next? Hardware Validation!
Quick-turn DPWiFi Prototype
8x 11.5 Gbps SMX-4 WiFi-7s 1x 92. 2 Gbps PMX-32 DPWiFi

## Slide 16
Summary and Conclusions
TGbn PHY candidate DPWiFi proposes breakthrough Polarization MIMO Multiplexing providing 92 Gbps P2P data transport within 320 MHz at 6 GHz, regardless of propagation channel impairments.
A MATLAB model has fully simulation-validated the above-claimed DPWiFi functionality and performance.
A WiFi-7 based prototype will attempt to correspondingly hardware-validate DPWiFi by this year’s end.
DPWiFi remains without peer as a candidate TGbn PHY

## Slide 17: Appendix DPWiFi RevA MATLAB Simulation Results

## Slide 18
Case 1: DPWiFi-32 MCS13 320MHz / ψ = 0.0o / No Adaptation

## Slide 19
Case 2: DPWiFi-32 MCS13 320MHz / ψ = 1.0o / No Adaptation

## Slide 20
Case 3: DPWiFi-32 MCS13 320MHz / ψ = 1.1o / No Adaptation

## Slide 21
Case 4: DPWiFi-32 MCS13 320MHz / ψ = 1.1o / Adaptation

## Slide 22
Case 5: DPWiFi-32 MCS13 320MHz / ψ = 5.0o / No Adaptation

## Slide 23
Case 6: DPWiFi-32 MCS13 320MHz / ψ = 5.0o / Adaptation

## Slide 24
Case 7: DPWiFi-32 MCS13 320MHz / ψ = 10.0o / No Adaptation

## Slide 25
Case 8: DPWiFi-32 MCS13 320MHz / ψ = 10.0o / Adaptation

## Slide 26
Case 9: DPWiFi-32 MCS13 320MHz / ψ = 25.0o / No Adaptation

## Slide 27
Case 10: DPWiFi-32 MCS13 320MHz / ψ = 25.0o / Adaptation

## Slide 28
Case 11: DPWiFi-32 MCS13 320MHz / ψ = 40.0o / No Adaptation

## Slide 29
Case 12: DPWiFi-32 MCS13 320MHz / ψ = 40.0o / Adaptation

## Slide 30: References
1. 23/1606r1-UHRSG Dynamic Polarization Multiplexing and Beamforming WLANs Carlos A Rios (Terabit Wireless Internet), 13-Sep-2023
23/1756r3-TGbn MIMO Dynamic Polarization and Beamforming: Proposed IEEE802.11bn PHY Carlos A Rios (Terabit Wireless Internet), 16-Nov-2023
24/0041r12-TGbn DPWiFi MATLAB Validation Carlos A Rios (Terabit Wireless Internet), 02-Feb-2024
24/0440r6-TGbn DPWiFi for IEEE802.11bn WMANs Carlos A Rios (Terabit Wireless Internet), 22-Apr-2024