## Slide 1: A Flexible Extension Structure
Date: 2024-09-09
Authors:

## Slide 2: Abstract
Some proposals are reusing existing frame/field/element to support different function, such as coexistence, power save, NPCA, DSO [1-4]
  Some frame/field/element does not have enough reserved bits
  Need careful consideration of each function’s priority to decide which reserved bits to use
Some proposals are reusing AID12 for different purposes [4-6]
  Some frame/field/element does not have the AID12 subfield
  May have limited flexibility to add new information: need to follow the pre-determined length and need to avoid conflict/ambiguity issues
This submission presents a flexible extension structure
  One bit in existing field or UHR field for Extension Indication to support multiple functions
  Can also support optional functions or support new functions for future 802.11 generations

## Slide 3: Proposal: A Flexible Extension Structure
The Extension Indication subfield indicates the presence of Length and Extension Context.
When Extension Indication is 0: the Length and Extension Context subfields are not present.
When Extension Indication is 1:
  STAs that do not understand or do not need the Extension Context can skip it by the Length subfield.
  STAs that understand the Extension Context can process it and take actions accordingly.
The Length subfield indicates the number of octets in the Extension Context subfield.
It may support different functions for 802.11bn and new functions for future 802.11 generations.
 | Extensible field/subfield | Extension Indication
Bits: | Certain length | 1
Present in extensible field/subfield
Present if Extension Indication subfield is 1
Length | Extension Context
0 or TBD | variable

## Slide 4: Comparison with Information Elements (1/2)
The proposed extension structure is similar to Information Elements.
The proposed structure
IEEE 802.11-2020 [7]
 | Extensible field/subfield | Extension Indication
Bits: | Certain length | 1
Present in extensible field/subfield
Present if Extension Indication subfield is 1
Length | Extension Context
0 or TBD | variable

## Slide 5: Comparison with Information Elements (2/2)
The proposed structure is not limited to management frames; can be used for any field/subfield of MAC header of any frame. May also work for certain PPDU fields in PHY header.
  E.g., if certain PPDU field has no difference between two generations, the Extension Indication is 0. Otherwise the Extension Indication is 1, followed by the Extension Context for the new generation.
Simple change with low overhead (as low as 1 bit)
Closely coupled with the specific field/subfield that is to be extended, which can be more efficient and effective for legacy STAs, UHR STAs and future generation STAs
Element ID is not needed and no need to occupy the Element ID or Element ID Extension space, although ID/type/version information can be included in the Extension Context
  If Extension Indication is 1, The Extension Context can be ignored by certain STAs that do not understand or do not need the Extension Context
No need to follow the relative Order, check the capability for the presence of each Element, and try to match the Element ID to process each Element

## Slide 6: Options for Multiple, Optional and Future Functions
Extend existing field to support multiple functions
  Extension Indication: reuse 1 bit in the existing field (reserved bits or multi-purpose bits). Set to false to disable Extension Context (baseline), set to true to support extended functions.
  Extension Context: ID/type information to identify different functions; Extension Context can also contain Extension Indication to be extended further in the future if needed.
  If the existing field has a subfield with variable length that can be matched with the Length subfield, the Extension Context can be appended right after the existing field. Otherwise, the Extension Context can be appended at the end of the MAC header.
Define new field to support optional functions and new functions in the future
  Extension Indication: 1 bit in 802.11bn fields for optional/future extensions. Set to false for basic 802.11bn functions, set to true for optional 802.11bn functions or for new functions for future 802.11 generations.
  Extension Context: present if optional or post-802.11bn functions are enabled.

## Slide 7: Options for Unicast and Broadcast/Multicast Frames
For unicast frames, STAs that understand the Extension Indication (for UHR and post-UHR STAs) can process or ignore the Extension Context. Do not send unicast frames with Extension Indication = 1 to legacy STAs, unless legacy STAs can skip the Extension Context properly.
For broadcast/multicast frames,
  For Management frames,
    Use certain reserved Element IDs, so legacy STAs can skip the Information field of the Element
  For Control frames,
    Use certain reserved type/subtype/AID values, so legacy STAs can skip the information/context associated with the type/subtype/AID
  For Data frames,
    Use certain reserved Control ID values of the A-Control subfield, so legacy STAs can skip the Control Information of the A-Control subfield
  If legacy STAs cannot skip the Extension Context properly, do not send broadcast/multicast frames with Extension Indication = 1 to legacy STAs.

## Slide 8: Options for Frame Format
Location of Extension Indication subfield
  At the end of the extensible field
  Anywhere of the extensible field that is unused/reserved/multi-purpose
Location of Length subfield and Extension Context subfield
  Right after the extensible field
  A dedicated part (e.g., at the end of MAC header) for a list of Length + Extension Context subfields, following the same order as the extensible fields
Content of Extension Indication subfield
  One bit in a extensible field
    For existing field/subfield: reuse reserved bit, or reuse certain multi-purpose subfield value
    For new field/subfield: define a dedicated bit for Extension Indication
  May have one bit to indicate whether a field is extensible or not
Content of Extension Context subfield: TBD. Size of Length subfield: one octet or TBD

## Slide 9: Examples (1/3)
Example 1: Extension Indication at the end of the extensible field, followed by Length and Extension Context
Example 2: Extension Indication at the middle of the extensible field, followed by Length and Extension Context
Example 3: Extension Indication at the middle of the extensible field, followed by other field(s) and then followed by Length and Extension Context
Example 1
Example 2
Example 3

## Slide 10: Examples (2/3)
Example 4: two extensible fields, each followed by Length and Extension Context, and with other field(s) between them
Example 5: two extensible fields, followed by other field(s), and then Length and Extension Context
Example 6: mix of example 4 and example 5
Example 5
Example 6
Example 4

## Slide 11: Examples (3/3)
Example 7: concatenated and continuous Extension Context subfields with no other field in between, and the first level of Length subfield indicates the overall length of two levels of Extension Context
Example 8: concatenated and continuous Extension Context subfields with no other field in between, and the Length subfield of each level indicates the length of each level of Extension Context separately
Example 9: concatenated and non-continuous Extension Context subfields with other field(s) in between, and the Length subfield of each level indicates the length of each level of Extension Context separately
Example 9
Example 7
Example 8

## Slide 12: Conclusion
This submission presents a flexible extension structure with Extension Indication, Length, and Extension Context subfields
  It can be used to extend existing fields to support multiple functions
  It can be used in extensible fields to support optional functions
  It can be used in extensible fields to support new functions for future 802.11 generations

## Slide 13: References
[1] 802.11-24/1126r1, ICF-ICR Discussion for DPS, GeonHwan Kim
[2] 802.11-24/0504r0, Considerations of A Unified Initial Control Frame Design, Hanqing Lou
[3] 802.11-24/0505r0, Considerations of Transmissions of Initial Control Response frames, Hanqing Lou
[4] 802.11-24/0857r0, ICR consideration, Liwen Chu
[5] 802.11-24/1129r1, Discussion on Intermediate FCS Signaling, SunHee Baek
[6] 802.11-24/1179r0, Trigger frame expansion, Vishnu Ratnam
[7] IEEE Std 802.11-2020

## Slide 14: Straw Polls
SP1: Do you support defining a mechanism in TGbn to allow a field to be extended?
An extensible field is similar to an (extensible) Information Element, but not limited to management frame
Signaling for the indication is TBD, e.g., by capability bits or reserved subfields/values
Naming and procedures for the mechanism are TBD
Results: Yes: , No: , Abstain:

## Slide 15: Straw Polls
SP2: Do you support defining a mechanism in TGbn to indicate whether a field is extended?
If a field is extended, it is followed by a length subfield and an extension context subfield
Exact location and context of extension indication, length subfield and extension context subfield are TBD
Naming and procedures for the mechanism are TBD
Results: Yes: , No: , Abstain: