## Slide 1: Framework of Multi-AP
Date: 2024-09-05
Authors:

## Slide 2: Introduction
11bn PAR defines performance improvement through cooperation between neighbor APs, and many contributions related to Multi-AP are presented for this purpose
Through Multi-AP operation, we can improve support for low latency traffic as well as spectral efficiency in OBSS environment

## Slide 3: Multi-AP Environment
It is obvious that the multi-AP function will operate more easily in the enterprise environment when we consider coordination, synchronization, and information sharing between APs
However, according to the log of Galaxy A/S series, more than 70% of traffic occurs in the residential environment
And considering the long replacement cycle of Wi-Fi APs, this ratio will not change much in the future
In order for the multi-AP function of 11bn to be widely implemented, it must be defined in the standard to support both the enterprise environment and the residential environment

## Slide 4: Multi-AP Tech Items
In order to design Multi-AP, the following items must be discussed
  Coordination between APs
  Information sharing between APs
  Frame exchange sequence
  PPDU/Frame format
  NAV Protection
  Multi-AP TX scheme
  Harmonization between M-AP functions
  Performance evaluation
This submission focuses on the coordination process between APs

## Slide 5
AP 1
AP n
Initial Setup
Long-term Coordination
Short-term Coordination
Multi-AP TX
…
…
Long-term Coordination
…
…
 | Explanation | Enterprise Environment | Residential Environment
Initial Setup | - Proximity check(Discovery) and capability information exchange between APs | - Managed by the controller - Both Over-the-DS & Over-the-air are all possible - Since the same vendor is likely to install, it can be implemented with minimal standards and vendor-specific protocol | - No controller - Only simple information exchange may be possible (OTA) - Standards for compatibility between vendors are required
Long-term Coordination | - Multi-AP set management - Performing channel sounding - Mass exchange of information between APs - Periodic (over-the-air) |  | 
Short-term Coordination | - Multi-AP TX scheme determination - Synchronization - Buffer/traffic information exchange - Aperiodic |  | 
Multi-AP TX | - TXOP aquisition/sharing - C-TDMA, C-R-TWT, C-SR, C-SN, C-BF, JT, C-OFDMA, etc. | - Most of the proposed schemes are possible | - Available schemes may be limited due to privacy issues
AP 2

## Slide 6: Scope of standard
The coordination process through over-the-DS may be TBD in 11bn scope
The coordination process through over-the-air is clearly 11bn scope, but the Multi-AP TX schemes are so diverse that it may be difficult to combine into one protocol, and there is no agreement at 11bn yet
  SFD will have to find a minimum agreement, and it is suggested to start with supporting all possible use cases/environments
  Also I think we should start with a simple protocol design for essential parts of coordination procedure (e.g. discovery, information sharing, negotiation, etc…)

## Slide 7: Conclusion
This submission pointed out that the Residential Environment should be considered for Multi-AP transmission
And we addressed the detail of coordination procedure for multi-AP

## Slide 8: Straw poll 1
Do you agree to consider the residential environment as the use case of Multi-AP?

## Slide 9: Straw poll 2
Which of the following multi-AP transmission schemes would you prefer for residential environment?
O1) C-TDMA
O2) C-R-TWT
O3) C-SR
O4) C-SN/C-BF/JT
O5) C-OFDMA