## Slide 1: Discussion on ultra-low power timing clock
Date: 2024-09-03
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com
Wangke |  |  |  | 
Shengjiang Cui |  |  |  | 
Chuanfeng He |  |  |  | 
Jinyu Zhang |  |  |  | 
Zhisong Zuo |  |  |  | 
Doc.: IEEE 802.11-24/1475r0
Sept. 2024

## Slide 2: Abstract
In this submission, we firstly discuss the necessity of maintaining of timing clock by AMP device. Then we present the feasibility of implementing ultra-low power timing clock in AMP device(AMP STA). In the end, we propose the timing requirement.
Doc.: IEEE 802.11-24/1475r0

## Slide 3
In[1], device capabilities of AMP client STA have been discussed, and we propose the following:
Weijie Xu (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1475r0
Sept. 2024
Use case | Short/Medium range AMP IoT |  | Close range AMP IoT | Compatible AMP IoT (i.e. 11n compatible)
UL Transmitter | Active Tx | Backscattering | Backscattering | Legacy OFDM Tx
UL Amplifier | Y(May) | Y (Reflection) | N | Y(Legacy)
DL Amplifier | Y(May) | Y(May) | N | Y(Legacy)
RF ED Rx：Sens. of ~-40dB | Y(Opt 1) | Y(Opt1) | Y | Y for wake-up
(Zero-) IF Rx: sens. of ~-70dB | Y(Opt 2) | Y(Opt2) | N | OFDM receiver after wake-up
Energy storage | Y | Y | N | Y
Clock accuracy | IF Rx and UL:<10^3 ppm RF ED :10^4~10^5 ppm |  | 10^4~10^5 ppm | <10^3 ppm for WUR ~20ppm for MR
Waveform | DL: MC-OOK UL:OOK as baseline, consider BPSK/MSK |  |  | MC-OOK for wake-up, then OFDM
Power consumption | 100X µW | 100X µW | X µW | X mW~10X mW
Background(1)

## Slide 4
Background(2)
Weijie Xu (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1475r0
Sept. 2024
  In[1], on how to achieve the design target: AMP IoT should aim for the use cases that can’t fully addressed by existing technologies, the following considerations are proposed to differentiate Ambient IoT with existing technologies (e.g., RFID):
    Potential longer range, via using
      Advanced techniques such as reflection amplifier, spreading, UL coding etc.
      Energy storage ( which help can lower energy harvesting threshold)
      Other kinds of ambient power such as light, heat etc.
      Higher sensitivity receiver (with different receiver Arch.)
    Potential higher system capacity/system efficiency
      Techniques such as FDM/CDM
      Higher peak data rate?
    Lower deployment cost
      Low-complexity AMP AP (e.g. by avoiding full-duplex operation)
    Enable more application, e.g. can link ambient IoT device with a smart phone

## Slide 5
Weijie Xu (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1475r0
Sept. 2024
  In [2], the operation state and operation procedure of AMP device is discussed. One promising mode is as in below:
    Note that in this mode, AMP device can only perform Rx/Tx in duty-cycle, it is reasonable because: instant harvested power will be very limited thus it can’t support always-on operation. However, there may scheduling delay due to lots of devices in queue.
      This will be different from RFID
Background(3)

## Slide 6
Weijie Xu (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1475r0
Sept. 2024
  In RFID, slot-aloha is used as the access procedure.
    RFID device is always on to monitor and decode the query signaling.
      It is feasible because of short working distance.
    The access timing is fully provided by the interrogator
      RFID device determines whether to access based on the its random number and the control of Query/QueryRep
      Figure: slot-Aloha in RFID[6]
Background(4)

## Slide 7
Discussion
Weijie Xu (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1475r0
Sept. 2024
  Based on previous slides, it can be seen that AMP device needs to maintain a timing clock during its operation procedure. Since,
    It is essential for power saving with duty-cycle operation, in order to store harvested power in case of longer operation distance
    It is essential to enable AMP IoT to work normally
    In sensor use case, the AMP device shall be able to report data periodically
  Besides duty-cycle operation, it can be expected there are also many other aspects, e.g., multiple access, scheduling timing etc., may require the AMP device to maintain a timing clock.
  The above requirements apply to both AMP device supporting active transmission and AMP device supporting backscattering.
  Therefore, we will further discuss the requirement of timing clock for AMP device.

## Slide 8
Influence of the timing accuracy
Weijie Xu (OPPO)
Slide 8
Doc.: IEEE 802.11-24/1475r0
Sep 2024
  Relaxed clock accuracy is necessary. However, too low clock accuracy, e.g., 10^5 ppm will result in poor system performance.
    Example 1: influence on duty-cycle operation
      In duty-cycle operation, AMP device finds its operation time window based on its timing clock. Timing error results in earlier wake-up for signaling Rx.
      Assuming the operation cycle is 100ms, 10^5 ppm means there will be a drifting of 10ms every 100ms, it requires increased Rx of more than 10ms
    Example 2:influence on multiple access
      If device can maintain a timing clock, it will ease TDM and improve the system efficiency. However, poor timing accuracy results in mutual-interference among TDMed transmissions (from different devices)

## Slide 9
Proposed requirements for timing
Weijie Xu (OPPO)
Slide 9
Doc.: IEEE 802.11-24/1475r0
Sept. 2024
  Relaxed clock accuracy is necessary (to reduce the complexity and power consumption) and feasible. However, considering the issues of poor timing accuracy, there shall be a proper compromise.
  In [1], the following requirements are proposed.
  In above table, it give the initial clock requirements(i.e. initial SFO) during Rx and Tx.
  For timing, we further propose a requirement of timing clock accuracy: 10^3 ppm~10^4 ppm for AMP device supporting active transmission or long range backscattering.
    For close range AMP IoT, it seems fine to reuse RFID requirement since it is peer-to-peer communication

## Slide 10
Feasibility analysis
Weijie Xu (OPPO)
Slide 10
Doc.: IEEE 802.11-24/1475r0
Sept. 2024
  For AMP device, the key factors need to be considered in order to support a timing clock are its complexity and power consumption
  Based on our investigation[3][4][5], with not so much increase of device complexity, ultra-low power RTC clock of 10^3ppm~ 10^4ppm (table bottom-right) is achievable.
    Power consumption of clock circuit can be as low as several Nano-Walt
    The RTC clock can be crystal or crystal-less(i.e. silicon-based)
    Temperature variation is the main challenge for the circuit. It may has temperature compensation (Figure: Bottom-left).

## Slide 11
Summary and proposal
  In this submission, we discuss the necessity, feasibility and requirement of having a timing clock for AMP device .
  We have the following proposal:
    Propose to a requirement of timing clock accuracy: 10^3 ppm~10^4 ppm for AMP device supporting active transmission or long range backscattering
Weijie Xu (OPPO)
Slide 11
Doc.: IEEE 802.11-24/1475r0
Sept. 2024

## Slide 12: Reference
IEEE 802.11-24/0853r0 Design target and device capabilities for AMP IoT
IEEE 802.11-24/0826r0, Energy balance of the state-based AMP station
D. Yoon, T. Jang, D. Sylvester and D. Blaauw, "A 5.58 nW Crystal Oscillator Using Pulsed Driver for Real-Time Clocks," in IEEE Journal of Solid-State Circuits, vol. 51, no. 2, pp. 509-522, Feb. 2016, doi: 10.1109/JSSC.2015.2501982.
Y. Lee, B. Giridhar, Z. Foo, D. Sylvester and D. Blaauw, "A 660pW multi-stage temperature-compensated timer for ultra-low-power wireless sensor node synchronization," 2011 IEEE International Solid-State Circuits Conference, San Francisco, CA, USA, 2011, pp. 46-48, doi: 10.1109/ISSCC.2011.5746213.
Y. Lin et al., "A 150pW Program-and-Hold Timer for Ultra-Low-Power Sensor Platforms", ISSCC Dig. Tech. Papers, pp. 326-327, Feb. 2009
RFID_gs1-epc-gen2v2-uhf-airinterface
Doc.: IEEE 802.11-24/1475r0
Sept. 2024