## Slide 1
Operating Channel Validation(OCV) in NPCA
Name | Affiliations | Address | Phone | Email
Jay Yang | ZTE |  |  | yang.zhijie@zte.com.cn
Yun Li |  |  |  | 
Yaodong Zhang |  |  |  | 
Date: 2024-09-03
Authors:

## Slide 2: Recap:NPCA
  TGbn has agreed to define NPCA feature
    TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
      The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
      A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.

## Slide 3: Recap: Operating Channel Validation(OCV)
To prevent from MC-MitM attacking, OCV feature was defined in the baseline via including the OCI(Operating Channel Information) element:
  E.g., OCI element is included in EAPOL-2/3,reassociation request/response,SA query request/response,WNM sleep mode request/response frame,etc.
  The receiver will compare the OCI element and the primary channel where the PPDU is received.
  If a mismatch issue occurs, the STA can infer the surrounding MC-MitM attacker, and then it may abort the current procedure .

## Slide 4
The operating channel mismatch issue in NPCA
The current OCI only contain the primary channel(PC) number
  But the actually frame transmitted channel can be either primary channel or NPCA-P channel.
  If the frame including OCI element is (re)transmitted on NPCA channel, it will cause the channel mismatch issue when STA compares the PC in OCI and the PPDU receiving channel.
The quoted baseline text is as bellow:
Jay Yang, et al. (ZTE)

## Slide 5: Motivation
In this contribution, we would like to discuss two possible solutions to address the mismatch issue mentioned above.

## Slide 6: Option 1:define the restrictive rule
The frames containing OCI are only allowed to be (re)transmitted on the primary channel.
  Pros. No change requirement on the current OCI element.
  Cons. It requires the implementation to identify each frame to check OCI element before (re)transmission on NPCA. It may bring additional processing delay issue.(e.g. the transmitter has to wait on the primary channel if it intends to send the frame including OCI in OBSS senario.)
Jay Yang, et al. (ZTE)

## Slide 7: Option2: add NPCA-P validation function
Allow the PPDU to include both PC and NPCA-P in an extended OCI once NPCA is enabled.
  The receiver may verify the PC when operating on the original channel, and the receiver may verify the NPCA-P when operating on NPCA channel.
  An alternative approach is to contain two OCI elements in one frame.
Jay Yang, et al. (ZTE)

## Slide 8: Summary
Analyze the mismatch issue when OCI is present in NPCA scenario
Propose two options:
  Opt1:
    Define restrictive rules
  Opt2:
    Adding NPCA-P validation via a new OCI element or including two OCI elements
Jay Yang, et al. (ZTE)

## Slide 9
THANK YOU
Jay Yang, et al. (ZTE)

## Slide 10: Reference
[1] Multi-Channel Man-in-the-Middle Attacks Against Protected Wi-Fi Networks: A State
of the Art Review
[2] 24/209r4 Specification Framework for TGbn
Jay Yang, et al. (ZTE)

## Slide 11: SP1
Do you agree to define a mechanism to address the operating channel mismatch issue when OCI element is present in a PPDU in NPCA scenario?

## Slide 12: Appendix:Multi-Channel Man-in-the-Middle Attacks
  The attacker performs the following procedures to obtain a MC-MitM position[1]:
    Force the STA to switch to rogue channels(e.g.,jam channel A and transmit copied Beacons on channel B to trick client, or using channel switch announcements CSA).
    Rogue AP collects authentication request from the STA on channel B and retransmit it to real AP on channel A.Rogue client collects authentication response from real AP on channel A and retransmit it to client on channel B.In the same way,association frames are exchanged.
    After successful association, rogue STA and rogue AP collects each 4-way handshake message from its originating channel and retransmit it on another channel.As a result, the STA and real AP derive a new PTK.
    Then the attacker can manage all the communication between end devices,so that he can reliably block, delay, buffer, modify, inject, or replay encrypted wireless frames.
Jay Yang, et al. (ZTE)