## Slide 1: ELR PPDU Transmission Design
Date: 2024-09-06
Authors:
Name | Affiliations | Address | Phone | Email
Shengquan Hu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | Shengquan.hu@mediatek.com
Jianhan Liu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
Enhanced Long Range (ELR) for UHR was proposed in contribution [1] to address the link budge/coverage range imbalance issues between DL & UL, which are caused by the difference Tx power and number of antennas at AP and STA
Contribution [2] discussed the ELR design targets in term of PHY data rates, coverage range improvement comparing to 11g, e.g.:
  PHY rate: ~1.5Mbps and ~3.0Mbps
  Range: ~6dB and 3dB range better than 11g
In this contribution, we will propose data portion transmission methods for ELR PPDU

## Slide 3: General Consideration of ELR Data Transmission
Meet ELR design target:
  Data rate: e.g. ~1.5Mbps and ~3.0Mbps
  Close the UL/DL coverage range gap (e.g. ~6dB range improvement vs 11g)
Simple for implementation
Reuse existing designs as much as possible
Minimize the efforts for spec changes/modifications
Avoid unnecessary complexity such as new coding, new numerology etc
Simple for signaling

## Slide 4: Studies for ELR Data Symbol Transmission
Several design candidates/options have been studied, evaluated and compared, such as:
  Using DRU (e.g. 26-tone or 52-tone DRU on BW20) as a narrowband transmission
  Symbol Repetition in Time Domain to achieve combining gain
  Coded Bits duplication to achieve effective low coding rate
  Tone repetition in frequency domain to achieve frequency diversity and combining gain
Above design options have some potential issues such as:
  Implementation complexity concerns
  Performance disadvantage
  Specification efforts
  New numerology
In this contribution, we propose a method of ELR payload transmission by using 52-tone RRU with 4 times duplication in frequency domain (RRU52 4x DUP)

## Slide 5: RRU52 4x DUP for ELR PPDU
52
52
52
52
13
13
DUP
DUP
DUP
RRU52 4x DUP
RRU52 based encoding/mod
Frequency duplication (DUP) has been used in several places in 11ax/be for better reliability:
  HE-SIG-A/B/U-SIG/EHT-SIG per-20MHz subchannel DUP (e.g. 2x/4x/8x DUP, etc)
  MCS14 is RU484 2x DUP, RU996 2x DUP etc in 11be
RRU52 4x DUP has the similarity with existing DUP modes, and it is just simply to extend to RRU52 with 4x DUP
RRU52 4x DUP is the simplest way to achieve ELR design target and the closest to what we have in existing designs:
  No new numerology
  Using existing MCS0 and MCS1
  Achieve design target with good margin
  Less efforts for spec changes
  Simple for implementation by reusing most of existing designs

## Slide 6: MCS and Data Rates for ELR PPDU
ELR-MCS | Duplication | Modulation | R | Nbpscs | Nsd | Ncbps | Ndbps | Data rate (Mb/s) |  | 
 |  |  |  |  |  |  |  | 0.8us GI | 1.6us GI | 3.2us GI
0 | RRU52 4x DUP | BPSK | 1/2 | 1 | 48 | 48 | 24 | 1.76 | 1.67 | 1.50
1 | RRU52 4x DUP | QPSK | 1/2 | 2 | 48 | 96 | 48 | 3.53 | 3.33 | 3.00
The following MCSs and data rates are proposed for ELR PPDU
    Simple for signaling and specification
    Good performance
    Reuse most of existing designs
meet design target

## Slide 7: PER Performance Simulations
ELR/UL vs 11g/DL: 4 antennas at AP; 2 antennas at STA
  ~ 11dB gain for 1.67Mbps
  > 8.0dB gain for 3.33Mbps
ELR/UL vs 11g/DL: 1 antennas at AP; 1 antennas at STA
  > 8.0dB gain for 1.67Mbps
  > 5.0dB gain for 3.33Mbps
Simulation Settings:
  11g/DL vs ELR/UL;
  1T1R1SS (i.e. 1x1x1); 2T4R1SS(i.e. 2x4x1, 2T@STA, 4R@AP for ELR/UL)
  D-NLOS, LDPC, MCS0/1, 256Byte packet
  2x LTF mode with two ELR-LTF symbols with 3dB power boost, estimated channel with smoothing
1x1x1
2x4x1

## Slide 8: PAPR Reduction for RRU52 4x DUP
RRU52 with 4x DUP has higher PAPR without applying PAPR reduction mask
We propose the following simple PAPR reduction method which can reduces PAPR significantly
  Splitting 2 segments (lower half & upper half) for each RRU52, each segment has 24 data subcarriers
  Total 8 segments for four RRU52
  the ELR data transmission shall apply the phase rotations as below for both BPSK and QPSK modulations:
52
52
52
52
13
13
DUP
DUP
DUP
RRU52 4x DUP
RRU52 based encoding/mod
1 1 1 1 -1 1 1 -1
RU1
RU2
RU3
RU4
lower half of data tones on RU3 is rotated by “-1”
upper half of data tones on RU4 is rotated by “-1”
  The rotation of -1 will be applied on data subcarriers of lower half of RU3 and upper half of RU4 for 52-tone regular RU (RRU52) on 20MHz

## Slide 9: PAPR Performance with Proposed PAPR Reduction Mask
PAPR of RRU52 4x DUP can be significantly reduced by applying proposed simple PAPR reduction mask
The PAPR performance in the following plots are simulated for both BPSK & QPSK with 50,000 OFDM symbols
BPSK
QPSK

## Slide 10: Summary
RRU52 with 4x DUP was proposed in this contribution for ELR data transmission:
  Simple for implementation
  Reuse most of existing designs
  Meet design target
  Simple for signaling
  Minimal efforts for spec changes/modifications
A simple PAPR reduction method also proposed for RRU52 4x DUP

## Slide 11: Reference
[1] 11-22-1928-01-0uhr-enhanced-long-range-usage-scenarios-design-target-and-feasibility
[2] 11-24-0873-02-00bn-design-targets-and-considerations-for-enhanced-long-range

## Slide 12: Straw Poll #1
Do you agree to include the following text to the 11bn SFD?
  ELR transmission schemes use RRU52 with four times duplication in frequency domain in 20MHz

## Slide 13: Straw Poll #2
Do you agree to include the following text to the 11bn SFD?
  ELR PPDU only supports the following two modulation and coding schemes:
    - BPSK with coding rate R=1/2
    - QPSK with coding rate R=1/2

## Slide 14: Straw Poll #3
Do you agree to include the following text to the 11bn SFD?
  ELR transmission shall apply the phase rotations as below for both BPSK and QPSK modulations
  The rotation of -1 will be applied on data subcarriers of lower half of RU3 and upper half of RU4 for 52-tone regular RU (RRU52) on 20MHz

## Slide 15: Straw Poll #4
  Do you agree to include the following text to the 11bn SFD?
  Pilot values and mapping rules of ELR-SIG and Data symbols in ELR PPDU are the same as that of four RRU52 in DL OFDMA