## Slide 1: More Consideration of ICR/CRF for in-device-coexistence
Date: 2024-11-13
Authors:
Name | Affiliation | Address | Phone | Email
Hongwon Lee | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hongwon.lee@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St, San Diego CA 92131 , USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
The Motion related to defining mechanism for a non-AP STA to report unavailability at TXOP level, which is related to aperiodic in-device-coexistence(IDC) signaling, was passed in July F2F meeting
Enhancing Multi-STA BA(M-BA) is one of the good options for ICR/CRF to perform aperiodic IDC signaling due to it’s flexibility [1]~[5]
We believe that M-BA with in-device coexistence is option not only for ICR but also CRF. We are considering additional options for ICR and/or CRF in various use cases
This contribution discusses several options for ICR/CRF in multiple use cases

## Slide 3: Recap: ICR Considerations [1]
In terms of Multi-STA BA, it should be carefully designed due to AID TID Info
  Depending on values of AID TID Info field, Per AID TID Info length is determined
  Therefore, we can use a special AID (e.g., 2007) while keeping existing values of TID/Ack type fields that will determine a container size including IDC Info (e.g., 2 octets + 4 octets)
    If we consider SU only, TID/Ack type can have other special values
    Different control information as well as IDC Info could be delivered if we generalize it
Allow a frame including one or more Control Info(s) (e.g., Action frame, BA)
    E.g., By having an Action frame for Control Info in response to BSRP TF, the Action frame can include BSR in A-control and other control info(s) in Body

## Slide 4: Recap: ICR Frame Choice [2]
By reviewing the structure of the existing control frames, Multi-STA BA (M-BA) is seen to be the best candidate frame:
  Includes the “Per AID TID Info” field which have plenty of room in replacement of the BA bitmap information.
  Very flexible with capability to include multiple “Per AID TID Info” fields each having a variable size “BA Bitmap” subfield.
  An already existing frame.

## Slide 5: More consideration of ICR for in-device-coexistence
Some Trigger frame such as BSRP can be ICF, and M-BA or new Action frame can be ICR to report unavailability
We need to consider including the Trigger frame response(e.g. BSR) and unavailability information (IDC Info) together in some cases
There are several options for including response information(e.g. BSRP + BSR and/or IDC Info) in M-BA
  Option 1: new Ack Type + TID combination in AID TID Info + Fragment Number
    It is applicable only to UHR devices and is not backward compatible (SU Only)
  Option 2: Special AID value in AID TID Info + Fragment Number (Preferred)
    It can be used with both UHR and legacy devices in multi-user case (SU and MU)
New Action frame can be one option of ICR
  Option 3: New Action frame with A-Control to include control information and IDC Info together
    It is applicable only to UHR devices and is not backward compatible (SU Only)
    This option cannot be used in the specific case(e.g. BlockAck response)
    The size of an Action frame may be larger than the size of a Control frame (30 octets + IDC Info vs 20 octets + Control Information(e.g. BSR) + IDC Info)
√

## Slide 6: Option 1 (M-BA with Ack Type / TID)
AID TID Info
  AID11 – not changed, Ack Type / TID – new values (e.g. 0 / 14)
  This option cannot cover legacy devices because they do not understand new Ack Type + TID combination. As a result, legacy devices do not recognize whether Block Ack Starting Sequence Control and Block Ack Bitmap are present or not)

## Slide 7: Option 2 (M-BA with AID11)
AID TID Info
  AID11 – Special value (e.g. 2046)
  Ack Type / TID – Existing value (e.g. 0 / 0 - Block Ack Starting Sequence Control subfield and Block Ack Bitmap subfields are present)
  The size of the AID TID info can be determined by the Fragment Number subfield in the Block Ack Starting Sequence Control subfield(up to 128 octets)
  This option can be used with both UHR and legacy devices in multi-user case
…..

## Slide 8: Multiple Control Info example in the case Option 2
How to include one or more Control information in the example below
  The AID11 subfield in the AID TID info is set to 2046
  The Fragment Number subfield is set to ‘0 0 0 0’ to indicate that the size of the Block Ack Bitmap as 8 octets
  Control information(e.g. BSR) + Additional Control Information (e.g. IDC Info) can be included in the Per AID TID Info(Starting Sequence Number + Block Ack Bitmap)
  This option can be used not only ICR but also CRF
Bits:
4
Per AID TID Info
Octets:
8
2
2
Fragment
Number
AID TID Info
Block Ack Starting
Sequence Control
Block Ack Bitmap
AID11 2046
B3 0, B2-B1 0, B0 0
Control Info 1 – IDC Info
Control Info 2 - BSR
(Length) | Presence Bit | Control Info 1 | Control Info 2 | … | Control Info n
IDC Present,
BSR Present,
etc.
12 bits + 8 octets
(including Starting Sequence Number)

## Slide 9: CRF from non-AP STA (IDC Info + BSR)
UHR AP
AP’s TXOP
MU-RTS
CTS
CTS
DATA
BA
BA
BSRP
QoS Null
M-BA
Unavailable Time
BA
BA
DATA
BSR
IDC event recognized
X
Frame Control | Duration | RA | TA | BA Control | BA Information | FCS
AID11 = 2046 | Ack Type = 0 | TID = 0 | Fragment Number = 0 0 0 0 | (Length) | Presence Bit | IDC Info | BSR Information
12 bits + 8 octets
STA1
(Legacy)
STA2
(UHR)

## Slide 10: CRF from non-AP STA (BA + IDC Info)
UHR AP
STA1
(Legacy)
AP’s TXOP
MU-RTS
CTS
STA2
(UHR)
CTS
DATA
BA
M-BA
Unavailable Time
BA
BA
DATA
IDC event recognized
X
Frame Control | Duration | RA | TA | BA Control | BA Information | FCS
AID – for UHR AP
Per AID TID Info (BlockAck) | AID11 = 2008 | Ack Type = 0 | TID = 0 | Fragment Number = 0 1 1 0 | (Length) | Presence Bit | IDC Info
12 bits + 4 octets

## Slide 11: CRF from Mobile AP (IDC Info)
STA1
(Legacy)
MU-RTS
CTS
STA2
(UHR)
CTS
Unavailable Time
RTS
CTS
AID – for STA1
Frame Control | Duration | RA | TA | BA Control | BA Information | FCS
Per AID TID Info | Per AID TID Info | AID11 = 2046 | Ack Type = 0 | TID = 0 | Fragment Number = 0 1 1 0 | (Length) | Presence Bit | IDC Info
12 bits + 4 octets
UHR
Mobile AP
TXOP
Basic Trigger
DATA
DATA
M-BA
AID – for STA2
STA2’s TXOP
IDC event recognized
X

## Slide 12: Conclusion
We’ve discussed three options of ICR and/or CRF to include multiple control information such as BSR and IDC Info together
  Option 1: new Ack Type + TID combination in AID TID Info + Fragment Number
  Option 2: Special AID11 value in AID TID Info + Fragment Number
  Option 3: New Action frame with A-Control to include control information and additional control information(e.g. IDC Info) together
Option 2 for ICR/CRF can include multiple control information, and can be used with both UHR and legacy devices in multi-user case
  ICR/CRF include multiple control information to support legacy mechanism
  ICR/CRF are backward compatible for legacy devices, especially in the case of Mobile AP

## Slide 13: Straw Poll 1
Do you agree to include the following into the 11bn SFD?
  11bn allows Multi-STA BA to carry one or more feedback (e.g. unavailability) information
    How to include feedback information is TBD

## Slide 14: Straw Poll 2
Do you agree to include the following into the 11bn SFD?
  11bn allows a Multi-STA BA frame to include both Block Ack Bitmap and Feedback information if the preceding PPDU includes QoS Data frame(s) that solicit an immediate response (e.g., Ack or BlockAck context) and the non-AP STA is operating in a mode that allows inclusion of feedback information(e.g. DUO mode)

## Slide 15: References
[1] 11-24/834r0, Some Details on In-Device Coexistence
[2] 11-24/543r1, Coexistence Protocols for UHR – Follow Up
[3] 11-24/1221r1, ICF ICR follow up
[4] 11-24/1226r0, ICF-ICR design
[5] 11-24/1247r0, ICF ICR Design For Coex

## Slide 16: Appendix. Option 3 (New Action frame) A-Control + Additional Control info.
Defining new Action frame for IDC Info
  Management frame format
Code | Meaning
… | …
38 | IDC
… | …
Value | Meaning
0 | IDC Info
1-255 | Reserved
Category values
IDC Action field values
Value | Meaning
0 | Category
1-255 | One or more IDC Info
IDC Info Action field format
Octets: | 2 | 2 | 6 | 6 | 6 | 2 | 0 or 4 | variable | 4
 | Frame Control | Duration | Address 1 | Address 2 | Address 3 | Sequence Control | HT Control | Frame Body | FCS
ACI Bitmap | Delta TID | ACI High | Scaling Factor | Queue Size High | Queue Size All
HE Variant(B0, B1 – 1 1), Control ID 3
Additional Control Information(e.g. IDC Info)
A-Control(e.g. BSR)
(Length) | Presence Bit | Control Info 1 | Control Info 2 | … | Control Info n