## Slide 1: Tone Plan Shift Value Design
Date: 2024-09-08
Authors:
Name | Affiliations | Address | Phone | Email
Bo Gong | Huawei |  |  | gongbo8@huawei.com
Jian Yu (Ross) |  |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | ming.gan@huawei.com

## Slide 2: Background
Sep. 2024
In ref [1], people have discussed DRU transmission on frequency subblocks of a wide bandwidth PPDU. It is recommended that DRU transmission over 20MHz subchannels of a/an 80MHz/160MHz/320MHz PPDU is defined as follows.
The DRU tone plan for a 20MHz PPDU is shifted into the 242-tone RU in a 20MHz subchannel.
The first non-zero tone of the DRU tone plan for a 20MHz subchannel is aligned with the first tone of the 242-tone RU.
The tone indexes of the DRU tone plan for a 20MHz subchannel of an 80MHz PPDU is obtained by the DRU tone plan for a 20MHz PPDU plus a constant value, which is -380,-133,132,379 corresponding to the 1st , 2nd, 3rd, 4th 20MHz subchannel of an 80MHz PPDU. The tone indexes of the DRU tone plan for a 20MHz subchannel in a 160MHz/320MHz PPDU can be obtained by a simple extension of an 80MHz PPDU.
In this proposal, we take the 20MHz only STAs into consideration and propose several new tone plan shift values for DRU transmission over 20MHz subchannel of a/an 80MHz/160MHz/320MHz PPDU.

## Slide 3: DC Tones Unalignment Issue of a 20MHz Only STA
Considering that 20MHz only STAs participate in transmission, the tone indexes of a 20MHz subchannel of a/an 80M/160M/320M PPDU need to be converted to the tone indexes of a 20MHz PPDU. Take the lowest 20MHz subchannel of a 80MHz PPDU as an example.
The converted tone indexes of the 242-tone RU is -116:125 and the converted tone indexes of the DRU tone plan for the 20MHz subchannel is -116:124 (first tone alignment). The converted DRU tone plan for the 20MHz subchannel can be regarded as the DRU tone plan for a 20MHz PPDU +4.
Sep. 2024

## Slide 4
  The tone indexes [-5 -4 -3] in the DRU tone plan for a 20MHz PPDU will become [-1 0 1] after +4. It means that in the converted DRU tone plan for the 20MHz subchannel, some DRUs will include tone indexes [-1 0 1], which are the DC tones of a 20MHz only STA.
  The tone indexes [119 120] in the DRU tone plan for a 20MHz PPDU will become [123 124] after +4. It means that in the converted DRU tone plan for the 20MHz subchannel, some DRUs will include tone indexes [123 124], which are the guard tones of a 20MHz only STA.
For this issue, 2 schemes are proposed:
Scheme-1: Disallow the DRUs including [-1 0 1] in the converted DRU tone plan for the 20MHz subchannel for a 20MHz only STA following 11ax/be, since it is more friendly to testing on the transmitter quality requirements, e.g. constellation error, EVM, spectral flatness.
Scheme-2: Null the tones with indexes [-1 0 1] in the converted DRU tone plan for the 20MHz subchannel for a 20MHz only STA.
  It seems there exists no need to put extra restriction on the DRUs including [123 124] in the converted DRU tone plan for the 20MHz subchannel for a 20MHz only STA, since the guard tones attenuation can be regarded as fading.
Sep. 2024

## Slide 5: Tone Plan Shift Value Design
In ref [1], it is proposed that for the DRU tone plan for a 20MHz subchannel,
it is obtained by shifting the DRU tone plan for a 20MHz PPDU.
the first non-zero tone is aligned with the first tone of the 242-tone RU in a 20MHz subchannel.
In fact, since DRU tone plan for a 20MHz PPDU spans 241 tones, there are 2 options when shifting it into a 242-tone RU,
The first option is placing the 241 tones on the first 241 tones of a 242-tone RU, which means the first non-zero tone is aligned with the first tone of a 242-tone RU.
The second option is placing the 241 tones on the last 241 tones of a 242-tone RU, which means the first non-zero tone is aligned with the second tone of a 242-tone RU.
By comparing the number of the DRUs including DC and guard tones of a 20MHz only STA, it can be determined which option is better for a 20MHz subchannel.
Sep. 2024

## Slide 6
Considering the 2nd and 4th 20MHz subchannels in an 80M PPDU, the tone indexes are converted to tone indexes of a 20M PPDU. The converted tone indexes of the 242-tone RU is -125:116.
For option-1, the converted DRU tone plan for the 20MHz subchannels spans -125:115, which can be regarded as the DRU tone plan for a 20MHz PPDU -5.
For option-2, the converted DRU tone plan for the 20MHz subchannels spans -124:116, which can be regarded as the DRU tone plan for a 20MHz PPDU -4.
Taking the tone plans for a 20MHz PPDU proposed in ref [2] and ref [3] as examples. The converted DRU tone plans for the 20MHz subchannels corresponding to option-1 and option 2 are given as follows.
Sep. 2024

## Slide 7
DRU Type | DRU index and tone range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-125:9:-17，1:9:109] | DRU2 [-121:9:-13，5:9:113] | DRU3 [-123:9:-15，3:9:111] | DRU4 [-119:9:-11，7:9:115] | DRU5 [-117:9:-9，0:9:108]
 | DRU6 [-124:9:-16，2:9:110] | DRU7 [-120:9:-12，6:9:114] | DRU8 [-122:9:-14，4:9:112] | DRU9 [-118:9:-10，-1:9:107] | 
52-tone DRU i=1:4 | DRU1 26-tone[DRU1，DRU2] |  | DRU2 26-tone[DRU3，DRU4] |  | 
 | DRU3 26-tone[DRU6，DRU7] |  | DRU4 26-tone[DRU8，DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone[DRU1~4]，[-8,-2] |  | DRU2 26-tone[DRU6~9]，[-7,-3] |  | 
DRU Type | DRU index and tone range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-124:9:-16，2:9:110] | DRU2 [-120:9:-12，6:9:114] | DRU3 [-122:9:-14，4:9:112] | DRU4 [-118:9:-10，8:9:116] | DRU5 [-116:9:-8，1:9:109]
 | DRU6 [-123:9:-15，3:9:111] | DRU7 [-119:9:-11，7:9:115] | DRU8 [-121:9:-13，5:9:113] | DRU9 [-117:9:-9，0:9:108] | 
52-tone DRU i=1:4 | DRU1 26-tone[DRU1，DRU2] |  | DRU2 26-tone[DRU3，DRU4] |  | 
 | DRU3 26-tone[DRU6，DRU7] |  | DRU4 26-tone[DRU8，DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone[DRU1~4]，[-7,-1] |  | DRU2 26-tone[DRU6~9]，[-6,-2] |  | 
The converted DRU tone plan for the 2nd and 4th 20MHz subchannels of an 80MHz PPDU corresponding to option-1 based on ref [2]
The converted DRU tone plan for the 2nd and 4th 20MHz subchannels of an 80MHz PPDU corresponding to option-2 based on ref [2]
Sep. 2024

## Slide 8
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-125:9:-17, 1:9:109] | DRU2 [-120:9:-12, 6:9:114] | DRU3 [-123:9:-15, 3:9:111] | DRU4 [-118:9:-10, -1:9:107] | DRU5 [-122:9:-14, 4:9:112]
 | DRU6 [-117:9:-9, 0:9:108] | DRU7 [-121:9:-13, 5:9:113] | DRU8 [-124:9:-16, 2:9:110] | DRU9 [-119:9:-11, 7:9:115] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-8, -3] |  | DRU2 26-tone [DRU6~9], [-7, -2] |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-124:9:-16, 2:9:110] | DRU2 [-119:9:-11, 7:9:115] | DRU3 [-122:9:-14, 4:9:112] | DRU4 [-117:9:-9, 0:9:108] | DRU5 [-121:9:-13, 5:9:113]
 | DRU6 [-116:9:-8, 1:9:109] | DRU7 [-120:9:-12, 6:9:114] | DRU8 [-123:9:-15, 3:9:111] | DRU9 [-118:9:-10, 8:9:116] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-7, -2] |  | DRU2 26-tone [DRU6~9], [-6, -1] |  | 
The converted DRU tone plan for the 2nd and 4th 20MHz subchannels of an 80M PPDU corresponding to option-1 based on ref [3]
The converted DRU tone plan for the 2nd and 4th 20MHz subchannels of an 80MHz PPDU corresponding to option-2 based on ref [3]
Sep. 2024

## Slide 9
 | Option-1 of the converted DRU tone plan for the 2nd and 4th 20MHz subchannels of an 80M PPDU |  | Option-2 of the converted DRU tone plan for the 2nd and 4th 20MHz subchannels of an 80M PPDU | 
 | The DRUs including DC tones [-1 0 1] of a 20MHz only STA | The DRUs including guard tones [-125 -124 -123] of a 20MHz only STA | The DRUs including DC tones [-1 0 1] of a 20MHz only STA | The DRUs including guard tones [-124 -123] of a 20MHz only STA
Tone plan for a 20MHz PPDU proposed in ref [2] | 26-tone DRU (3): 1、5、9 52-tone DRU (2): 1、4 106-tone DRU (2): 1、2 | 26-tone DRU (3): 1、3、6 52-tone DRU (3): 1、2、3 106-tone DRU (2): 1 、2 Note that 106-1 includes 2 guard tones. | 26-tone DRU (2): 5、9 52-tone DRU (1): 4 106-tone DRU (2): 1、2 | 26-tone DRU (2): 1、6 52-tone DRU (2): 1、3 106-tone DRU (2): 1 、2
Tone plan for a 20MHz PPDU proposed in ref [3] | 26-tone DRU (3): 1、4、6 52-tone DRU (3): 1、2、3 106-tone DRU (2): 1、2 | 26-tone DRU (3): 1、3、8 52-tone DRU (3): 1、2、4 106-tone DRU (2): 1 、2 Note that 106-2 includes 2 guard tones. | 26-tone DRU (2): 4、6 52-tone DRU (2): 2、3 106-tone DRU (2): 1、2 | 26-tone DRU (2): 1、8 52-tone DRU (2): 1、4 106-tone DRU (2): 1 、2
By simple comparison, it can be seen that for Option-2, the DRUs including DC tones of a 20MHz only STA are less than Option-1; In addition, the DRUs including guard tones of a 20MHz only STA are also less than Option-1.
Thus, we prefer Option-2. It means for the 2nd and 4th 20MHz subchannels of an 80MHz PPDU, the first non-zero tone of the DRU tone plan is aligned with the second tone of the 242-tone RUs.
Note: Following the same comparison principle, for the 1st and 3rd 20MHz subchannels in an 80MHz PPDU, Option-1 will be preferred. It means that the first non-zero tone of the DRU tone plan for the 20MHz sunchannels is aligned with the first tone of the 242-tone RUs. Since it is the same as the ref [1], it is not described here again.
Sep. 2024

## Slide 10
In the following table, we provide the shift values for the 2nd and 4th 20MHz subchannels in a/an 80MHz/160MHz/320MHz PPDU. It means that the DRU tone plans for the 2nd and 4th 20MHz subchannels of an 80MHz PPDU and the lower/upper 80MHz frequency subblock of a 160MHz PPDU and the lowest/second lowest/second highest/highest 80MHz frequency subblock of a 320MHz PPDU are obtained by the DRU tone plan for a 20MHz PPDU plus the shift values.
 | Shift values for the 2nd 20MHz subchannel | Shift values for the 4th 20MHz subchannel
80MHz PPDU | -132 | 380
Lower 80MHz frequency subblock in a 160MHz PPDU | -644 | -132
Upper 80MHz frequency subblock in a 160MHz PPDU | 380 | 892
The lowest 80MHz frequency subblock in a 320MHz PPDU | -1668 | -1156
The second lowest 80MHz frequency subblock in a 320MHz PPDU | -644 | -132
The second highest 80MHz frequency subblock in a 320MHz PPDU | 380 | 892
The highest 80MHz frequency subblock in a 320MHz PPDU | 1404 | 1916
Sep. 2024

## Slide 11: Summary
In this proposal, for DRU transmission over 20MHz subchannel of a/an 80MHz/160MHz/320MHz PPDU, 20MHz only STAs are taken into consideration. It is found that there exist DC and guard tones unalignment issue for 20MHz only STAs. The DRU tone plan shift values are redesigned which makes less DRUs overlap with the DC and guard tones of 20MHz only STAs.
Sep. 2024

## Slide 12: Reference
[1] 11-24-1189-01-00bn-dru-transmission-on-frequency-subblocks-of-wide-bandwidth-ppdu
[2] 11-24-0468-02-00bn-dru-tone-plan-for-11bn
[3] 11-24-1096-00-00bn-mirror-symmetric-20-mhz-dru-tone-plan-within-242-rru-boundary
Sep. 2024

## Slide 13: SP 1A
Do you agree to add the following text to the TGbn SFD?
For the DRU tone plan for a 20MHz subchannel of an 80MHz/160MHz/320MHz PPDU, the DRUs including the DC tones of a 20MHz only STA shall be disallowed for a 20MHz only STA.
  — The DRU indexes are TBD.
Sep. 2024

## Slide 14: SP 1B
Do you agree to add the following text to the TGbn SFD?
For the DRU tone plan for a 20MHz subchannel of an 80MHz/160MHz/320MHz PPDU, the tone within a DRU that is overlapping with the DC tones of a 20MHz only non-AP STA shall be nulled for a 20MHz only non-AP STA.
  — The DRU indexes are TBD.
  NOTE: This still allows a 20MHz only non-AP STA to use a DRU that has a tone that is overlapping with the DC of a 20MHz only non-AP STA.
Sep. 2024

## Slide 15: SP 2
Do you agree to add the following text to the TGbn SFD?
The DRU tone plans for the 2nd and 4th 20MHz subchannels in a 80MHz PPDU and the lower/upper 80MHz frequency subblock of a 160MHz PPDU and the lowest/second lowest/second highest/highest 80MHz frequency subblock of a 320MHz PPDU are obtained by the DRU tone plan for a 20MHz PPDU plus the shift values. The shift values are shown in the following table.
Sep. 2024
 | Shift values for the 2nd 20MHz subchannel | Shift values for the 4th 20MHz subchannel
80MHz PPDU | -132 | 380
Lower 80MHz frequency subblock in a 160MHz PPDU | -644 | -132
Upper 80MHz frequency subblock in a 160MHz PPDU | 380 | 892
The lowest 80MHz frequency subblock in a 320MHz PPDU | -1668 | -1156
The second lowest 80MHz frequency subblock in a 320MHz PPDU | -644 | -132
The second highest 80MHz frequency subblock in a 320MHz PPDU | 380 | 892
The highest 80MHz frequency subblock in a 320MHz PPDU | 1404 | 1916