## Slide 1: A transmission scheme for UHR
Date: 2024-9-4
Authors:

## Slide 2: Introduction
11bn will provide:
  at least one mode of operation capable of reducing latency by 25% for the 95th percentile of the latency distribution compared to the Extremely High Throughput MAC/PHY operation and
  at least one mode of operation capable of reducing MAC Protocol Data Unit (MPDU) loss by 25% compared to the Extremely High Throughput MAC/PHY operation for a given scenario, especially for transitions between BSSs.
In this contribution, we discuss a transmission scheme for low latency and high reliability traffic.

## Slide 3: A Transmission Scheme for Low Latency and High Reliability Traffic
PPDU 1
PPDU 2
PIFS
The transmission scheme consists of a series of consecutive PPDUs separated by PIFS. PPDU 2/3… have data field that is replication of PPDU 1’s data field.
  U-SIG of the PPDUs indicate the transmission scheme.
  PPDU i…is not sent while ACK or BA is received SIFS after previous PPDU (shown in figure 1)
  PPDU i… is sent while ACK or BA is not received, as PIFS recovery. (shown in figure 2)
  If the received signal is poor, the receiver can better treat the signal via soft combining data fields of PPDUs.
BA
SIFS
t
PPDU 1
BA
SIFS
t
(1)
(2)
BA is not received

## Slide 4: A Transmission Scheme for Low Latency and High Reliability Traffic (cont’d)
PPDU 1
PPDU 2
PIFS
If PPDU 1 is collided, the receiver has PPDU 2.
The BSS can set a threshold Lth to make PPDU 2 success transmission with higher probability.
  The PPDUs for low latency and high reliability traffic is longer than Lth and others are shorter than Lth.
BA
Colliding PPDU
SIFS
Lth
t
BA is not received

## Slide 5: Summary
In this contribution, we discuss a transmission scheme for low latency and high reliability traffic.
  The transmission scheme consists of a series of consecutive PPDUs separated by PIFS, in which PPDU 2/3… have data field that is replication of PPDU 1’s data field.
  PPDU i exists while ACK or BA is not received SIFS after previous PPDU, as PIFS recovery.
  The transmission scheme is indicated by U-SIG.
PPDU 1
PPDU 2
PIFS
BA
SIFS
t
BA is not received

## Slide 6: SP:
Do you agree to define the following transmission scheme in UHR for low latency and high reliability traffic as following?
  The transmission scheme consists of a series consecutive PPDUs separated by PIFS, in which PPDU 2/3… has data field that is replication of PPDU 1’s data field.
  PPDU i… exists while ACK or BA is not received SIFS after previous PPDU, as PIFS recovery.
  The transmission scheme is indicated by U-SIG.
PPDU 1
PPDU 2
PIFS
BA
SIFS
t
BA is not received

## Slide 7: References
[1] https://development.standards.ieee.org/myproject-web/app#viewpar/14476/10639
[2] 11-24-0740-00-00bn-time-domain-a-ppdu-for-collision-reduction-and-priority-access Ning Gao