## Slide 1: PPDUs in AMP
Date: 2024-09-03
Authors:
Name | Affiliations | Address | Phone | Email
Bin Qian | Huawei | Shenzhen, China |  | qianbin14@huawei.com
Lei Huang |  | Singapore |  | 
Panpan Li |  | Singapore |  | 
Wei Lin |  | Shenzhen, China |  | 
David, Xun Yang |  | Singapore |  | 
Sep. 2024
Notes: September 2012

## Slide 2: Abstract
This contribution provides an overview of the PPDU categories to be utilized by enhanced legacy 802.11 devices, active devices, mono-static backscatter, and bi-static backscatter within TGbp
Sep. 2024

## Slide 3: AMP Downlink and Carrier PPDU (DC-PPDU)
The AMP DC-PPDU unifies downlink data transmission and the provision of a carrier signal for backscatter communication in a single, versatile PPDU format
Key components of AMP DC-PPDU example
  Wi-Fi Preamble: Detected by third party devices for better coexistence
  AMP-Sync: Provides synchronization for the entire PPDU
  AMP-SIG: Contains control information, such as MCS and payload length, crucial for decoding the AMP-Data
  AMP-Data: Carriers the actual data payload, with its specific design depending on the AMP STA’s capability
  Energizer Symbols: Provides the carrier signal for backscatter communication
Sep. 2024

## Slide 4: AMP DC-PPDU (1/3)
Scenario 1: Downlink data transmission
  The AMP DC-PPDU could be used solely for downlink data transmission from the AP to AMP STAs [1-4]
  Applicable Devices: Enhanced 802.11 legacy devices, active devices, and backscatter devices
  In this use case, the Energizer Symbols are not present, focusing exclusively on data transmission
Sep. 2024

## Slide 5: AMP DC-PPDU (2/3)
Scenario 2: Carrier Signal Provision
  The AMP DC-PPDU serves as the input carrier for backscatter devices, enabling communication by reflecting this carrier
  Only the Wi-Fi Preamble and Energizer Symbols are present; AMP-SYNC, AMP-SIG and AMP-Data fields are not present
  Applicable to both mono-static and bi-static backscatter scenarios
  In bi-static backscatter case, the carrier source (i.e., non-AP STA), separate from the AP, transmits the AMP DC-PPDU
Sep. 2024

## Slide 6: AMP DC-PPDU (3/3)
Scenario 3: Combined downlink Data and Carrier Signal Transmission
  The PPDU includes the Wi-Fi Preamble, AMP-SYNC, AMP-SIG, AMP-Data, and Energizer Symbols
  This use case integrates all fields, making it suitable for comprehensive communication and backscatter needs
  Applicable to both mono-static and bi-static backscatter scenarios
  In bi-static backscatter case, the carrier source (i.e., non-AP STA), separate from the AP, transmits the AMP DC-PPDU
Sep. 2024

## Slide 7: AMP Uplink PPDU
The UL PPDU is used for data transmission from the AMP STAs to the AP, primarily applicable to active devices
For enhanced 802.11 legacy devices, the uplink data transmission relies on existing 802.11 standards [6]
For backscatter devices, the uplink data transmission is not independent but depends on the input carrier symbols (i.e., Energizer Symbols)
UL PPDU example
  Active devices may not be able to transmit the Wi-Fi Preamble
Sep. 2024

## Slide 8: AMP WPT PPDU
The WPT PPDU facilitates wireless power transfer to various devices, including enhanced 802.11 legacy devices and active devices
The WPT PPDU operates in sub-1 GHz frequency range
The specific format of the WPT PPDU is TBD
Sep. 2024

## Slide 9: Device Capabilities and Their PPDUs
Sep 2024

## Slide 10: Summary
In this contribution, we aim to illustrate the relationship between different AMP STA capabilities and the specific PPDUs they utilize
Sep. 2024

## Slide 11: References
[1] 11-24-0847-00bp-initial-thought-on-2.4-ghz-dl-amp-ppdu-design
[2] 11-24-0861-00bp-amp-dl-ppdu-consideration
[3] 11-24-1213-01bp-2.4-ghz-downlink-amp-ppdu-follow-up
[4] 11-24-1345-00bp-high-level-requirements-for-downlink-phy-in-2.4-ghz
[5] 11-24-1236-00bp-close-range-backscattering-waveform-and-modulation
[6] 11-24-1263-00-00bp-amp-supported-legacy-mode
Sep. 2024

## Slide 12: SP 1
Do you support that 11bp shall define an AMP Downlink and Carrier PPDU (DC-PPDU) applicable to enhanced 802.11 legacy devices, active devices, and backscatter devices in 2.4 GHz frequency band
  Yes:
  No:
  Abstain:
Sep. 2024

## Slide 13: SP 2
Do you support that 11bp shall define an AMP uplink PPDU applicable to active devices in 2.4 GHz frequency band
  Yes:
  No:
  Abstain:
Sep. 2024

## Slide 14: SP 3
Do you support that 11bp shall define an AMP wireless power transfer (WPT) PPDU applicable to enhanced 802.11 legacy devices and active devices in sub-1 GHz frequency band
  Yes:
  No:
  Abstain:
Sep. 2024