## Slide 1: PPDUs in AMP
Date: 2024-09-03
Authors:
Name | Affiliations | Address | Phone | Email
Bin Qian | Huawei | Shenzhen, China |  | qianbin14@huawei.com
Lei Huang |  | Singapore |  | 
Panpan Li |  | Singapore |  | 
Wei Lin |  | Shenzhen, China |  | 
David, Xun Yang |  | Singapore |  | 
Sep. 2024
Notes: September 2012

## Slide 2: Abstract
This contribution provides an overview of the PPDU categories to be utilized by enhanced legacy 802.11 devices, active devices, mono-static backscatter, and bi-static backscatter within TGbp
Sep. 2024

## Slide 3: AMP Downlink and Excitation PPDU (DE-PPDU)
The AMP DE-PPDU unifies downlink data transmission and the provision of excitation signals for backscatter communication in a single, versatile PPDU format
Key components of AMP DE-PPDU example
  Legacy Preamble: Detected by third party devices for better coexistence
  AMP-Sync: Provides synchronization for the entire PPDU
  AMP-SIG: Contains control information, such as MCS and payload length, crucial for decoding the AMP-Data
  AMP-Data: Carriers the actual data payload, with its specific design depending on the AMP STA’s capability
  Excitation Symbols: Provides the carrier signal for backscatter communication
Sep. 2024

## Slide 4: AMP DE-PPDU (1/3)
Scenario 1: Downlink data transmission
  The AMP DE-PPDU could be used solely for downlink data transmission from the AP to AMP STAs [1-4]
  Applicable Devices: Enhanced 802.11 legacy devices, active devices, and backscatter devices
  In this use case, the Excitation Symbols are not present, focusing exclusively on data transmission
Sep. 2024

## Slide 5: AMP DE-PPDU (2/3)
Scenario 2: Excitation Signal Provision
  The AMP DE-PPDU serves as the input carrier for backscatter devices, enabling communication by reflecting this carrier
  Only the Legacy Preamble and Excitation Symbols are present; AMP-SYNC, AMP-SIG and AMP-Data fields are not present
  Applicable to both mono-static and bi-static backscatter scenarios
  In bi-static backscatter case, the carrier source (i.e., non-AP STA), separate from the AP, transmits the AMP DE-PPDU
Sep. 2024

## Slide 6: AMP DE-PPDU (3/3)
Scenario 3: Combined downlink Data and Excitation Signal Transmission
  The PPDU includes the Legacy Preamble, AMP-SYNC, AMP-SIG, AMP-Data, and Excitation Symbols
  This use case integrates all fields, making it suitable for comprehensive communication and backscatter needs
  Applicable to both mono-static and bi-static backscatter scenarios
  In bi-static backscatter case, the carrier source (i.e., non-AP STA), separate from the AP, transmits the AMP DE-PPDU
Sep. 2024

## Slide 7: AMP Uplink PPDU
The UL PPDU is used for data transmission from the AMP STAs to the AP, primarily applicable to active devices
For enhanced 802.11 legacy devices, the uplink data transmission relies on existing 802.11 standards [6]
For backscatter devices, the uplink data transmission is not independent but depends on the input carrier symbols (i.e., Excitation Symbols)
UL PPDU example
  Active devices may not be able to transmit the Legacy Preamble
Sep. 2024

## Slide 8: AMP WPT PPDU
The WPT PPDU facilitates wireless power transfer to various devices, including enhanced 802.11 legacy devices and active devices
The WPT PPDU operates in sub-1 GHz frequency range
The specific format of the WPT PPDU is TBD
Sep. 2024

## Slide 9: Device Capabilities and Their PPDUs
Sep 2024

## Slide 10: Summary
In this contribution, we aim to illustrate the relationship between different AMP STA capabilities and the specific PPDUs they utilize
Sep. 2024

## Slide 11: References
[1] 11-24-0847-00bp-initial-thought-on-2.4-ghz-dl-amp-ppdu-design
[2] 11-24-0861-00bp-amp-dl-ppdu-consideration
[3] 11-24-1213-01bp-2.4-ghz-downlink-amp-ppdu-follow-up
[4] 11-24-1345-00bp-high-level-requirements-for-downlink-phy-in-2.4-ghz
[5] 11-24-1236-00bp-close-range-backscattering-waveform-and-modulation
[6] 11-24-1263-00-00bp-amp-supported-legacy-mode
Sep. 2024

## Slide 12: SP 1
Do you agree with the following text:
  IEEE 802.11bp shall specify, in 2.4 GHz, an AMP Downlink and Excitation PPDU that contains a Legacy Preamble field, and optionally one or more of an AMP-Sync field, an AMP-Data field, and an Excitation field. Inclusion of an AMP-SIG field is TBD.
    Note, the details of the Legacy Preamble field are TBD
    For combined downlink data and excitation signal transmission, the Excitation field would follow the AMP-Data field
    For combined downlink data and excitation signal transmission, there can be multiple segments of the AMP-Data field and the Excitation field
    Supporting list: [24/1345r1, 24/1496r1]
  Yes:
  No:
  Abstain:
Sep. 2024

## Slide 13: SP 2
Do you agree with the following text:
  IEEE 802.11bp shall specify, in 2.4 GHz, an AMP uplink PPDU that contains an AMP-Sync field and an AMP-Data field. Inclusion of an AMP-SIG field in AMP uplink PPDU is TBD
  Yes:
  No:
  Abstain:
Sep. 2024

## Slide 14: SP 3
Do you agree with the following text:
  IEEE 802.11bp shall define an AMP wireless power transfer (WPT) PPDU in sub-1 GHz frequency band
    The AMP WPT PPDU format is TBD
  Yes:
  No:
  Abstain:
Sep. 2024