## Slide 1: Uplink Rates for Active Transmission
Date: 2024-09-09
Authors:

## Slide 2: Abstract
We present feasibility for uplink of active transmitters as well as recommend an underlying set of MCSs and the way to select them.

## Slide 3: Usage of Uplink With Active Transmitters
Scenarios from [1] suggest working distances 1-50m for active transmitters
Some use cases require fast efficient 1-5m access:
  Smart Manufacturing, Logistics & Warehouse, Smart Agriculture, Fresh Food Supply Chain:
    Conveyor belt, loading docks, pass-by forklift
Some use cases require wide coverage and long range
  Smart home, Logistics & Warehouse, Smart Agriculture, Fresh Food Supply Chain:
    Storage room inventory, find an item, large corn field coverage
The reader is usually aware of the usage/application, not the tag
  The rate of uplink transmission can be requested by the reader trigger message
    Avoid any rate control at tag.
    No need for a single sync field for all rates. Higher rates can use shorter sync fields since the receiver is aware in advance about the rate.

## Slide 4: Example for Uplink Link Budget of Active Transmitter
We assume active transmitter AMP device can transmit with -25dBm EIRP, with an overall power efficiency of 2%.
The bandwidth which can be utilized depends on the channel width. As in [2], we assume 22MHz/20MHz of a single channel as baseline.
We assume convolutional code with coding rate=½ ([43,65], K=6) or no-code. This code can be encoded with very low power and low complexity, while providing SNR improvement of 6-8dB.
We assumed both MSK and OOK-Manchester.
We used Manchester encoding for OOK to make sure robust symmetric reception for ’0/1’.

## Slide 5: Example for Uplink Lineup and Energy Budget
Lineup Assumptions
SNR [dB] for FRIIS channel
Energy/Charging Impact
Payload | 200 | bit
Power Consumption | 158 | uW
Charge power | 0.01 | uW
bitrate [Mbps] | 1 | 2 | 4 | 8 | 16
transmission time [us] | 200 | 100 | 50 | 25 | 12.5
Energy [nJ] | 31.62 | 15.81 | 7.91 | 3.95 | 1.98
Charge Time [ms] | 3162.28 | 1581.14 | 790.57 | 395.28 | 197.64
EIRP | -25 | dBm
receiver NF | 9 | dB
KT | -174 | dBm/Hz
Fc | 2.45 | GHz
BW [MHz] |  | 1 | 2 | 4 | 8 | 16
distance [m] | RSSI [dBm] |  |  |  |  | 
1 | -65 | 39.77 | 36.76 | 33.75 | 30.74 | 27.73
5 | -79 | 25.80 | 22.79 | 19.77 | 16.76 | 13.75
50 | -99 | 5.80 | 2.79 | -0.23 | -3.24 | -6.25

## Slide 6: Example for Uplink Lineup [cont]
Active transmitters can efficiently use the 802.11 defined bandwidth.
We estimate between 200-3000ms charge times for the various rates using the assumption.
The variability in use cases suggests that a single modulation and coding scheme may not be sufficient - defining several MCSs significantly improves product proposition to the agreed use cases.
Since CTS-to-Self and also legacy headers reserve 20MHz channel, using lower bandwidths means leaving unutilized spectrum. Thus multiple rates significantly improve coexistence with legacy networks and inventory time.
Allowing the reader trigger frame to determine the MCS removes the rate control from the tag and can also reduce sync overheads

## Slide 7: Suggested MCS Table
Modulation | OOK-Manchester |  |  |  | 
MCS | Bit rate [Mbps] | Coding rate | Symbol rate [MHz] | BW [OOK-Manchester] | Sensitivity [dBm]
0 | 0.5 | 0.5 | 1 | 2 | -99
1 | 1 | 0.5 | 2 | 4 | -96
2 | 2 | 0.5 | 4 | 8 | -93
3 | 4 | 0.5 | 8 | 16 | -90
4 | 8 | 1 | 8 | 16 | -82
Modulation | MSK |  |  |  | 
MCS | Bit rate [Mbps] | Coding rate | Symbol rate [MHz] | BW [FSK] | Sensitivity [dBm]
0 | 0.5 | 0.5 | 1 | 1 | -96
1 | 1 | 0.5 | 2 | 2 | -93
2 | 2 | 1 | 2 | 2 | -92
3 | 4 | 1 | 4 | 4 | -90
4 | 8 | 1 | 8 | 8 | -87
5 | 16 | 1 | 16 | 16 | -84

## Slide 8: Transmission Properties of MSK/OOK-Manchester

## Slide 9: Conclusions
The necessity of using several MCS for uplink of active transmitters was shown.
Several MCSs were proposed for reaching products that can effectively cover the variaty of use cases for both MSK and OOK-Manchester modulations, as suggested by [3].
Several extensions to these suggested MCS are possible. Mainly:
  Higher coding rates
  Better codes
  Pilots

## Slide 10: References
[1] 11-23-1005-00-0amp-discussion-on-requirements-for-amp-use-cases
[2] 11-24-1253-01-00bp-ultra-low-power-features-for-active-devices
[3] 11-24-0849-01-00bp-harmonization-of-waveform

## Slide 11: Strewpoll #1
Do you agree to include more than one uplink modulation and coding scheme (MCS) for the uplink of active transmitters?
Answer:
Y
N
A

## Slide 12: Strewpoll #2
Do you agree that an AMP-trigger frame from the AMP-Reader will specify the uplink MCS?
Answer:
Y
N
A

## Slide 13: Strewpoll #3
Do you agree to include uplink MCSs for active transmission with the minimum bit rate of
Answer:
0.125Mbps
0.25Mbps
0.5Mbps
1Mbps
Abstain

## Slide 14: Strewpoll #4
Do you agree to include uplink MCSs for active transmission MCSs with the maximum bit rate of
Answer:
1Mbps
4Mpbs
8Mps
16Mbps
Abstain