## Slide 1: Duty-cycle AMP operation
Date: 2024-09-02
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com
Chuanfeng He |  |  |  | 
Doc.: IEEE 802.11-24/1500r0
Sept. 2024

## Slide 2: Abstract
This submission is to discuss access procedure of AMP IoT.
Doc.: IEEE 802.11-24/1500r0

## Slide 3
Background(1)
  For AMP IoT, there are mainly two kinds of scenario considering the number of AMP devices:
    Scenario 1: only limited number of devices
      E.g. peer-to-peer communication in close range scenario
    Scenario 2: large number of devices
      E.g. in logistics and warehouse scenarios
      E.g. sensors in smart manufacturing scenario
Weijie Xu (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1500r0
Sept. 2024

## Slide 4
Weijie Xu (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1500r0
Sept. 2024
  In [1], the operation state and operation procedure of AMP device is discussed. One promising mode is as in below:
Background(2)

## Slide 5
Weijie Xu (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1500r0
Sept. 2024
  For many cases, harvested power level is lower than consumed power level, due to e.g. longer distance than RFID, usage of LNA/Reverse amplifier, active transmitter etc. That’s why it need dedicated power storage.
      Note that in RFID tag, there is also small capacitor in the circuit, but it is only used to smooth the fluctuation of energy signal
    The harvested power is ~100 Nano-Walt @-30 dBm (the possible RF energy harvesting threshold)
    Power consumption of AMP device for different operation:
      Rx: ~1 uw using envelope detector and ~100 uw using IF detector
      Amplifier: ~100uw
      Backscattering: ~1 uw
      Active transmission: ~100uw
      Temperature sensors: ~1uw
Background(3)

## Slide 6
Weijie Xu (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1500r0
Sept. 2024
  In RFID, slot-aloha is used as the access procedure.
    RFID device is always on to monitor and decode the query signaling.
      It is feasible because of short working distance.
    The access timing is fully provided/controlled by the interrogator
      RFID device determines whether to access based on the its random number and the control of Query/QueryRep
      Figure: slot-Aloha in RFID[2]
Background(4)

## Slide 7
AMP operation in scenario 1
Weijie Xu (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1500r0
Sept. 2024
  In scenario 1, it is easy for the AMP AP to handle limited number of AMP devices. One example procedure is:
  The following characteristics can be seen:
    There is no collision issue thus no power waste due to repetition
    No scheduling delay/no waiting time thus no power waste during Rx
      AMP trigger from the AP will be dedicated to the AMP device since there is no other device
    Instant harvested power is sufficient for operation, or, stored power is sufficient for limited number of operation steps.

## Slide 8
AMP operation in scenarios 2
Weijie Xu (OPPO)
Slide 8
Doc.: IEEE 802.11-24/1500r0
Sept. 2024
  In scenario 2, it becomes much more challenging.
    There may be collision issue, it will affect the system efficiency and waste device’s power.
    There is scheduling delay due to multiple user scheduling. AMP device may waste power to decode AMP trigger/grant which is for other AMP devices.
    With limited power storage, AMP device will soon run out of its energy if it needs to continuously listen to AMP trigger/grant.
      Even AMP device can harvest sufficient power again, there is still the problem and the issue will happen again and again, resulting in dead-lock and unacceptable latency

## Slide 9
Discussion
Weijie Xu (OPPO)
Slide 9
Doc.: IEEE 802.11-24/1500r0
Sept. 2024
  In the following, it focus on how to provide efficient mechanisms to address the identified issue. The general ideas include,
    Strive to reduce the time duration when the AMP devices are performing Rx/Tx which are the main contributors of energy consumption, in order to reduce power consumption.
    Try to provide sufficient transmission opportunities when the AMP devices are awake and ready for data transmission and reduce the collisions among AMP devices and speedy the access process
      It will be discussed in another companion contribution[3] on multiple access.

## Slide 10
Duty-cycle AMP operation
Weijie Xu (OPPO)
Slide 10
Doc.: IEEE 802.11-24/1500r0
Sept. 2024
  In duty-cycle AMP operation, the whole procedure is triggered by AMP AP. For each AMP device, the trigger signaling will be only send in its duty-cycle window.
    Different AMP device may have non-overlapping time window.
    Multiple AMP device may have overlapping time window.
  AMP device only needs to monitor the trigger in its monitoring window and it can possibly enter into a low-power mode in the rest of the time.
  The necessity and benefit of duty-cycle operation is obvious:
    Reduce the collision probability with distributed access in the time domain
    Lower the average power consumption via reducing the DL monitoring effort
    It enable normal AMP operation via high-efficiency usage of the harvested power

## Slide 11
Requirements
Weijie Xu (OPPO)
Slide 11
Doc.: IEEE 802.11-24/1500r0
Sept. 2024
  Requirement of the AMP devices:
    It shall have energy storage. It can harvest and store energy when it enter into low-power mode.
      The stored power will increase once the harvested power is greater than the consumed power during sleep
    Maintaining a timing clock, as discussed in[4].
      An ultra-low power RTC clock will be sufficient, the power consumption can be very low e.g., several Nanowatt.
  Requirement of the network:
    AMP AP shall provide the timing reference to AMP device, via beacon or other signaling, as discussed in[5].

## Slide 12
Summary and proposals
  In this submission, the issues in case of large number of AMP devices have been identified. To address the issues, duty-cycle AMP operation is proposed.
Weijie Xu (OPPO)
Slide 12
Doc.: IEEE 802.11-24/1500r0
Sept. 2024

## Slide 13
Straw Poll #1
Weijie Xu (OPPO)
Slide 13
Doc.: IEEE 802.11-24/1500r0
Sept. 2024
Do you agree with the following text:
  AMP device needs to be able to support duty-cycle operation.
Yes
No
Abstain

## Slide 14: Reference
IEEE 802.11-24/0826r0, Energy balance of the state-based AMP station
Specification for RFID Air Interface Protocol for Communications at 860 MHz – 960 MHz
IEEE 802.11-23/1140r0 multiple access
IEEE IEEE 802.11-24/1475r0 Discussion on ultra-low power timing clock
IEEE IEEE 802.11-24/1202r0 Scanning and discovery for AMP IoT
Doc.: IEEE 802.11-24/1500r0
Sept. 2024