## Slide 1: Channel Protection In ELR Scenarios
Date: 2024-09-02
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Zhenpeng Shi |  |  |  | 
Ming Gan |  |  |  | 
Stephen McCann |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
A motion about ELR（Enhanced Long Range）PPDU has been passed in 11bn;
  Move to include the following in the 11bn SFD:
    Define Enhanced Long Range (ELR) PPDU and potentially other Range Extension mechanisms.
The main use case is to overcome the link budget imbalance between uplink and downlink
  Usually uplink link budget is smaller than downlink, e.g. up to 6dB.
The hidden node issue is more serious due to reasons below
  The legacy STA can not understand an ELR PPDU
  The normal PPDU doesn’t provide a large coverage
We will discuss the hidden node issues under various ELR scenarios and suggest some procedures.

## Slide 3: Hidden Node Issues Under ELR Scenarios
There are two types of STAs with different capabilities
  STA11 and STA12 can transmit both normal and ELR PPDUs ;
  STA21 and STA22 can only transmit normal PPDUs
When AP and STA11 do an RTS/CTS frame exchange using normal PPDUs, the CTS can not be correctly received by the AP.
AP
STA11
STA12
STA21
STA22
RTS @ normal PPDU
CTS @ normal PPDU

## Slide 4: Hidden Node Issues Under ELR Scenarios
There are two types of STAs with different capabilities
  STA11 and STA12 can transmit both normal and ELR PPDUs ;
  STA21 and STA22 can only transmit normal PPDUs
When AP and STA11 do an RTS/CTS frame exchange through ELR PPDUs, a legacy STA can not understand the ELR PPDU, thus they will not respect the NAV protection.
AP
STA11
STA12
STA21
STA22
RTS @ ELR PPDU
CTS @ ELR PPDU

## Slide 5: Use Case 2
There are two possible cases
  Case 1: only a non-AP UHR STA can transmit ELR PPDUs;
  Case 2: both a UHR AP and non-AP UHR STA can transmit ELR PPDUs;
The TGbn standard hasn’t made a decision that supports case 1 or case 2, or case 1 in some bands and case 2 in the other bands;
As it probably will be an optional feature, it will be good to assume case 1 when discussing channel protection due to below reasons
  The main scenarios that need to improve the channel protection is the power imbalance between UL and DL, in which case the target non-AP STA can correctly receive a non-ELR PPDU sent from the associated AP, so AP doesn’t need to transmit frame in ELR PPDU;
  When considering both case 1 and case 2, there will have to be multiple procedures depending on different cases. It will make the implementation more complex.
So, case 1 is the assumption in the following discussion.
  Please note that, all the procedures will also apply to case 2, if case 2 is supported in TGbn.

## Slide 6: Channel Protection in DL TXOP
One way to improve the protection at the ELR STA side is that the ELR STA responds with two CTS, one in an ELR PPDU and the other in a non-HT PPDU;
  ELR CTS can be correctly received by AP, so that a TXOP is setup
  CTS frame can be used to protect from the legacy STA’s contention.
The problem of this procedure is that STAs hidden from the ELR STA will reset the NAV to 0 according to RTS NAV reset rule;
  A STA that used information from an RTS frame as the most recent basis to update its NAV setting is permitted to reset its NAV to 0 if no frame is received within a NAVTimeout period after the RTS frame.
AP
ELR STA
RTS
ELR CTS
CTS
Data
ELR Ack
A third party STA may initiate the transmission due to NAV reset
ELR CTS = CTS frame in ELR PPDU
CTS = CTS frame in non-HT PPDU
Notes: A STA that used information from an RTS frame or MU-RTS Trigger frame as the most recent basis to update
its NAV setting is permitted to reset its NAV if no (#3038)PHY-RXEARLYSIG.indication or PHYRXSTART.
indication primitive is received from the PHY during a NAVTimeout period starting when the
MAC receives a PHY-RXEND.indication primitive corresponding to the detection of the RTS frame or MURTS
Trigger frame.

## Slide 7: Channel Protection in DL TXOP
In order to resolve the RTS NAV reset problem, two options are provided;
Option 1: use a different frame to trigger dual CTS frames;
  The CTS-Poll frame would be a new control frame, or reuse an existing frame (e.g. a Trigger frame)
AP
ELR STA
CTS-Poll
ELR CTS
CTS
Data
ELR Ack
ELR CTS = CTS frame in ELR PPDU
CTS = CTS frame in non-HT PPDU

## Slide 8: Channel Protection in DL TXOP
Option 2: an AP send out a CTS-to-self frame to setup the TXOP first, and then send a RTS frame to solicit dual CTS frames;
The third party STAs will set the NAV base on the CTS-to-self frame, instead of the RTS frame, so the RTS NAV reset issue can be avoided.
AP
ELR STA
CTS-to-self
ELR CTS
CTS
Data
ELR Ack
RTS
ELR CTS = CTS frame in ELR PPDU
CTS = CTS frame in non-HT PPDU

## Slide 9: Channel Protection in UL TXOP
The ELR STA first sends out an RTS frame in an ELR PPDU to solicit a CTS frame from the AP to setup the TXOP;
After the TXOP is setup, the ELR STA sends out a CTS-to-self frame to set the NAV for the surrounding legacy STAs;
Why not send a first CTS-to-self, then ELR RTS/CTS?
  If the ELR RTS/CTS frame exchange fails, a legacy STA can not reset the NAV based on the CTS-to-self frame;
Whether a third party legacy STA will initiate transmission before CTS-to-self frame?
  No. A legacy STA will fail to decode the ELR RTS, and then wait for an EIFS, where the EIFS will cover the CTS transmission period.
AP
ELR STA
ELR RTS
CTS
CTS-to-self
ELR Data
Ack

## Slide 10: Summary
Channel protection issue needs to be considered after an ELR PPDU is introduced;
  ELR PPDU can not be decoded by a legacy STA
  Legacy PPDU sent by an ELR STA can not be received by AP
In order to simplify the potential procedures, it is suggested to assume that the AP can not (or doesn’t need to) send an ELR PPDU in channel protection procedures;
  I.e., the suggested procedure is irrelevant to whether AP can send an ELR PPDU or not
The channel protection procedures for both DL and UL TXOPs are suggested.

## Slide 11: SP1
xxx