## Slide 1: NPCA During Intra-BSS Traffic On Primary Channel
Date: 2024-09-DD
Authors:

## Slide 2: Abstract
TGbn has agreed to define a non-primary channel access (NPCA) mode which allows a STA to opportunistically access a non-primary channel in a BSS when the primary channel of that BSS is occupied by an OBSS.
NPCA related motioned text from SFD [1]:
  TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
    The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
    A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.
In this contribution, we discuss an opportunity to support NPCA during intra-BSS traffic on the primary channel.

## Slide 3: Background
There can be a large mismatch in operating bandwidths of AP and non-AP STAs in Wi-Fi networks.
In recent Wi-Fi generations, AP STAs are mandated to support wide operating bandwidths such as 80 MHz (applicable for Wi-Fi 7 in 5 GHz, Wi-Fi 6 (6E) in 5(6) GHz) or 160 MHz (applicable for Wi-Fi 7 in 6 GHz) [2, 3].
  Moreover, Wi-Fi 7 AP STAs may support operating bandwidths up to 320 MHz, and Wi-Fi 6/6E AP STAs may support operating bandwidths up to 160 MHz.
Non-AP STAs have no such mandatory bandwidth requirements and may support an operating bandwidth as low as 20 MHz only.
Some standardized (e.g, SST in 802.11ah and OFDMA in 802.11ax) or discussed (e.g., DSO in TGbn) modes of operation may help to address the abovementioned bandwidth mismatch, however an AP STA is required to be in control in all these modes.
Meanwhile, EDCA is understood to be the main channel access mechanism in real-world Wi-Fi deployments [4] – it provides differentiated, distributed channel access to both APs and non-APs.

## Slide 4: Problem
When devices with mismatched operating bandwidths are communicating in a BSS, large portions of the spectrum may be wasted in the BSS, e.g., when TXOPs are initiated by narrow bandwidth non-AP STAs.
Example: If a 20 MHz non-AP STA wins contention and initiates a TXOP with a 160 MHz AP STA, 140 MHz bandwidth will be wasted.

## Slide 5: Opportunity
When the full operating bandwidth of a BSS is not utilized in a TXOP, idle portions of the remaining bandwidth could be used for opportunistic communications in the same BSS.
Such opportunistic NPCA operation during intra-BSS traffic on the primary channel could provide multiple advantages:
  Improved overall throughput,
  Improved spectrum usage in the BSS,
  Transparent operation for legacy devices communicating on primary channel,
  Improved support for low latency applications, for example, by enabling transmission of high priority packets or buffer status reports on a non-primary channel.
Most of the considerations and concepts being discussed in TGbn for OBSS traffic based NPCA could be reused for intra-BSS traffic based NPCA without large efforts.

## Slide 6: Example Illustration and Some Potential Challenges
The following are some potential challenges that may need to be addressed:
  Ensuring acceptable probability of successful packet reception in both TXOPs, i.e., the baseline TXOP occupying the primary channel, and the opportunistic TXOP obtained using NPCA.
  Ensuring fairness to legacy devices operating in the BSS when proposed type of NPCA is supported.

## Slide 7: References
11-24/209r4, Specification Framework for TGbn.
IEEE Std 802.11ax, 2021.
Draft P802.11be D7.0, 2024.
11-24/0840r0, Low latency channel access, Dmitry Akhmetov et. al.

## Slide 8: Straw Poll
Do you believe TGbn should consider NPCA also when primary channel is known to be busy due to intra-BSS traffic?
  Yes
  No