## Slide 1: Automotive WLAN use case study
Authors:
Name | Affiliation | Address | Phone | Email
Jing Ma | Toyota Motor Corporation | Otemachi Bldg. 6F, 1-6-1 Otemachi, Chiyoda-ku, Tokyo, 100-0004, Japan |  | jing_ma@toyota-tokyo.tech
Jing Ma (Toyota)

## Slide 2: Abstract
Jing Ma (Toyota)
In the July meeting, IEEE 802.11 WG approved the creation of Automotive (AUTO) TIG to investigate[1]:
  Use cases, current and planned mechanisms in 802.11 for vehicle connectivity to external APs
  Gaps between requirements and standards for automotive connectivity to external APs
  Recommendations to address gaps
An automotive use case study is discussed in this contribution

## Slide 3: Background
Automotive applications such as Reginal HD Map, remote diagnostics, will need WLAN to provide efficient local connectivity to transfer area of data traffic between vehicles and the cloud
Data center
Core & network
Local data exchange between vehicle and WLAN AP
Reginal HD MAP
Remote Diagnostics
Jing Ma (Toyota)

## Slide 4: Use case : Regional HD MAP
This use case focuses on the use of opportunistic Wi-Fi connectivity for vehicles either running or parked within a specific geographic region.
The vehicle connects to local Wi-Fi access points (APs) to transmit environmental data and receive updated high-definition (HD)
map information from the edge cloud.
It can enhance the accuracy and timeliness of
HD maps while utilizing local infrastructure
for efficient data exchange.
Actors: Vehicle, AP, Edge Cloud

## Slide 5: Use case : Regional HD MAP
16m/s
AP1
Access network (WLAN)
Download the updated map info.
Upload the detected info.
 | Assumed service level requirement | 
Range | 500m | Urban area
Information requested/ generated [2] | - 100 bytes/ object, - 50 objects detected in vehicle | assumed uplink
 | 5000 objects updates | Assumed downlink
Look-ahead time | 1s prior to entering the interested area | 
Assumed service level requirement
4Mbps
40kbps
Scenario 1:

## Slide 6: Use case : Regional HD MAP
16m/s
AP1
Access network (WLAN)
Download the updated map info.
Upload the detected info.
Assumed service level requirement
40kbps
 | Assumed service level requirement | 
Range | 500m | Urban area
Information requested/ generated[2] | - 100 bytes/ object, - 50 objects detected in vehicle | assumed uplink
 | 5000 objects updates | Assumed downlink
Look-ahead time | 5s | 
0.34Mbps
Scenario 2

## Slide 7: Use case : Regional HD MAP
Requirements
  Fast & reliable connection setup
    Optimize network scanning & selection
    Simplify authentication & authentication procedure
    Enhance the reliability of frame exchange for
    connection setup when vehicle in motion
  Fast & seamless AP handover
scanning
Wi-Fi
16m/s
AP1
AP2
Access network (WLAN)
authentication
association
Connection setup
Data transmission
AP1
AP2
Seamless AP handover

## Slide 8: Summary
An automotive use case study is discussed in this contribution
We will continue to study the details regarding the requirements of connection setup, handover to support using the opportunistic Wi-Fi connectivity for automotive use case such as regional HD map update
Jing Ma (Toyota)

## Slide 9
References
[1] 11-24/415r1 Data offload using WLAN in connected vehicle case, March, 2024
[2] 5gaa-t-200111-tr-c-v2x-use-cases-and-service-level-requirements-vol-i-v3.0