## Slide 1: In-Device Coex – Non-periodic
Date: 2024-09-05
Authors:

## Slide 2: Abstract
Several contributions in TGbn discuss In-Device Coexistence. Typically split:
Periodic (known in advance, duration constant)
Non-Periodic (last minute, duration variable)
This contribution proposes non-periodic IDC (NP-IDC) related signalling, within current TXOP, to improve performance for different use cases:
  Non-AP STA
  AP
  P2P
  Concurrent operation (a device operates multiple roles concurrently)

## Slide 3: Scenarios – Use cases
NP-IDC starts within current TXOP (and beyond)
  DL TXOP initiated by AP – STA is available for a portion of the TXOP (and is not certain for how long it will be unavailable for)
  DL TXOP initiated by AP – STA is available for a portion of the TXOP and knows/plans to be unavailable afterwards
NP-IDC event for concurrent P2P or Mobile AP within current TXOP (and beyond)
  DL TXOP initiated by AP
  STA also concurrently scheduled as a Mobile AP or P2P
  Unavailability similar for Mobile AP or P2P – has to be signalled within TXOP
NP-IDC imminent
  STA did not manage to get UL TXOP to announce/signal unavailability
  If STA does not respond to ICF, AP will retry (not efficient)

## Slide 4: Problem
Recipient (typically non-AP STA) can’t stop TXOP overlapping with NP-IDC
Recipient might not even know that an overlap will occur
  That happens when the originator uses single protection (e.g. RTS duration covers CTS + A-MPDU + BA)

## Slide 5: Recipient shortens TXOP
Originator always uses ICF and multiple protection
  New signalling of some kind (capability, Action frame, OMN, etc.)
Recipient knows TXOP duration - Duration in ICR reduces TXOP duration
CF-End ensures medium released at end of shortened TXOP
“Coex Event End” may be communicated in one of the Response frames

## Slide 6: Non-AP STA that is also M-AP shortens TXOP and asks for TXOP sharing
Duration in IRF reduces TXOP duration and asks for TXOP Sharing
CTS-to-self from M-AP device reserves medium around it
  inc. M-AP’s STAs

## Slide 7: Non-AP STA shortens TXOP and signals PS mode
Non-AP STA in PS mode at end of TXOP

## Slide 8: STA signals complete unavailability
Ack confirms receipt of PM=1 signalling
  else originator that didn’t rx CTS-EXT might retransmit

## Slide 9: What should be signalled in ICR?
Assumes that we can enhance ICR (or/and other response frames) in TGbn
Transition into Power Save mode, within TXOP or immediately
TXOP Sharing request
Peer Coex event: another STA in the BSS which has same unavailability
  Covers concurrent P2P use cases
One-off “Local Coex element” to contain:
  Coex event start time (may be after end of TXOP from ICF)
  Coex event end time (may be after end of TXOP)
  Or duration of Coex event
…

## Slide 10: Straw Polls
SP1: Do you support enhancing the NP-IDC signaling to achieve:
STA unavailability after the end of the current TXOP (PS signalling)
Results: Y, N, A

## Slide 11: Straw Polls
SP2: Do you support enhancing the NP-IDC signaling to achieve:
STA imminent unavailability (PM=1 & Ack)
Results: Y, N, A

## Slide 12: Straw Polls
SP3: Do you support enhancing the NP-IDC signaling to achieve:
Concurrent operation signalling (using TXOP sharing)
Results: Y, N, A

## Slide 13: References
[1] 11-23-0816-01-0uhr-enhancements-for-latency-sensitive-traffic-and-in-device-coexistence
[2]11-23-0298-00-0uhr-improved-reliability-in-presence-of-interference
[3] 11-23-1103-00-0uhr-in-device-interference-discussion
[4] 11-23-1964-01-00bn-coexistence-protocols-for-uhr
[5] 11-24-0420-02-00bn-enabling-flexible-coexistence-operation
[6] 11-24-0543-01-00bn-coexistence-protocols-for-uhr-follow-up